行政院所屬各機關因公出國人員出國報告書

參加「石油工程師協會亞太地區之技術研討會」及

前往Schlumberger公司研討水平注產氣井相關技術

服務機關：中國石油公司台灣油礦探勘總處

出國人	職    稱：副主任

姓    名：孫啟三

出國地點：馬來西亞

出國期間：民國九十年十月六日至十月十二日

報告日期：民國九十年十一月二十日

摘      要

本公司為了因應天然氣發電廠用氣量於尖峰與離峰間之巨大變化，以及應付緊急供氣之需，計畫擴充目前鐵砧山儲氣窖之注產規模，提高注產氣能力，經可行性評估後，研議在鐵砧山地區鑽鑿多口水平井。水平井之鑽井、防砂完井及生產等技術，均為本公司極重要且極需建立之技術。

此次出國主要目的有二：(一)參加石油工程師協會（SPE）所舉辦之亞太激勵採油技術研討會(APIORC)，(二)參訪Schlumberger公司研討水平注產氣井相關技術。此次在馬來西亞吉隆坡市所舉辦之亞太激勵採油技術研討會(APIORC)亦將水平井應用及防砂完井技術列為主要議題之一。除了有論文發表之外，並有石油工業之服務公司在現場展覽，且派員在當場解說並與參觀人員互相研討。會後順道參訪Schlumberger公司，除了參觀該公司實驗室外，該公司並針對水平井之鑽井、水泥工程及同步測井等技術作簡報及研討，研討內容豐富實用，受益良多。

其中水平井應用、防砂完井、負壓穿孔、修井復產及堵水等技術，與未來本公司進行擴大儲氣窖工程以及油氣生產作業均有非常重要之關係，特別是裸孔礫石填充完井技術、膨脹型篩管防砂技術、膠化物堵水及水泥填塞器（Cement Packer）之修井技術等，值得進一步評估研究。為了提升本公司鑽採技術水準，以及引進水平井鑽井完井應用於儲氣窖工程之需，未來應多派員參加有關國際性石油相關協會，藉以瞭解各公司的研究發展方向及技術進步情形，作為今後我們的借鏡與努力之目標。

目      次

摘要．．．．．．．．．．．．．．．．．．．．．．．．．2

壹、目的．．．．．．．．．．．．．．．．．．．．．．．5

貳、過程．．．．．．．．．．．．．．．．．．．．．．．6

參、心得．．．．．．．．．．．．．．．．．．．．．．．7

一、亞太激勵採油技術研討會(APIORC)．．．．．．．．．7

二、Schlumberger公司研討水平注產氣井相關技術 ．．．13

肆、建議．．．．．．．．．．．．．．．．．．．．．．．15

伍、附錄．．．．．．．．．．．．．．．．．．．．．．．17

## 目的

本公司已在鐵砧山氣田完成六口注產氣井，但為了因應天然氣發電廠用氣量將逐年大幅地成長，用氣量於尖峰與離峰間產生巨大變化，以及為應付緊急供氣不時之需，同時紓解購氣合約Take or Pay儲槽無法容納之壓力，乃有研議擴大目前鐵砧山儲氣窖之注產規模，並提高注產能力之計畫。經可行性評估後，擬引進水平井技術，在鐵砧山地區鑽鑿多口水平井作為注產氣井，以達到提高所需產能之目的。

本總處在水平井技術方面仍處於萌芽階段，無任何之實際經驗，急需及早建立此項技術，因此如有相關國際性石油工程技術研討會，應儘量派員參加。參加SPE研討會，除可獲得此項水平井相關技術資料外，並可與有關之專家作技術交流，吸取他們的技術經驗，有助於將來擴大注儲工程之順利推展。

## 貳、過程

以下為此次出國開會之行程︰

90年10月6日︰台北→馬來西亞吉隆坡市。

90年10月7日～90年10月9日︰參加SPE所舉辦之亞太激勵採油技術研討會(APIORC)。

90年10月10日～90年10月11日︰至Schlumberger公司參觀及研討水平注產氣井相關技術。

90年10月12日︰馬來西亞吉隆坡市→台北。

- 心得

此次參加在馬來西亞吉隆坡舉行之SPE亞太激勵採油技術研討會(APIORC)及前往Schlumberger公司研討水平注產氣井相關技術，經過一系列的討論，感到受益良多，在此提出與大家分享。這個心得報告將分為兩部分，一部分為參加亞太激勵採油技術研討會(APIORC)，另一部分則為前往Schlumberger公司研討水平注產氣井相關技術，將把開會及參訪期間所聞做一摘要報告。

SPE亞太激勵採油技術研討會(APIORC)中，發表的文章相當豐富，而且涵蓋技術範圍甚廣，有激勵採油技術、水平井之應用、負壓穿孔技術、防砂完井及堵水等技術。在此並不對發表文章一一進行討論，而是綜合發表感想，並提出研討會中所發表比較特殊的新技術，值得吾人再深入研究與評估並引進應用。

  - 亞太激勵採油技術研討會(APIORC)

近年來由於水平鉆井的優點及經濟效益已被肯定及普遍應用，此次之SPE亞太激勵採油技術研討會(APIORC)亦將水平井之應用列為議題。會議期間並安排有服務公司之展示，並有綜合專題研討(Panel Session)，在此會議中，總共有五十五篇論文獲得接受並安排於大會發表，APIORC宣讀論文題目詳見附錄，此次論文發表共分為以下十一類，茲將其分述如下：

- IOR Strategy-Lifecycle and Environmental Prospective相關題目四篇。

- Gas Injection Processes相關題目四篇。

- Quantifying the Remaining Hydrocarbon相關題目三篇。

- IOR Methods I相關題目六篇。

- EOR Methods I相關題目四篇。

- IOR Methods II相關題目五篇。

- EOR Methods II相關題目四篇。

- IOR Methods III相關題目三篇。

- New Technology相關題目五篇。

- Data and Knowledge Management相關題目五篇。

- Poster Session十二篇。

備註：1. EOR (Enhanced Oil Recovery)：激產採油法或強化採油法；通常指火攻法(Thermal flooding)、化學沖排法(Chemical flooding)等三期採油法(Tertiary Oil Recovery)，不包含水沖排法(Water flooding)、注氣法(Gas Injection)等傳統方法。

2. IOR (Improved Oil Recovery)：改善式採油法；包含範圍廣泛，例如(1)初期採油法(Primary Oil Recovery)：液裂或酸處理方法、(2)二期採油法(Secondary Oil Recovery)：水沖排法(Water flooding)、注氣法(Gas Injection)、(3)三期採油法(Tertiary Oil Recovery)：火攻法(Thermal flooding)、化學沖排法(Chemical flooding)等任何增產採油方法。

3. 近年來，EOR(Enhanced Oil Recovery)一詞已很少人用，已被IOR(Improved Oil Recovery)取代。

在上述發表文章，其中水平井應用、防砂完井、負壓穿孔及堵水等技術，與未來本公司進行地下儲氣工程均有非常重要之關係，特別值得一提的是其中的七篇，分別為：

- Horizontal Openhole Gravel Packs Boost Oil Production in Brunei.
J. P. Van Vliet, H. C. Lau, O. B. Skilbrei, and S. H. Rahman, Brunei Shell Petroleum Co. Sdn. Bhd ; L. A. Bernardi, T. P. McPike, E. E. Shumilak, and A. S. Halal, Shell E&P Technology Co.

在過去三年，水平井裸孔礫石填充完井已推廣應用於汶萊殼牌油公司（Brunei Shell Petroleum Co.）之油井防砂工程，其主要之理由有如下三點：

- 由生產資料顯示，利用篩管（Stand-alone Screen）裸孔完井的生產井中易受堵塞，產率降低。

- 裸孔礫石填充完井增加油氣流入面積（Inflow Area）且降低堵塞。

- 水平礫石填充完井降低膚表因子。

截至目前該公司已成功地完成21口井水平礫石填充生產井。其水平段長度為100至1,000公尺甚至1,000公尺以上。從他們實際工作所獲得之結論如下：

- 裸孔礫石填充之技術証實已適用於長距離水平段且孔隙與破裂壓力相近之地層。

- 為了達成妥善之礫石填充且在不超越地層強度範圍內泵送礫石，事先應做好電腦模擬工作。

- 各工作小組之密切合作，包括技術輔導小組、井內設備小組、地質與鑽井工程師以及服務公司等乃為裸孔礫石填充之主要關鍵。

- 另外現場專家對於各項工作細節之配合與認真執行，地面與井內設備事前之規劃與準備，礫石填充進行中之注意事項亦為達成成功礫石填充之重要因素。

- Openhole Expandable Sand Screen Completions in Brunei.
H. C. Lau, and J. P. Van Vliet, Brunei Shell Petroleum Co. Sdn. Bhd.

使用膨脹型防砂篩管之水平裸孔完井技術已成功地發展應用於汶萊兩口海域生產井，其主要成功之因素在於選擇良好之鑽入泥漿（drill-in-fluid），以維持井眼之穩定，在接近標準井孔（Near-gauge）之情況下，使篩管能夠順利組下通過。兩口井所使用之鑽入泥漿其中一口井為Synthetie based之泥漿，另一口井使用水基型者（Water based）。

膨脹型防砂篩管有如下之優點：

- 提供較大流入面積，減少篩管受堵或被沖蝕。

- 操作及安裝簡單便捷。

- 較其他之篩管內徑大，易於通過設置隔層封塞器。

- 裸孔完成時，膨脹型篩管可緊貼井壁，避免井壁崩塌出砂，且成本較礫石填充完井低。

- Effective Thru Tubing Gravel Pack Methods in Attaka Field.
C. C. Lee and C. M. Darby, Schlumberger; and T. R. Popp, Unocal Indonesia Ltd.

本文介紹印尼Attaka礦區有多口井因出砂而停產，而這些井因其剩餘可採量有限，用傳統的礫石填充完井法來重新完井不具經濟價值，乃考慮應用1.5”撓曲油管完成礫石填充之修井方式予以完井，避免繼續出砂，恢復生產。此方法之主要優點為：

- 因是不用鑽機之完井（Rigless completion），費用較省。

- 操作簡單容易。

- 採用新礫石填充流體系統，降低地層污損及漏失。

利用撓曲油管經油管完成礫石填充之完井方式有兩種方法，一為封塞法（packoff Method），另一種為釋排篩管法（Vent Screen Method）。所謂封塞法就是利用通過油管之礫石填充篩管以及封塞裝置（Packoff Ass’y），通過3-1/2”油管進入套管內或已存在之礫石填充篩管內，予以設置並封塞在生產管串內部，如圖一示所示。

釋排篩管法乃是利用兩段篩管中間以一般生產管連接置於套管內，生產流體由底部及上部篩管進入而產出，如圖二示所示。

圖二：釋排篩管法	圖一：封塞法

- Maximizing Productivity with Extreme Underbalancing Perforation.
I. Potapieff, L. Francois, A. Rusly, and D. W. Zen, TotalFinaElf; and A. Retnanto and M. Kermoud, Schlumberger.

本文介紹負壓穿孔在Tunu礦區之成功應用情形，此新技術可降低地層污損，提升產率約15%。

由於負壓穿孔在最高差壓4,800psi作業，安全為第一考量因素，本文在陳述如何達成超高負壓之穿孔保護措施。

- Chemical Water & Gas Shutoff Technology - An Overview.
A. H. Kabir, PETRONAS Carigali Sdn. Bhd.

本文介紹利用各種化學方法堵水或堵氣技術，用於處理已出水或因出水而停產之油氣井、或處理油井之堵氣，可讓已出水油氣井恢復生產或油井減少產氣，以延長生產，提高採收率。

- Research of Polyacrylamide Gel Application for Water Shutoff in High Temperature Fractured Granite Basement Reservoirs.
P. Nguyen, Q. V. Ngo, V. Pham, Inst. of Materials Science. 應用膠化物在高溫有裂縫地層堵水成功之實例，膠化物處理已出水或因出水而停產之油氣井，可讓已出水井恢復生產。

- New Technique to Recover By-Passed Reserves Above Packer Reduces the Completion Cost and Maximizes the Production in ONWJ Field, Indonesia.

Yoliandri Susils；Wahju Wibowo；David；Rich；Pajang Priyandoko，BP Indonesia.

一般油氣井如已停產或雙串完成一串停產，另一串仍生產中，為了恢復生產，擬予穿試生產填塞器上面之層次，通常必須利用鑽機，起出井內油管，回堵下層，穿試上層，重新設置新生產填塞器，重下油管予以完井，所需費用高，且費時，如新生產層可採量大，修井仍具經濟價值，否則則無法回收修井成本，修井效益則大打折扣了。

本文乃是針對生產填塞器以上之層次其可採蘊藏量有限，屬於邊際蘊藏量（Marginal Reserves），如用傳統鑽機修井不具經濟價值，因此為降低修井費用不用鑽機，不起油管，改用撓曲油管通過油管於填塞器上方欲穿試生產層部位施行下水泥工作，使欲穿試生產部位及上部約200呎之區段油管與套管間環孔充滿水泥，水泥封固後即有生產填塞器之功能，稱為水泥填塞器（Cement Packer）。水泥封固後經油管穿試生產，如獲生產，則完成修井的目的。按本文介紹利用此種水泥填塞器之方法修井，對於海域井而言，其修井費用約為傳統鑽機修井之20 ~ 60%。

利用水泥填塞器改換生產層之修井技術，在引進應用以前，必須對於三個議題要有充份的把握，才能做到：

第一：水泥填塞器之封固情形影響生產安全至鉅，因此利用撓曲油管通過井內油管下水泥必須做的非常妥善，其水泥配方與操作細節為成敗之關鍵，同時下水泥後油管內不可殘留水泥，否則無法進行通過油管穿試生產層。

第二：通過油管穿孔之穿透能力要能深達地層。在水泥填塞器封固後，通過小徑油管之穿孔器必須穿過油管→水泥→套管→水泥→地層之層層關卡，因此穿孔器之選用至為重要。

第三：要有合適的井才能引進應用，除了事先應詳加評估生產井各層次之剩餘可採量，必須對整體井內結構，套管水泥封固情形，套管油管狀況研判等有充分的了解才可。傳統修井與利用水泥封塞器之修井如圖三所示。

圖三：傳統修井與利用水泥封塞器之修井

除此之外大會還安排綜合專題研討，由E. O. Egbogah，P. L. Coyne，D. Wang，P. McGuire，K. Sampath，G. J. Stosur等六位專家學者輪流報告，主題為IOR/EOR方法之重要性，強調到2020年將有50%的石油應用IOR/EOR方法生產，並提出未來在墨西哥灣至西非之深海區域較具探勘潛能。

  - Schlumberger公司研討水平注產氣井相關技術

參訪Schlumberger公司，除了參觀該公司實驗室外，該公司並針對水平井之鑽井、水泥工程及同步測井等技術作簡報及研討，研討內容均為本公司極重要且需建立之技術，故受益良多。茲摘要分述如下：

- 實驗室參觀：

有泥漿、水泥、岩石力學及地層污損等試驗設備。其特色為高溫高壓泥漿及水泥試驗設備可模擬地層條件且與一般試驗設備隔離，注重工作環境之整潔安全。

- 水平鑽井：

在水平鉆井發展應用初期，由於受限於鉆井設備的功能及技術經驗的不足，因此國際石油工程界決策者常會問工程師「為何要鉆水平井？」。時至今日，由於鉆井設備不斷更新改進及技術日益精進，決策者反而會問「為何不鉆水平井？」。由此可見水平鉆井的優點及經濟效益已被肯定及普遍應用。

近年來，水平鉆井技術及設備之重點歸納簡述如下：

- 地質導向技術(Geological Steering Technology)：使用能轉向的井底馬達(Down-hole Motor)結合隨鉆測井儀(MWD及LWD)，以便能立即提供地層特性、鉆頭轉速、井斜及方向等資料，使鉆井工程人員能隨時修正井程，使鉆頭能沿著生產層或油水界面（或氣水界面）鉆進。

- 頂驅鉆進系統(Top-drive Drilling System)：頂驅鉆進系統的應用可以減少起下鉆的次數，減少泥漿靜置時間，避免卡鉆等事故發生。

- 撓曲鋼管(Coiled Tubing)：新的撓曲鋼管具有高屈服強度、加大外徑、配合其他新式器材已可應用於水平井鉆鑿，以提高鉆進率及降低鉆井成本。

- 單井多水平孔段水平井(Multilateral Horizontal Well)：單井多水平孔段水平井大幅提高產率及生產井壽命，可同時採收不同生產區間，彌補了水平井鉆鑿費用較高的缺點。

- 電腦在鉆井工程的應用：由於個人電腦功能的提升及能精確快速的計算，已被廣泛應用於鉆井工程設計及模擬工作，並將進一步發展成整合式鉆井操作系統。

- 水泥工程：

介紹Schlumberger公司之新水泥配方及施工技術。針對不同環境、地層特性及需求有LiteCRETE、DensCRETE、DeepCRETE、SqueezeCRETE等配方。應用新水泥配方及施工技術可解決生產層上部及水平孔段水泥封固不易之問題。

- 同步測井：

應用同步測井儀(MWD、LWD)可同時測量井程及地層特性。地質導向技術(Geological Steering Technology)能立即提供地層特性、鉆頭轉速、井斜及方向等資料，使鉆井工程人員能隨時修正井程，使鉆頭能沿著生產層或油水界面（或氣水界面）鉆進。

- 建議

本公司為了因應天然氣發電廠用氣量於尖峰與離峰間之巨大變化，以及應付緊急供氣之需，計畫擴充目前鐵砧山儲氣窖之注產規模，提高注產氣能力，研議在鐵砧山地區鑽鑿多口水平井。此次在馬來西亞吉隆坡市所舉辦之亞太激勵採油技術研討會(APIORC)亦將水平井應用及防砂完井技術列為主要議題之一。參訪Schlumberger公司，除了參觀該公司實驗室外，該公司並針對水平井之鑽井、水泥工程及同步測井等技術作簡報及研討，研討內容均為本公司極重要且需建立之技術，故受益良多。經由此次參加「國際水平注產氣井技術研討會」及前往Schlumberger公司研討水平注產氣井相關技術，可歸納出下列之建議：

- 近年來，由於水平鉆井的優點及經濟效益已被肯定及普遍應用，此次之SPE亞太激勵採油技術研討會(APIORC)亦將水平井之應用列為議題。水平井有許多優點例如增加生產區間、提高注/產氣率，避免水錐問題、提高採收率，減少注/產氣井數目等，本公司應評估引進應用。水平井防砂完井方式採用裸孔礫石填充完井或篩管（Stand-alone Screen）完井何者為佳，眾說紛紜，惟依此次SPE汶萊殼牌油公司發表之文章強調採用裸孔礫石填充完井可降低堵塞、產率大、生產壽命長，而篩管完井較易受堵、產率下降、生產壽命短。至於膨脹型篩管防砂技術，因防砂篩管可緊貼井壁，避免井壁崩塌出砂，此為新發展之技術，尚未推廣使用，但值得進一步研究。

- 水平井之水泥配方及施工技術影響套管水泥封固之品質與長久注產安全至鉅，Schlumberger公司建立有完整之水泥試驗設備，可模擬地層條件下之最佳水泥配方，以確保注產氣井套管水泥封固完善，不致因長期受注產切換操作頻繁之影響。針對此問題，將來鐵砧山儲氣窖注產氣井之套管水泥工程亦必須做嚴謹之模擬試驗。

- 傳統利用鑽機修井復產費用昂貴，為降低費用免用鑽機，不起出油管，利用撓曲油管通過油管內可從事各種修井復產工作，諸如通過油管做礫石填充復產、堵水復產、水泥填塞器之修井復產等，此等技術實有進一步研究引進應用之可行性。

- 為了提升本公司之鑽採技術水準能與國際石油工程界並駕齊驅，未來應多派員參加國際性石油相關學會之年會。其優點有：與有關之專家交換研究心得，吸取他們之技術經驗、增加資訊及知識的雙向交流，使深度與廣度都得以提昇、拓展人脈關係及研究資源、提昇公司知名度與形象。

- 附錄

亞太激勵採油技術研討會(APIORC)宣讀論文目錄

SPE 72102 Options for Carbon Recycling From Hydrocarbon Production

A.A. Espie, C.A. Christopher, M.B. Wilkinson, and P. Middleton

SPE 72103 Identifying Improved Oil Recovery Potential: A New Systematic Risk Management Approach

M.A. Thompson and S.G. Goodyear, AEA Technology plc

SPE 72106 Evaluation of CO 2 Gas Injection for Major Oil Production Fields In Malaysia—Experimental Approach Case Study: Dulang Field

Zahidah Md. Zain, N.I. Kechut, and Ganesan Nadeson, Petronas Research & Scientific Services Sdn. Bhd.; Noraini Ahmad, Petronas; and D.A. Raja, Petronas Carigali Sdn. Bhd.

SPE 72107 Unconventional Miscible EOR Experience at Prudhoe Bay: A Project Summary

P.L. McGuire and B.M. Holt, BP plc

SPE 72108 Intelligent Internal Gas Injection Wells Revitalise Mature S.W. Ampa Field

H.C. Lau, Robert Deutman, Salim Al-Sikaiti, and Victor Adimora, Brunei Shell Petroleum Co.

SPE 72110 EOR Possibilities for Development of a Mature Light-Oil Reservoir in Oman

T. Babadagli, A. Al-Bemani, and F. Boukadi, Sultan Qaboos U., and A.W. Iyoho, Petrogas

SPE 72111 Determination of Residual Oil Saturation in a Carbonate Reservoir

Joseph Tang and P-X. Zhang, China Inst. of Atomic Energy, JT Petroleum

SPE 72113 Efficient Two-Phase Upscaling in 2D

G.A. Virnovsky and A. Lohne, RF-Rogaland Research

SPE 72114 Reservoir Monitoring Methodology for a Giant Gas Field

Igor Potapieff, TotalFinaElf E&P Indonesie, and Joop de Wit, Kappa.

SPE 72117 Experience of a Reservoir Waterflood Failure and Remediation Treatment in the Stag Reservoir, Australia

Allan McDiarmid, Helix Well Technologies, and Ivor Alexander, Andy Ion, and Jeffrey Thompson,Apache Energy

SPE 72118 Successful Gas Shutoff Using Latest Gel Technology in an Indian Offshore Carbonate Field—A Case Study

T.K. Sengupta, Rudal Singh, RamAvtar, and Kharak Singh, Oil and Natural Gas Corp.

SPE 72120 Research of Polyacrylamide Gel Application for Water Shutoff in High Temperature Fractured Granite Basement Reservoirs

P.T. Nguyen, V.H. Pham, Q.V. Ngo, and Q.K.L. Bui, Inst. of Materials Science-Vietnam NCNS

SPE 72121 Sensitivity Analysis of Horizontal Well Productivity Under Steady-State Conditions

S.A. Shedid, Suez Canal U., and A.Y. Zekri, United Arab Emirates U.

SPE 72122 Prediction of IPR Curve of Oil Wells in Visco-elastic Polymer Solution Flooding Reservoirs

Xia Huifen, Daqing Petroleum Inst.; Yue XiangAn, Petroleum U.; and Wang Dexi, Li Qun,

and Zhang Xuebin, Daqing Oil Field Co.

SPE 72123 Viscous-Elastic Fluids Can Mobilize Oil Remaining After Water-flood by Force Parallel to the Oil-Water Interface

Wang Demin, Cheng Jiecheng, Xia Huifen, Li Qun, and Shi Jingping, Daqing Oil Co. Ltd.

SPE 72125 Microbial Enhanced Oil Recovery (MEOR) Technology in Bokor Field, Sarawak

M.G. Abd Karim and M.A. Hj Salim, Petronas Carigali Sdn. Bhd., and Zahidah Md. Zain

and N.N. Talib, Petronas Research & Scientific Services Sdn. Bhd.

SPE 72126 Microbial EOR Study To Improve Sweep Efficiency in Caltex Fields:Phase I—Nutrient Selection

Sri Kadarwati, M. Udiharto, and Noegroho Hadi Hs, Lemigas, and J.P. Brinkman and Bangun Yulianto, PT Caltex Pacific Indonesia

SPE 72127 A Numerical Study To Evaluate the Use of WAG as an EOR Method for Oil Production Improvement at B.Kozluca Field, Turkey

Mustafa Cobanoglu, Turkish Petroleum Corp.

SPE 72128 Microbial EOR Laboratory Studies on the Microorganisms Using Petroleum Hydrocarbon as a Sole Carbon Source

Han Peihui, Sun Fengrong, and Shi Mei, Daqing Oilfield Co. Ltd.

SPE 72129 Microbial Enhanced Oil Recovery: Diverse Successful Applications of Biotechnology in the Oil Field

S.A. Bailey, T.M. Kenney, and D.R. Schneider, Micro-Bac Intl. Inc.

SPE 72130 Horizontal Openhole Gravel Packs Boost Oil Production in Brunei

J.P.M. van Vliet, H.C. Lau, O.B. Skilbrei, and S.H.A. Rahman, Brunei Shell Petroleum Co. Sdn. Bhd., and L.A. Bernardi, E.E. Shumilak, and A.S. Halal, Shell E&P Technology and Applied Research

SPE 72131 Openhole Expandable Sand Screen Completions in Brunei

H.C. Lau, Jacques Van Vliet, Mike Ward, David Morin, Arifun Djamil, and Paul Kuhnert, Brunei Shell Petroleum, and Walter Aldaz and Steven Shanks, Weatherford Completions Systems.

SPE 72132 Effective Thru Tubing Gravel Pack Methods in Attaka Field

C.C. Lee and M.C. Darby, Schlumberger, and T.R. Popp, Unocal Indonesia Co.

SPE 72134 Case Study: Maximizing Productivity With Extreme Underbalance Perforation

Igor Potapieff and Francois Lallemant, TotalFinaElf; Albert Rusly and D.W. Zen, TFE E&P Indonésie; and Albertus Retnanto, Mohamed Kermoud, Heru Danardatu, and Murdiyono, Schlumberger

SPE 72135 Field Performance of Propellant/Perforating Technologies To Enhance Placement of Proppant on High Risk Sand Control Completions

K.C. Folse, R.L. Dupont, C.G. Coats, and Doug Finley, Halliburton Energy Services Inc., and D.B. Nasse, Shell Offshore Inc.

SPE 72137 Benchmarking of Steamflood Field Projects in Light/Medium Crude Oils

Alfredo Pérez-Pérez, PDVSA Intevep; Marjorie Gamboa, U. Central de Venezuela; and César Ovalles and Eduardo Manrique, PDVSA Intevep

SPE 72138 Emulsification Characteristic and De-emulsifiers Action for

Alkaline/Surfactant/Polymer Flooding

Wanli Kang, Daqing Petroleum Inst., and Demin Wang, Daqing Oilfield Ltd. Co.

SPE 72142 Sensitivity Study on Geomechanical Properties To Determine Their Impact on Fracture Dimensions and Gas Production in the Khuff and Pre-Khuff Formations Using a Layered Reservoir System Approach, Ghawar Reservoir, Saudi Arabia

Zillur Rahim and M.Y. Al-Qahtani, Saudi Aramco

SPE 72143 Multiphase Pumps for Light Oil Steam Flood, From Design and Operation Perspectives

Erwinsyah Putra, Caltex Pacific Indonesia

SPE 72145 New Technique To Recover By-Passed Reserves Above Packer Reduces the Completion Cost and Maximizes the Well Production in ONWJ Field, Indonesia

Yoliandri Susilo, Wahju Wibowo, David Rich, and Pajang Priyandoko, BP Indonesia

SPE 72146 An Automatic Production Monitoring System—Design and Applications

S-M. Chen, Husky Energy Inc.

SPE 72147 Successful Field Test of the First Ultra-Low Interfacial Tension Foam Flood

Wang Demin, Cheng Jiecheng, Yang Zhenyu, Li Qun, Wu Wenxiang, and Yu Huiyu, Daqing Oil Co. Ltd.

SPE 72148 Use of Permanent Resistivity and Transient Pressure Measurements for Time-Lapse Saturation Mapping

# M. Charara, Y. Manin, C. Bacquet, and J.P. Delhomme, Schlumberger

SPE 72154 A Comparison of Various Laboratory Techniques To Measure Thermodynamic Asphaltene Instability

A.K.M. Jamaluddin, Oilphase; J. Creek, Chevron Petroleum Technology Co.; C.S. Kabir, Chevron Overseas Petroleum Inc.; J.D. McFadden, BHP Petroleum (Americas) Inc.; and D. D’Cruz, M.T. Joseph, N. Joshi, and B. Ross, Oilphase

SPE 72155 Simultaneous Snubbing and Drilling Operation on Long Reach Multi Lateral Improves Field Economics

Dale Tupper and Bryan Anderson, Weatherford Intl..

SPE 72159 The Integrated Technology Solution (ITS)—A Program for the 21st Century

R.M. Nor

SPE 72160 Reservoir Characterization—Integrated Interpretation of Borehole Data and Surface Seismic Data

H. Cao, T. Endo, H. Yamamoto, and D. Cao, Schlumberger

SPE 72165 Hydraulic Fracture Stimulation in Changbei Tight Gas Reservoir—Challenges and Achievements

S-W. Wong, Shell Intl. E&P, and K-K. Hii, Shell Exploration (China) Ltd.

SPE 72166 Monte Carlo Simulation on the Effect of Fracture Characteristics on Reduction of Permeability by In-Situ Bacteria Growth

C. Han, J.M. Kang, and J. Choe, Seoul Natl. U.

SPE 72168 Computer Applications To Enhance Production Optimisation and Process Efficiency

C.E. Scott, Shell Todd Oil Services Ltd.

SPE 72169 Simulation and Optimization of Continuous Gas Lift System in Aghajari Oil Field

Alireza Bahadori, Natl. Iranian South Oil Co., and Sh. Ayatollahi and M. Moshfeghian, Shiraz U.

SPE 72171 Artificial System—Plunger Lift—Time of Fall of the Plunger Under Operative Condition of Well of Petroleum

Eduardo Braganza, U. Nacional del Comahue; Enrique Rost, U. Nacional de la Patagonia; and Esteban Gonzalez and Antonino Salleo, U. Nacional del Comahue

SPE 72192 The Technology of Microbial Treating Drained Water of Oil Field

Wang Weidong, Li Ximing, Chen Yong, Zhang Songting, and Jiang Yan, Oil Production Research Inst. of Shengli Oil Field

SPE 72100 Maximizing Field Potential Through Improved and Enhanced Oil Recovery

A. Taha and R. Muslim, Petronas, and D.A. Raja, Petronas Carigali Sdn. Bhd.

SPE 72116 Pressure-Dependent Pore Volume Compressibility—A Cost-Effective Approach

S. Ong, Z. Zheng, and R.V. Chhajlani, Baker Atlas

SPE 72119 Chemical Water & Gas Shutoff Technology—An Overview

A.H. Kabir, Petronas Carigali Sdn. Bhd.

SPE 72136 Reservoir and Heat Management To Optimize Steam Injection in a Mature Multi-Zone Steam Flood in the Duri Field

A. Widyantoro, W. Winderasta, C. Muharam, P. Saptarani, and A.R. Deemer, PT Caltex Pacific Indonesia

SPE 72140 Assessment of Dulang Field Immiscible Water-Alternating Gas (WAG) Injection Through Composite Core Displacement Studies

G. Nadeson and Z. Md Zain, Petronas Research/Scientific Services

SPE 72141 Cyclic Waterflooding and Fast IOR Evaluation Using Analytical Solutions

L.M. Surguchev and E. Reich, Petec Software & Services, and G.A. Virnovsky, RF-Rogaland Research.

SPE 72149 SF-30, The World’s First SMART Field

P.J. Bogaert, A.C. Chong, K. Ngu, and B. Sim, Sarawak Shell Berhad

SPE 72150 Evaluations of Horizontal Wells Performance With Optical and Electrical Probes

C. Mas, Schlumberger; J.P. Van Vliet and S.H. Rahman, Brunei Shell Petr. Co. Sdn. Bhd.; and B. Walterhouse, Schlumberger

SPE 72153 New-Generation Underbalanced Drilling 4-Phase Surface Separation Improves Operational Safety, Efficiency, and Data-Management Capabilities

R.R. Bullock, J.M. Karigan, and T.O. Wiemers, Halliburton Energy Services

SPE 72161 Development and Implementation of a Multi-User, Integrated Database Management System: An In-House Effort G. Das, Oil India Ltd., and P. Bandyopadhyay, Reliance Industries Ltd.

SPE 72162 Subsurface Data Management—Of Softer Issues and Staying Sane P.C. Lesslar, Sarawak Shell Berhad

SPE 72163 Jintan: Multi-Scenario Reservoir Modelling—Step 1: Static Modelling

F.M. David, Sarawak Shell Berhad

SPE 72164 Modified Technologies of Injecting Cross-linked Polymer Compositions Into Layer

A.G. Telin, M.E. Khlebnikova, I.S. Kolchugin, and V.K. Singizova, Yukos Oil Co., and T.I. Zainatdinov

SPE 72167 Optimizing Field Performance Using Reservoir Modeling and Simulation M.A. Naguib, Suez Oil Co.

SPE 72170 Defining the Evolve Gas Rate and Composition From the Crude Oil During Its Storage in Tanks E.M. Braganza, L.G. Fernandez, and C.A. Garcia Tourn, U. Nacional del Comahue