摘    要

本計畫係配合九十一年度研究計畫「裂縫油氣層評估技術研究」執行。本公司在開拓國內、外礦區時曾遭遇一些裂縫油氣層（如BGOI、F構造等），隨著國外業務的拓展，未來接觸裂縫油氣層的機會勢將愈來愈多。裂縫油氣層與一般傳統油氣層有截然不同的生產流動特性，本公司過去對於此種油氣層的評估與開發並未累積太多的經驗。希望藉由參加裂縫油氣層評估技術研討會的機會，蒐集資料並累積經驗與技術。

本出國計畫係參加美國石油工程師學會2002技術年會及展覽，會中有多場裂縫油氣層評估技術之相關分組討論，包括裂縫系統、裂縫診斷方法、裂縫模式之建立、裂縫個案研究及裂縫油氣層特性研究等議題。配合此次會議同時尚有石油開採相關設備展示，可從中獲取最新先進軟硬體資訊。

本報告描述會議過程及多篇論文摘要，並針對所參加之裂縫油氣層相關分組討論提出心得。

目   錄

頁次

摘  要			I

壹、出國目的			1

貳、行程			1

參、技術論文發表			1

肆、參展廠商			9

伍、心得與建議			9

附錄－分組討論論文詳細目錄			  17

- 出國目的

本公司在開拓國內、外礦區時曾遭遇一些裂縫油氣層（如BGOI、F構造等），隨著國外業務的拓展，未來接觸裂縫油氣層的機會勢將愈來愈多。裂縫油氣層與一般傳統油氣層有截然不同的生產流動現象，本公司過去對於此種油氣層的評估與開發並未累積太多的經驗，希望藉由參加裂縫油氣層評估技術研討會的機會，蒐集資料並累積經驗與技術。

- 行程

本計畫參加美國石油工程師學會2002技術年會及展覽（SPE 2002 Annual Technical Conference and Exhibition），此會議中討論各種石油工程之實務議題，其中裂縫油氣層之評估與開發為本計畫之重點。會中有多場裂縫油氣層評估技術相關分組討論，包括裂縫系統、裂縫診斷方法、裂縫模式之建立、裂縫個案研究及裂縫油氣層特性研究等議題。配合此次會議同時有SPE之設備與軟硬體展覽，可獲取最新先進軟硬體資訊。

今年度美國石油工程師學會技術年會及展覽，於91年9月29－10月2日假美國德州聖安東尼市會議中心（Henry B. Gonzalez Convention Center）舉行，議程包含年會、委員會會議、技術論文發表、展覽及訓練課程等。

- 技術論文發表

本次會議的重頭戲技術論文發表計有近380篇的論文發表，共分76個場次，最多同時有14個會場在進行論文宣讀。內容涵括管理、開發地質與地球物理、鑽井、經濟與評估、新穎與周邊技術（Emerging & Peripheral Technology）、設施與建造、流體力學、天然氣技術、油層監測與測試、生產操作、油層工程、完井、電測等石油工程領域（圖一）。其中與本計劃較為相關的為：

- 9/30上午Fundamentals of Fractured Systems

- 9/30下午Fracture Diagnostic Methods

- 10/1上午Well Testing for Formation Characterization

- 10/1下午Hydraulic Fracturing Modeling and Methodology

- 10/2上午Fracturing Case Study

- 10/2下午Characterizing Fractured Reservoirs

以下擷取部分論文精華。

  - 使用靜態與動態資料建構裂縫網路模式Construction of Fracture Network Model Using Static and Dynamic Data（SPE 77741）

本文為日本JAPEX公司所發表，以井孔影像的靜態資料配合微分壓力曲線的動態資料，建構一分散式的裂縫網路模式（DFN）。在DFN中由兩種流動機制所組成，一是寬孔徑之裂縫，為主要流動通道；另一為窄孔徑之裂縫，主要功能為儲存流體。每一種流動都以碎形理論及地質統計方法來定義裂縫的尺寸與空間分布，

  - 沙烏地阿拉伯Ghawar油田裂縫受孔隙壓力控制而再度活動Pore Pressure Control of Fracture Reactivation in the Ghawar Field, Saudi Arabia（SPE 77642）

Ghawar油田為世界上目前所發現之最大油田，位於沙烏地阿拉伯東部省份。1983-1990期間此油田之南側因國際需求減少而暫時封存，在這段期間內仍照常監測油層壓力與溫度。由這些數據中發現有壓力下降區間的現象，由於當時並沒有生產，此一現象應當與人為無關，因此利用模擬程式與裂縫特性研究來尋找其成因。

研究結果顯示此一現象之成因可能如下：在初期生產涸竭之後，自然裂縫因壓力下降而關閉，而裂縫面之有效應力上升，隨後孔隙壓力由於停產也上升，孔隙壓力係因為流體膨脹而增加，因而降低了有效應力，當有效應力降到臨界值時，斷層即再度活動並且造成自然裂縫延伸。此一說法由壓力下降區間與裂縫發達方向之對比可獲得證實（圖二－圖五）。

  - 整合壓力與震測數據以決定單或雙孔隙油氣層特性Integrating Pressure-Transient and Seismic Data to Determine the Characteristics of Single- and Double-Porosity Reservoirs （SPE 77451）

本文整合壓力試驗與多分量震測（Multi-Component Seismic）資料以決定單孔隙或雙孔隙油氣層特性，作者認為由壓力試驗所求得之儲存容量比（Storage Capacity Ratio，）與由震測資料所估算之正常裂縫空間（Normal Fracture Compliance，ZNf）間存在著一定的關係，經由不同方法來計算這些參數可降低各單一方法之非唯一性的問題。圖六為本文範例中與ZNf之關係。

  - 密集監測油氣層以分析低滲透率凝結油相態Characterisation of Low Permeability Gas Condensate Behaviour by Intensive Reservoir Monitoring（SPE 77618）

位於北海北部的Alwyn North Complex生產Triassic Upper Lunde油氣層，其厚度達700 m但其滲透率極低，在油氣層上部450 m為凝結油。至2001年底已進行16次PLT，搭配MDT（Modular Dynamic Tester）及安裝於佐證井中之井下永久壓力與溫度計所得到的數據，以兩種方法計算六口井之連通體積（圖七）。

井下數據可監測生產指數之變化，此外尚可由壓力上升試驗瞭解有效滲透率及膚表因子隨時間之變動情況，同時獲知定量因凝結油形成所造成之影響，以及岩石物理性質間之關係。

  - 裂縫碳酸岩油氣層流動網路之組織架構：關鍵參數之確認與特性分析Hierarchical Organization of Flow Network in Fractured Carbonate Reservoirs: Identification and Characterization of Key Parameters（SPE 77488）

這篇由Total Fina Elf公司所提出的論文，藉現場數據、露頭觀察與地下水流動研究等方法尋找裂縫網路（Fracture Network）與流動通路（Flow Network）間之關係，顯示瞭解裂縫網路架構為油氣層特性分析的重要關鍵（圖八）。

Lacq氣田，為一巨型裂縫碳酸岩油氣層，其生產層並非位於裂縫密度最高的區域，由隧道及地下採石場觀察現地裂縫網路及地下水流動也發現同樣的結果，因此可知裂縫密度並非流動的驅動參數。在計算裂縫模式的相當滲透率時發現裂縫孔徑（Aperature）分布（也就是水力性質分布）在不確定性評估上比裂縫分布的影響更為重要。

  - 裂縫中流動在基岩與裂縫轉換中所扮演之角色Role of Fracture Flow in Matrix-Fracture Transfer（SPE 77336）

超過三分之一的油氣田具有裂縫，最常用的裂縫模式為雙孔隙率或雙滲透率模式，在這種模式中假設流體經由裂縫流動，基岩（Matrix）負責儲存流體，基岩與裂縫間的交換以轉換函數（Transfer Function）描述。自生逆向自吸（Spontaneous Countercurrent Imbibition）是水濕性岩石基岩與裂縫間交換的主要機制，因此瞭解其物理現象可改善此種模式。

過去固然有許多逆向自吸的相關研究，但於裂縫流體流速對採收率之關係上則較少討論。本文作者提出一微滴解離模式（Droplet Detachment Model）以計算位於基岩-裂縫介面上之有效含水飽和度，此一飽和度是流體類型、流體於裂縫中之速度與裂縫幾何形狀的函數。

研究結果顯示，裂縫流體流速為影響基岩-裂縫介面上有效含水飽和度之重要參數，當裂縫流體流速大於臨界流速時，介面上之有效含水飽和度會增加，因而增加基岩之採收率。

  - 日本第一個裂縫處理成功案例：深層天然裂縫火山岩之激勵增產挑戰The First Successful Propped Fracture Treatment Campaign Conducted in Japan: Stimulation Challenges in a Deep, Naturally Fractured Volcanic Rock（SPE 77678）

位於日本新瀉縣的Minami-Nagaoka氣田，在10年前施行裂縫處理時相當困難，只有約20%的支撐劑能送達預定位置，在尚未泵送支撐劑前，淨壓力（Net Pressure）即已達到4,000 psi，這是在其他油氣田少見的現象，代表其裂縫生長極為複雜。事後評估發現問題可能出在同時產生許多極窄的多重裂縫，這種裂縫既無導通能力也不具經濟價值。

本文介紹許多非傳統的改變來降低這些負面效應，這些改變包括：改變完井以獲致最高注入率、主動的支撐劑策略、即時裂縫處理分析、凝膠試驗、細心穿孔、極度過平衡穿孔以及使用小顆粒的支撐劑等。

  - 連接天然裂縫生產井凝膠處理之實驗室與現場結果Connecting Laboratory and Field Results for Gel Treatments in Naturally Fractured Production Wells（SPE77411）

本文介紹利用HPAM聚合物與有機Crosslinker，在實驗室岩心沖排所得到之油及水之RRF分別為20與200，將此凝膠實際應用於委內瑞拉之Motatan油田。其P-47號井在注入1,000桶凝膠之後，水切由97%降到64%，油產率增加36%。成功的因素主要來自地層滲透率、孔隙率、流體飽和度、流體性質、流體產率及施放凝膠前、中、後之壓力降，尤其以後者最為重要。

  - 直接分析油基泥漿及鑽屑中碳氫化合物的新工具Pollut-Eval: An Innovative Tool for Direct Hydrocarbon Characterization in Oil Base Mud & Cuttings（SPE 77472）

由於環境保護的要求日益嚴格，油基泥漿及其鑽屑不再可以任意棄置，油公司必須開發具經濟性的處理方式。IFP將其原先使用於探勘的Rock-Eval改裝成適合環保用途的Pollut-Eval。

本文即分別從純碳氫化合物分析、鑽井泥漿TOC評估及棄置鑽屑的殘餘含油量等分析結果，展示Pollut-Eval的功能。最後並與氣相層析儀的分析結果比較（表一），結果並不遜色。IFP認為Pollut-Eval不需要前處理，且對於低含油量較為準確，於安裝泥漿線上監測也非常簡單。

  - 由鑽屑中快速且直接量測滲透率的方法A Fast and Direct Method of Permeability Measurements on Drill Cuttings（SPE77563）

本篇也是由IFP所提出之論文。將約100 cc的鑽屑置於壓力容器（圖九）中，以黏度較高的油填滿，油在進入鑽屑前會有一定量的殘存氣，在對容器施壓時，油會因氣體壓縮而進入鑽屑中，然後採用一簡單的數學模式由油進入鑽屑的動態中推算滲透率。此方法已經利用已知滲透率的岩樣磨碎後量測得到證實（圖十），整個量測過程只需要數分鐘，適用於鑽井現場。

  - 鑽井廢棄物之管理：過去、現在與未來Drilling Waste Management: Past, Present, and Future（SPE77388）

根據美國石油學會（API）估計1995年美國陸上鑽井所產生的廢棄物有一億五千萬桶之多，陸上或海域鑽井廢棄物之處理方法因地區而異，海域大多以排放、注入地層或運送回岸處理；路上則採舖地、現場掩埋、地下注入、焚化或其他熱處理方法、生物處理及回收再利用等方法為原則。

由於法令日趨嚴格，未來必須採行對環境衝擊較低的鑽井方式，本文認為選擇處理方法必須考量法規、廢棄物處理成本及操作者的責任等三方面。

  - 以天然氣水合物做為資源與輸送機制Gas Hydrate as a Resource and a Mechanism for Transmission（SPE 77334）

本文由世界能源未來供需平衡，認為天然氣水合物為21世紀之重要能源，能在2050年提供大量的能源，為開發天然氣水合物，未來20年將著重在確認資源的存在及安全的生產技術上。此外，許多天然氣資源可能以水合物的型態運送到市場，根據前蘇聯在1970年代的研究，以水合物型態作長程運輸並不可行，但以水合物漿（Hydrate Slurry）方式在管線中作短距離輸送則屬可行，未來重點在於如何製成水合物漿而非固體水合物。

  - 以油層特性描述改善整治系統的設計與操作之個案研究Case Studies Using Reservoir Characterization To Improve Remediation System Design and Operation（SPE 77554）

本文將原先運用於石油探採的油層描述方法有效應用於描述地表的地下水系統，以研判淺層污染含水層系統之水力流動單元及連通性，便於有效地發展整治設計與操作計畫。本文討論兩處案例，探討包括岩心描述、沉積環境對比等技術之應用情形。

  - 垂直井氣錐或水錐時毛細流體介面之預測Prediction of Capillary Fluid Interfaces During Gas or Water Coning in Vertical Wells（SPE 77772）

水錐或氣錐會使生產量降低而成本大幅提高，過去以模擬與實驗配合簡單的解析解或相關式來降低水錐或氣錐並提高產率，但目前的解析解並未考慮毛細壓力，因此導致分散流動（Segregated Flow），本文提出新的解析解以補救此一缺失。

新的解析解假設垂直井內流體達到垂直平衡，探討控制水錐之重要無因次參數，並建立無因次之兩相生產視窗（圖十一），用以預測臨界產率及不會發生水錐或氣錐之最大產率。

  - 其他論文

限於篇幅無法一一介紹，其他值得一讀的論文尚有：

SPE 77347	Enhanced Gas Recovery by Carbon Dioxide Sequestration in Depleted Gas Reservoirs（注入二氧化碳增加天然氣採收）

SPE 77348	CO2 Enhanced Gas Recovery Studied for an Example Gas Reservoir（二氧化碳增加天然氣採收）

SPE 77371	Natural Gas: The Excruciating Transition（天然氣：苦惱的過渡時期）

SPE 77382	An Efficient Tuning Strategy To Calibrate Cubic EOS for Compositional Simulation（有效的狀態方程式調諧策略）

SPE 77386	Analysis of Black Oil PVT Reports Revisited（黑油PVT分析報告）

SPE 77499	A Neural Network Model for Prediction of Liquid Holdup in Two-Phase Horizontal Flow（預測兩相水平流動之液體聚積）

SPE 77540	Relative Permeability From Capillary Pressure（由毛細壓力推估相對滲透率）

SPE 77545	A Unified Theory on Residual Oil Saturation and Irreducible Water Saturation（殘餘油飽和度與原生水飽和度）

SPE 77549	Forecasting Liquid Condensate and Water Production From Gas-Condensate Wells（產水量預測）

SPE 77550	Direct Estimation of Gas Reserves Using Production Data（油生產數據估算天然氣蘊藏量）

SPE 77553	Drill Cuttings Injection: A Review of Major Operations and Technical Issues（鑽屑注入）

SPE 77557	Extending Foam Technology From Improved Oil Recovery to Environmental Remediation（運用泡沫技術於環境整治）

SPE 77561	High Resolution Downhole Measurements of Porosity and Fluid Saturation While Coring

SPE 77649	Wellbore Heating To Prevent Liquid Loading

SPE 77668	A Case Study: Field Development Plan for a Highly Overpressured Gas Reservoir in China by a Multidiscipline Consulting Team

SPE 77671	A Case Study: Using Modern Reservoir Characterization To Optimize Future Development of a Mature Asset

SPE 77683	What is the Magic of Water in Producing Sand?

SPE 77686	Sand Control: Sand Characterization, Failure Mechanisms, and Completion Methods

SPE 77691	Effective Well and Reservoir Evaluation Without the Need for Well Pressure History

SPE 77693	Experiences Learned After Producing More Than 300 Million Barrels of Oil by Polymer Flooding in Daqing Oil Field

SPE 77701	Gas/Condensate and Oil Well Testing - From the Surface（由地表做油井測試）

SPE 77742	An Effective Technique of Estimating Drainage Shape, Magnitude and Orientation in A Low-Permeability Gas Sand

SPE 77743	Successful Integration of Sparsely Distributed Core and Welltest Derived Permeability Data in a Viable Model of a Giant Carbonate Reservoir

SPE 77569	The Analysis and Interpretation of Water-Oil-Ratio Performance

- 參展廠商

本次會議的展覽部分計有400家以上的廠商參展，展示內容包括探勘、鑽井、生產、開發、電測、工安環保等石油工程上、中、下游之軟硬體設備。

其中Schlumberger、Halliburton、BJ、Weatherford、Baker Hughes、M-I等公司更以極大的攤位展示其產品與服務。相片一及二為展覽會場之一隅。

- 心得與建議

- 分組討論熱烈，部分專題並有尖銳對話，顯露與會者的積極投入及工程師求真本色的發揮。

- 參加人數眾多，且與會人員不僅限於美國地區，歐亞非等外國人有增多的趨勢，這可能和SPE積極國際化有關。

- 參加此一會議不僅可以掌握最新技術，獲取新知及新設備之訊息，同時在與國外專家交談之間也是交換訊息、資訊的好機會。

- 為因應與會者換場的需求，每一分組討論之主席在時間之掌握極恰當，當然每一論文排定充裕的時間（25分鐘）發表與討論也是主要原因。

- 除了石油工程以外，SPE尚接受其他相關論文的發表，如二氧化碳注入、天然氣水合物及污染整治（利用石油工程之技術），顯示SPE的恢弘氣度能夠兼容並蓄，同時也意味著這些領域將漸漸為石油工程界所肯定。

- 煤層甲烷氣（Coal Bed Methane）為未來趨勢，宜加關注。

- SPE年會之分組討論均多場同時舉行，且內容範圍包羅萬象，建議本公司宜同時派遣不同領域工作同仁參與或組團前往，不僅可壯聲色也免捉襟見肘。

圖一	分組討論議程

| 圖二 壓力下降區間（摘自SPE 77642） | 圖三 裂縫發達方向（摘自SPE 77642） |
| --- | --- |
| 圖四 模擬壓力下降情形（摘自SPE 77642） | 圖五 裂縫網路分布情形（摘自SPE 77642） |

圖六	與ZNf之關係（摘自SPE 77451）

圖七 各井連通模式（摘自SPE 77618）

圖八	裂縫油氣層型態與性質（摘自SPE 77488）

圖九 以鑽屑量測滲透率之實驗設備（摘自SPE 77563）

圖十 實驗與模式結果吻合情形（摘自SPE77563）

圖十一	無因次之兩相生產視窗（摘自SPE 77772）

表   Pollut-Eval與氣相層析儀分析結果比較（摘自SPE 77472）

相片一	展覽會場一隅

相片二	展覽會場一隅

附錄－分組討論論文詳細目錄

2002 SPE ANNUAL TECHNICAL CONFERENCE AND EXHIBITION

OUT OF THE BOX LOGGING

77329 Viscosity Predictions for Crude Oils and Crude Oil Emulsions Using Low Field NMR A.Z.

77330 A New Method of Calibrating Wireline Log Data With Carbonate Core Measurements To Recognize Pay Zones

77331 Watercut Measurement Using Microwave Energy Absorption—Theory, Field Trial, and Applications

##### NONCONVENTIONAL GAS

77332 Advances in the Prediction and Management of Elemental Sulfur Deposition Associated With Sour Gas Production From Fractured Carbonates

77333 Application of Leaky Aquifer Type Curves for Coalbed Methane Characterization

77334 Advances in Gas Hydrate Technology

77335 Development of a Heterogeneous Low Permeability Gas Field: What Is Most Important?

### FUNDAMENTALS OF FRACTURED SYSTEMS

77336 Role of Fracture Fluid Flow in Matrix-Fracture Transfer

77338 Fluid Flow in Fractures Visualized by MRI During Waterfloods at Various Wettability Conditions: Emphasis on Fracture Width and Flow Rate

77339 Characterization of Acid Gas Diffusion in a Carbonate Fractured Reservoir Through Experimental Studies, Numerical Simulation

77340 Modeling Coupled Fracture-Matrix Fluid Flow in Geomechanically Simulated Fracture Networks

### WIRELINE FORMATION TESTING

77342 In-Situ Permeability Anisotropy vs. Depth in a Fluvial Sandstone Reservoir Using a Multiprobe Formation Tester

77343 Pressure-Pressure Convolution Analysis of Multiprobe and Packer-Probe Wireline Formation Tester Pressure Data

77344 Recent Examples of Single-Probe Transient Pressure Analysis From Wireline Formation Testers

77345 Inversion of Multiphase Petrophysical Properties Using Pumpout Sampling Data Acquired With a Wireline Formation Tester

### CARBON DIOXIDE AND GAS STORAGE

77346 Phenomenological Inventory Analysis of Underground Gas Storage in Salt Caverns .

77347 Enhanced Gas Recovery by Carbon Dioxide Sequestration in Depleted Gas Reservoirs

77348 CO2 Enhanced Gas Recovery Studied for an Example Gas Reservoir

### WET GAS METERING

77349 Wet Gas Metering Using Dissimilar Flow Sensors: Theory and Field Trial

77350 Wet Gas Metering With Venturis and V-Cones

77351 Wet Gas Metering: Trends in Applications and Technical Developments

### WELLBORE STABILITY AND LOST CIRCULATION

77352 Light Annular MudCap Drilling—A Well Control Technique for Naturally Fractured Formations

77353 Making a Case for Rethinking the Lost Circulation Treatments in Induced Fractures

77354 Application of Quantitative Risk Analysis to Pore Pressure and Fracture Gradient Prediction

77355 Borehole Stability in Naturally Fractured Reservoirs

### DEEPWATER DRILLING

77356 Deepwater Drilling Performance

77357 Innovative Design Method for Deepwater Surface Casings

77358 Drilling Parameter Selection for Well Quality Enhancement in Deepwater Environments

### GEOPHYSICAL APPLICATIONS

77359 Assessing the Value of 3D Seismic Data in Reducing Uncertainty in Reservoir Production Forecasts

77360 Pore Pressure Prediction for the Cocuite Field, Veracruz Basin

77361 Real-Time 4D Reservoir Characterization Using Passive Seismic Data

77362 Rapid Assessment of 3D Seismic and Its Economic Impact

### PERFORATING ADVANCES

77363 A New Skin Factor Model for Perforated Horizontal Wells

77364 New Underbalanced Perforating Technique Increases Completion Efficiency While Eliminating Costly Acid Stimulation

77365 Correlating Particle Size Distribution in a Crushed Zone to Perforating Permeability Damage and Modeling Using Fragmentation Fractal Theory

### MATRIX ACIDIZING

77366 Chelating Agent Based Fluids for Optimal Stimulation of High-Temperature Wells

77368 Successful Diversion of Acid Stimulation in Water-Producing Oil Wells: Case Histories Nisku Formation, Central Alberta

77369 Modeling, Simulation, and Comparison of Models for Wormhole Formation During Matrix Stimulation of Carbonates

77370 The Impact of HCI to HF Ratio on Hydrated Silica Formation During the Acidizing of a High-Temperature Sandstone Reservoir in Saudi Arabia

### POSTERS

77758 A Petrophysics and Reservoir Performance-Based Reservoir Characterization of the Womack Hill (Smackover) Field (Alabama)

77759 Feasibility Assessment of a New Approach for Integrating Multiscale Data for High-Resolution Reservoir Characterization

77760 KONSAS: An Exhaustive Reservoir Model To Evaluate the Contribution of Seismic to Reservoir Characterization

77761 Temperature Effects in Brazilian, Uniaxial, and Triaxial Tests With High Porosity Chalk

77762 The Kitchen Prospects, Cook Inlet Alaska: A Giant Natural Gas Accumulation

77763 Real-Time 4D Passive Seismic Imaging of Hydraulic Fracturing

77764 An Integrated Approach to Basinwide Management Plans

77765 Natural Gas Liquids and LNG Production From Crudes and Wet Gases

77766 U.S. Natural Gas Market: Recent Dynamics and Future Concerns

77767 Productivity Decline in Oil Wells Related to Asphaltene Precipitation and Emulsion Block

77768 Field Application of a Novel Emulsified Scale Inhibitor System to Mitigate Calcium Carbonate Scale in a Low-Temperature, Low-Pressure Sandstone Reservoir in Saudi Arabia

77769 Development Well Testing Enhancement Using a Multiphase Flowmeter

77770 Phase Envelope Calculations for Hydrocarbon-Water Mixtures

77771 Getting the Best From Formation Testing Sampling

77772 Prediction of Capillary Fluid Interfaces During Gas or Water Coning in Vertical Wells

77773 Multizone Gas Well Stimulation Using a High-Performance Composite Bridge Plug: A Review of 75 Runs and Selected Case Histories

77774 A Comparison of Interventionless Packer Setting Techniques and Enhanced Functionality Considerations

77775 New Technique Restores Initial Fluid Efficiency Observed in Mini-Frac and Results in Increased TSO Frac-Pack Success

77776 Stability of an Open Hole Completed in a Limestone Reservoir With and Without Acid Treatments

77778 Use of Core Data in Log Lithology Calibration: Arab-D Reservoirs, Abqaiq and Ghawar Fields

77779 Utilization of Geomechanics for Medusa Field Development, Deepwater Gulf of Mexico

77780 3D Quantification of Vugs and Fracture Networks in Limestone Cores

77781 An Integrated Approach for Secondary-Porosity Evaluation in Carbonate Reservoirs: A Kuwait Case Study

77782 Integrating Borehole Flow Images With a Conventional Production Log Interpretation Method

77783 A Method for Developing Rock Mechanical Property Logs Using Electrofacies and Core Data

77784 Identifying Bypassed Reserves and Monitoring Fluids Using Carbon-Oxygen Logs in Tia Juana Field, Lake Maracaibo, Venezuela

77785 Case History and Applications in a Permian Basin Devonian Gas Pay Using a Cased-Hole Pulsed Neutron Logging Tool and Acid-Soluble Diverter Cement Techniques To Accurately Improve Pay Identification and Significantly Increase Production

77786 A New Technology for Resistivity Anisotropy Evaluation in Conductive Borehole Environments

77787 Primary and Secondary Porosity Estimation of Carbonate Formations Using Total Porosity and the Formation Factor

77788 New C/O Methodology Applied for Reservoir Monitoring in Atypical Casing Completion and Complex Lithology: A Case Study

77789 A Visualization of Thomas Stieber Shale Distribution Model and Resistivity Anisotropy and an Error Sensitivity Comparison Between Water Saturation Equations Utilizing Scalar and Tensorial Resistivity Data

77792 Application of Shear Anisotropy From a New Generation Crossed Dipole Acoustic Tool

77793 Wellsite Resistivity Anisotropy Interpretation: A 2D Method and Case Studies From the Gulf of Mexico

77794 A Method To Improve Stimulation and Completion Design by Integrating Nuclear Magnetic Resonance (NMR) Logs With NMR Measurements on Core Samples

77972 Comparisons of Predictions From Reservoir Models to Actual Production Data: Field Examples

### STRANDED GAS

77371 Natural Gas: The Excruciating Transition

77373 Advances in Advanced Gas-to-Liquids Technology

### STREAMLINE SIMULATION

77374 Statistical Ranking of Stochastic Geomodels Using Streamline Simulation: A Field Application

77375 New Reservoir Dynamic Connectivity Measurement for Efficient Well Placement Strategy Analysis Under Depletion

77376 IOR Forecasting Using a Full-Field Front-Tracking Reservoir Simulator in the Kuparuk River Field, North Slope, Alaska

77377 A Streamline Approach for Ranking Reservoir Models That Incorporates Production

77378 A Combined Geostatistical and Streamline-Based History Matching Procedure

77379 Compositional Streamline Simulation

77380 An Analysis on Advection-Dispersion Ratio To Incorporate Dispersive Transport Into Streamline Simulation

### RESERVOIR PVT

77381 Simplified Method for Calculation of Minimum Miscibility Pressure or Enrichment

77382 An Efficient Tuning Strategy To Calibrate Cubic EOS for Compositional Simulation

77383 Modeling the Effect of External Gas Flux on Reservoir Fluid Distribution

77384 Complex Phase Behavior of the Subsurface Fluids K. Luo, Research Inst. of Exploration and Development

77385 Cubic Equations of State Applied to HT/HP and Highly Aromatic Reservoir Fluids

77386 Analysis of Black Oil PVT Reports Revisited

77387 Multiphase Equilibrium Calculation Using Reduced Variables

### HSE SUMMIT: EXPERTS ON THE ISSUES

77388 Drilling Waste Management: Past, Present, and Future

77389 Produced Water Regulations in the United States: Then, Now, and in the Future

77390 Environmental Regulatory Framework in the North Sea: An Update of the Existing and Foreseeable Constraints

77391 The New Gulf of Mexico NPDES Permit: How Does It Shape Up?

77394 Determination of Environmental Liabilities and Development of a Facility Closure Plan for a State Oil Company

77393 Aging Facilities Present a Potential Environmental Threat

### NUCLEAR MAGNETIC RESONANCE LOGGING

77395 Nuclear Magnetic Resonance While Drilling in the Southern North Sea

77396 Study of Vuggy Carbonates by Using NMR and X-Ray CT Scanning

77397 Wettability, Saturation, and Viscosity Using the Magnetic Resonance Fluid Characterization Method and New Diffusion-Editing Pulse Sequences

77398 Numerical Simulations of NMR Responses for Improved Interpretation of NMR Measurements in Reservoir Rocks

77399 Quantification of Multiphase Fluid Saturations in Complex Pore Geometries From Simulations of Nuclear Magnetic Resonance Measurements

77400 Applications of a New-Generation Wireline NMR Logging Tool

77401 An Evaluation of the Application of Low Field NMR in the Characterization of Carbonate Reservoirs

### PROCESSES FOR TECHNOLOGY TRANSFER

77402 Practical Preparations for the Big Crew Change

### MULTIPHASE FLOW METERING

77403 Field Implications of Uncertainties in Multiphase Flow Measurements

77404 Field Experience of Multiphase Flow Measurements in Scaling Conditions

77405 PVT Sampling With Multiphase Flowmeters—Theoretical Justifications and Field Limitations

77406 Testing Conventionally Untestable High-Flow-Rate Wells With a Dual-Energy Venturi Multiphase Flowmeter in Usari Field, Offshore Nigeria

77407 Knowledge Discovery in Databases and Multiphase Flow Metering: The Integration of Statistics, Data Mining, Neural Networks, Fuzzy Logic, and Ad Hoc Flow Measurements Toward Well Monitoring and Diagnosis

77408 Low Field NMR Water Cut Metering

77409 A Method for Real-Time Well Cleanup Optimization

77410 Survey Paper on the Use of MPFMs in Venezuela, Present and Future

### WATER CONTROL AND MANAGEMENT

77411 Connecting Laboratory and Field Results for Gel Treatments in Naturally Fractured Production Wells

77412 Relative Permeability Modifier and Scale Inhibitor Combination in Fracturing Process at San Francisco Field in Columbia, South America

77413 Application of Laboratory Techniques To Assess Water Quality Standards: Review of Water Quality Requirements for a Saudi Arabian Carbonate Reservoir To Aid in the Diagnosis of Injectivity Decline Noted in Some Injectors

77414 Relative Permeability Modification Using an Oil-Soluble Gelant To Control Water Production

77415 A Study of Water Coning Control in Oil Wells by Injected or Natural Flow Barriers Using a Scaled Physical Model and a Numerical Simulator

77416 New Dual-Completion Technology Reduces Water Cresting in Horizontal Wells and Improves Oil Recovery Factor

77417 Case Study: Using a New Crosslinked Polymer Technology To Reduce the Water-to-Gas Ratio in a Mississippi Canyon Well

### GETTING A GRIP ON RISKS

77418 Assess Risk and Size Dependencies in a Geologic Play With Multiple Zones and Multiple Prospects

77419 The Exploitation Enigma

77420 Exploration Economics of Multizone Prospects: A Comparison With Single Zone Approximations

77421 Distributions of Parameters for Use in Stochastic Evaluations and Decision and Risk Analysis

77422 Sums and Products of Distributions: Rules of Thumb and Applications

77423 Decision-Making Process for a Deepwater Production System Considering Environmental, Technological and Financial Risks

77424 Valuation of Technology and Information for Reservoir Risk Management

### GEOSTATISTICAL MODELING

77425 Modeling of a Deepwater Turbidite Reservoir Conditional to Seismic Data Using Multiple-Point Geostatistics

77426 Feature-Based Geostatistics: An Application to a Submarine Channel Reservoir

77427 Geostatistical Assignment of Reservoir Properties on Unstructured Grids

77428 Reservoir Modeling Methods and Parameters for a Shoreline-Shelf Reservoir: What Is Important for Fluid Flow Performance?

77429 Geostatistical History Matching Under Training-Image Based Geological Model Constraints

77430 Sensitivity Analysis of Petrophysical Properties Spatial Distribution and Flow Performance Forecasts to Geostatistical Parameters Using Derivative Coefficients

77431 Representation of Reservoirs Generated by Object-Based Stochastic Simulation in Numeric Flow Modeling

### SAND CONTROL I

77432 Innovative Sand-Control Screen Assembly Enables Successful Multilobe Frac Pack in Adverse Recompletion Conditions

77433 Openhole Horizontal Gravel Packing: An Evolving Mainstay Deepwater Completion Method

77434 Ceiba Completion Optimization: A Fast-Track Approach to Success

77435 New Technologies Enhance Operational Efficiency in Difficult Gravel-Pack Operations

77436 New Single Trip Perf-and-Pack Completion System Increases Cost Efficiency in Gulf of Mexico Completions

77437 Simultaneous Stimulations and/or Packing in Multiple Zones: Effective Solutions

77438 Advanced Openhole Completions Utilizing a Simplified Zone Isolation System

### FRACTURE DIAGNOSTIC METHODS

77439 Microseismic Images of Hydraulic Fractures: More Questions Than Answers?

77440 Microseismic Imaging of Hydraulic Fracture Complexity in the Barnett Shale

77441 Integrating Fracture Mapping Technologies To Optimize Stimulations in the Barnett Shale

77442 A Practical Guide to Hydraulic Fracture Diagnostic Technologies

77443 Calibrating Coalbed Methane Fracture Geometry in the Helper Utah Field Using Treatment Well Tiltmeters

77444 Running Two BHP Gauges To Determine Fracture Growth and Entry Pressure: A Case Study in Canada, Basal Quartz Formation

### DRILLING FLUIDS

77445 Chemical and Physical Characterization of Aphron-Based Drilling Fluids

77818 Influence of Temperature and Clays/Emulsion Microstructure on Oil-Based Low Shear Rate Rheology

77446 Toward Zero Fluid Loss

77447 Development of Novel Membrane Efficient Water-Based Drilling Fluids Through Fundamental Understanding of Osmotic Membrane Generation in Shales

77448 Drilling Fluid Sweeps: Their Evaluation, Timing, and Applications

77449 Filtercake Cleanup Techniques for Openhole Water Injectors With Sand Control: Lessons From Laboratory Experiments and Recommendations for Field Practices

77450 Effect of Low and High Temperature and Pressure Effects on the Rheology of Oil-Based Drilling Fluids

### WELL TESTING FOR FORMATION CHARACTERIZATION

77451 Integrating Pressure Transient and Seismic Data To Determine the Characteristics of Single- and Double-Porosity Reservoirs

77452 Effect of Scaleup and Aggregation on the Use of Well Tests To Identify Geological Properties

77453 Multiwell Interference Test in the Colville River Field, Alaska

77454 Application of Injection Tests for Reservoir Appraisals: A Conceptual Study

77455 Timing and Distance of Well Interference in Anisotropic Reservoirs

77456 Determining Reservoir Stratigraphic Continuity via Well Testing in Deepwater Gulf of Mexico, Fuji Prospect

### HEAVY OIL AND THERMAL PROCESSES

77457 Mechanisms of Bubble Formation by Pressure Decline in Porous Media: A Critical Review

77459 An Integrated Experimental and Numerical Approach To Assess the Performance of Solvent Injection Into Heavy Oil

77460 Identification of Steam Breakthrough Intervals Using DTS Technology

77461 Wettability Alteration of Diatomite Induced by Hot-Fluid Injection

77462 The Impact of Structure and Heterogeneity on Modeling the SAGD Process

### PERFORMANCE ANALYSIS

77464 Comparing Production Responses From Devonian Shale and Berea Wells Stimulated With Nitrogen Foam and Proppant vs. Nitrogen Only, Pike Co., Kentucky

77465 Analysis of Layered Gas Reservoir Performance Using a Semianalytical Solution for Rate and Pressure Behavior

77466 Inflow Performance Relationships for Gas Condensate Wells

77467 Investigation of the Relationship Between the Dimensionless and Dimensional Analytic Transient Well Performance Solutions in Low-Permeability Gas Reservoirs

77468 Effects of Non-Darcy Flow on Pressure Transient Analysis of Hydraulically Fractured Gas Wells

77469 A Comprehensive Reservoir Evaluation of a Shale Reservoir: The New Albany Shale

75392 The Study of Performance Prediction of Treatment Wells in Low Permeability and Abnormal High-Pressure Gas Reservoirs

### REGULATORY ENVIRONMENTAL WELL CONTROL ISSUES

77470 The Health, Safety, and Environmental Benefits of Real-Time Operations

77471 Impact of Drilling Activities: Seabed Recolonization

77472 Pollut-Eval: An Innovative Tool for Direct Hydrocarbon Characterization in Oil Base Mud & Cuttings

## 77473 Practical and Successful Prevention of Annular Pressure Buildup on the Marlin Project

## 77474 Gas Diffusion: Its Impact on a Horizontal HP/HT Well

## 77475 Interactions Between Drilling Fluid and Reservoir Fluid

## 77476 Estimation of Underground Blowout Magnitude Using Temperature Logs

### LOGGING WHILE DRILLING

## 77477 Field Testing of a New Magnetic Resonance Logging-While-Drilling Tool

## 77478 Standoff Compensation and Hole Size Correction of a New LWD Density/Neutron Logging System

## 77479 An Integrated Caliper From Neutron, Density, and Ultrasonic Azimuthal LWD Data

## 77480 LWD Sonic Logging in Large Diameter Surface Holes

## 77481 Design, Calibration, Characterization, and Field Experience of New High-Temperature Azimuthal, and Spectral Gamma Ray Logging-While-Drilling Tools

## 77482 Case Study: Combining Pulsed Neutron Spectroscopy and LWD Resistivity for Analysis Behind Casing in Small Holes

## 77483 The Design, Response, and Field Test Results of a New Slimhole LWD Multiple- Frequency Resistivity Propagation Tool

### RESERVOIR STUDIES

## 77484 Estimating Non-Darcy Flow Coefficient From Buildup Test Data With Wellbore Storage

## 77485 Identification of Unknown Permeability Trends From History Matching of Production Data

## 77486 Comparison of 2D and 3D Flow Behavior Based on High-Resolution Geophysical Surveys, Outcrop Data, and Flow Simulations: Ferron Sandstone, Utah, USA

## 77487 Quantifying Bypassed Oil in the Vicinity of Discontinuous Shales

## 77488 Hierarchical Organization of Flow Network in Fractured Carbonate Reservoirs: Identification and Characterization of Key Parameters

## 77489 Determination of OHIP and Aquifer Constant Without Prior Knowledge of Aquifer Models

## 77490 A Case Study of Asphaltene Precipitation in High Gas-Oil Ratio Wells

### SEPARATION TECHNOLOGIES

## 77491 New Inclined Separator Design Extends Economic Limit of High Water-Cut Field

## 77492 Design of a Crude Oil Dehydration Unit C.

## 77493 Optimization of a Horizontal Flow Electrostatic Coalescer in Offshore Gulf of Mexico Service

## 77494 Computational Fluid Dynamic (CFD) Simulation of Fluid Motion in Process Vessels on Fixed and Floating Platforms

## 77495 Increasing Separation Capacity With New and Proven Technologies

## 77496 Rheology and Special Requirements on the Flow System and Equipment for Large Scale Injection, Production, and Gathering of Viscous-Elastic Polymer Fluids in Chemical Floods To Solve the Problems That Emerge

## 77497 Crude Oil Emulsions: A State-of-the-Art Review

## 77498 Optisep R&D Makes a Breakthrough in Hydrocyclone Separation

### MULTIPHASE FLOW: MEASUREMENTS AND MODELING

## 77499 A Neural Network Model for Prediction of Liquid Holdup in Two-Phase Horizontal Flow

## 77500 Modeling Reservoir/Tubing/Pump Interaction Identifies Best Candidates for Multiphase Pumping

## 77501 Mechanistic and Simplified Models for Oil-Water Countercurrent Flow in Deviated and Multilateral Wells

## 77502 Application of Transient Multiphase Compositional Tracking for Pipeline Flow Analysis

## 77503 Severe Slugging Attenuation for Deepwater Multiphase Pipeline and Riser Systems

## 77504 Experimental Research on Downward Two-Phase Flow

## 77505 Two-Phase Gas-Condensate Flow in Inclined Pipes

U.S. TAXES, PRODUCTION SHARING CONTRACTS, AND COUNTRY RISKS

## 77506 World Energy Beyond 2050

## 77507 Reverse Tax-Free Exchanges for Oil and Gas Transactions Enter a New Era: New IRS Procedures Add Needed Flexibility

## 77508 Fair Value: What Your Accountant Wants To Know

## 77509 What is a Good Decision?

## 77510 Evaluation of Fiscal Terms, Reporting Reserves, and Financials Under International Agreements

## 77511 Overseas and Above Ground: Managing Country Risk in the Energy Industry

## 77512 Recent Evidences of Exploration Risk Policy in the Oil Industry

### 4D MONITORING AND INTEGRATION

## 77513 Surface Gravity Monitoring of the Gas Cap Water Injection Project—Prudhoe Bay, Alaska

## 77514 Improved Reservoir Modeling With Time-Lapse Seismic in a Gulf of Mexico Gas Condensate Reservoir

## 77518 Fluvial Channel Parameter Estimation Constrained to Static, Production, and 4D Seismic Data

## 77516 An Integrated Reservoir Characterization Study Matching Production Data and 4D Seismic

### HORIZONTAL AND MULTILATERAL COMPLETIONS

## 77519 Improving Production Results in Monobore, Deepwater, and Extended-Reach Wells

## 77520 Planning and Execution of Long Horizontal Gravel Packs in Extended Reach Wells

## 77521 A Case History on the Use of Downhole Sensors in a Field Producing From Long Horizontal/Mulilateral Wells

## 77522 Real-Time Monitoring and Control of Water Influx to a Horizontal Well Using Advanced Completion Equipped With Permanent Sensors

## 77523 Improved Cleanup Practices for Horizontal Well Completions in Unconsolidated Sands: Correlation Models for Filter-Cake Removal

## 77524 World's First Perforated Level 4 Multilateral Completion: A Case History

DIRECTIONAL DRILLING

## 77525 Real-Time 3D Earth Model Updating While Drilling a Horizontal Well

## 77526 3D Azimuthal LWD Caliper

## 77527 How to Efficiently Remove Sand From Deviated Wellbores With a Solids Transport Simulator and a Coiled-Tubing Cleanout Tool

## 77528 A Rational Approach to Multilateral Project Planning

## 77529 Underbalanced Production Steering Delivers Record Productivity

## 77530 Reservoir Characterization During Underbalanced Drilling: Methodology, Accuracy, and Necessary Data

## 77531 Specifically Engineered Gauge Structures To Enhance Directional Performance on Rotary Steerable Tools

APPLICATIONS OF RESERVOIR TESTING

## 77532 Application of Water Injection/Falloff Tests for Reservoir Appraisal: New Analytical Solution Method for Two-Phase Variable Rate Problems

## 77533 Effects on Well Test Analysis of Pressure and Flowrate Noise

## 77534 Effects of Formation Damage and High-Velocity Flow on the Productivity of Perforated Horizontal Wells

## 77535 Productivity Changes in Reservoirs With Stress-Dependent Permeability

## 77536 Waterflood and Production-Induced Stress Changes Dramatically Affect Hydraulic Fracture Behavior in Lost Hills Infill Wells

## 77537 Introduction to a Method To Obtain Formation Pressure by Pressure Buildup Curves and Some Characteristics of Formation Pressure in Multizone Heterogeneous Reservoirs of Daqing Oil Field

## 77538 Study of Gas-Condensate Well Productivity in Venezuelan Santa Barbara Field by Well Test Analysis

### WETTABILITY AND RELATIVE PERMEABILITY

## 77539 A New Three-Phase Relative Permeability Model Based on Immiscible Displacement Theory

## 77540 Relative Permeability From Capillary Pressure

## 77541 An Improved Formulation of the Leverett J-Function

## 77542 Wettability Effect on Oil Relative Permeability During a Gravity Drainage

## 77543 Prediction of Wettability Variation and Its Impact on Waterflooding Using Pore-to-Reservoir-Scale Simulations

## 77544 A General Scaling Method for Spontaneous Imbibition

## 77545 A Unified Theory on Residual Oil Saturation and Irreducible Water Saturation

### CONDENSATE IN THE RESERVOIR

## 77546 Laboratory Measurements of Condensate Blocking and Treatment for Both Low and High Permeability Rocks

## 77547 Wettability Alteration to Intermediate Gas-Wetting for a Real Condensate Fluid at High Temperatures

## 77548 Well Test Investigation of Condensate Drop-Out Behavior in a North Sea Lean Gas Condensate Reservoir

## 77549 Forecasting Liquid Condensate and Water Production From Gas-Condensate Wells

## 77550 Direct Estimation of Gas Reserves Using Production Data

## 77551 Engineering Calculations of Gas Condensate Well Productivity

## 77552 Quantifying Production Impairment Due To Near-Wellbore Condensate Dropout and Non-Darcy Flow Effects in Carbonate and Sandstone Reservoirs With and Without Hydraulic Fractures in the Ghawar Field, Saudi Arabia

### HSE TECHNOLOGY: TOWARD A CLEANER ENVIRONMENT

## 77553 Drill Cuttings Injection: A Review of Major Operations and Technical Issues

## 77554 Case Studies Using Reservoir Characterization To Improve Remediation System Design and Operation

## 77555 An Approach to Offshore Field Abandonment

## 77556 Thermal Desorption as an Alternative to Cutting Reinjection in Niger Delta WasteManagement Operations

## 77557 Extending Foam Technology From Improved Oil Recovery to Environmental Remediation

## 77558 Phase Segration Kinetics During Production Waste Recovery

## 77559 Water Control in Oil Wells With Downhole Oil-Free Water Drainage and Disposal

### WELL LOGGING INTERPRETATION AND NEW TECHNOLOGIES

## 77560 The Development and Testing of a Garaged Openhole Logging System for High-Angle Wells and Bad Hole Conditions

## 77561 High Resolution Downhole Measurements of Porosity and Fluid Saturation While Coring

## 77562 A New Microresistivity Imaging Device for Use in Oil-Based Mud

## 77563 A Fast and Direct Method of Permeability Measurements on Drill Cuttings

### RESERVOIR MANAGEMENT TECHNIQUES

## 77567 An Alternative Method To Calculate Reserves Distribution for Geologically Dependent Layers

## 77564 Developing New Fields Using Probabilistic Reservoir Forecasting.

## 77566 Logistic Approach in Using an Array of Reservoir Simulation and Probabilistic Models in Developing a Giant Oil Reservoir With Superpermeability and Natural Fractures

## 77565 Optimum Location and Trajectory of Nonconventional Wells

## 77568 A Model for Analysis of Injection-Well Thermal Fractures

## 77569 The Analysis and Interpretation of Water-Oil-Ratio Performance

## 77570 Fast Computation of Effective Properties for Two-Phase Flow Problems

### FLOW ASSURANCE

## 77571 Modeling of Wax Deposition in Pipelines From Irreversible Thermodynamics

## 77572 A New Technique To Troubleshoot Gas Hydrate Buildup Problems in Subsea Christmas Trees

## 77573 Wax Deposition in North Sea Gas Condensate and Oil Systems: Comparison Between Operational Experience and Model Prediction

77574 Thermal Behavior During Restart of Ultradeepwater Flowlines

77575 Phase Behavior Modeling of Gas Condensate-Methanol-Water Mixtures by Peng-Robinson and SAFT Equations of State

77576 Challenges in Pigging of Subsea Gas Flowlines

77577 Subsea Heat Bank—An Alternative to Conventional Insulation

77578 Development, Deployment, and Optimization of Combined Scale/Corrosion Production Chemicals Within Subsea Facilities in the North Sea Basin

ENERGY ENGINEERING EDUCATION TRENDS FOR THE NEXT DECADE

77579 A New Degree Program in Oil and Gas Engineering

77580 Energy Education: A Course for the 21st Century

#### REAL OPTIONS FOR THE REAL WORLD

77581 The Valuation in Real Option Analysis: What It Is, What It Is Not, and Why It Is Important

77582 A Practical Approach to Evaluating the Value of Information and Real Option Decisions in the Upstream Petroleum Industry

77587 Real Options Applied to Selection of Technological Alternative for Offshore Oilfield Development

77584 Deepwater Real Options Valuation: Waiting for Technology

77585 Project Valuation: Progressing From Certain Outcomes Through Passive

77586 The Value of Flexibility in Managing Uncertainty in Oil and Gas Investments

#### COMPARTMENTALIZATION AND ARCHITECTURE

77588 The Impact of Turbiditic Reservoir Architecture on Production Mechanism: A Field Case

77589 Identifying Reservoir Compartmentalization and Flow Barriers Using Primary Production Response: A Streamline Approach

77590 The Impact of Faulting on Field Compartmentalization: A Question of Tools and Time for True Dynamic Assessment

77591 Assessment and Modeling of High Permeability Areas in Carbonate Reservoirs

77592 3D Modeling of Stratigraphically Controlled Petrophysical Variability in the South Wasson Clear Fork Reservoir

77593 Capturing and Preserving Sandbody Connectivity for Reservoir Simulation: Insights From Studies in the Dacion Field, Eastern Venezuela

#### FRACTURING MODELING AND METHODOLOGY

77596 Modeling Polymer Cleanup in Hydraulic Fractures

77597 Identification of Successful Practices in Hydraulic Fracturing Using Intelligent Data Mining Tools: Application to the Codell Formation in the DJ Basin

77598 Analysis of Generated and Reflected Pressure Waves During Fracturing Reveals Fracture Behavior

77599 A Multiphase Model for Evaluation of Filtration During Drilling and Fracturing of Wells

77600 Modeling the Effect of Water Blockage and Geomechanics in Waterfracs

77601 Development and Application of Improved Reservoir Characterization Models for Optimizing Screenless Fracturing in the Gas Condensate Jauf Reservoir, Saudi Arabia

77603 A Study of the Friction Pressure and Proppant Transport Behavior of Surfactant-Based Gels

#### ARTIFICIAL INTELLIGENCE II

77604 Barriers to Adoption: A Case History of Robotics and the Oil Field

77605 An Intelligent Identificaton Method of Fuzzy Models and Its Applications to Inversion of NMR Logging Data

77606 Adaptive Fuzzy Clustering for Efficient Segmentation of Wellbore Resistivity Images

77607 Neural Network Analysis for Lithology Identification and Drilling Process Optimization

77608 Applied Production Optimization: i - Field

77609 Development of an Intelligent Distributed Management System for Automated Wells (SGPA)

#### NEW DRILLING TECHNOLOGIES

77611 Expanding the Envelope of Coiled Tubing Collapse Ratings in High-Pressure/High-Temperature Wells

77612 Reaching Deep Reservoir Targets Using Solid Expandable Tubulars

77613 Extending the Frontiers of Solid Expandable Tubular Technology (SET): The Challenges—A Review of Installations in the Niger Delta

77614 Improved Drilling Efficiency Through BHA Oscillation

77615 Appropriate Placement of Drilling Jars in the Drillstring Can Reduce the Incidence of Fatigue Failure

77616 Influence of Bit-Rock Interaction on Stick-Slip Vibrations of PDC Bits

77617 Quantifying Tortuosities by Friction Factors in Torque and Drag Mode

#### MODERN WELL TEST ANALYSIS

77618 Characterization of Low Permeability Gas-Condensate Behavior by Intensive Reservoir Monitoring

77619 Why We Should Stop Using Pseudopressures and Other Good Oil Tools in Well Test Interpretation After So Many Years of Good Service

77620 Use of Downhole Production/Reinjection for Zero-Emission Well Testing: Challenges and Rewards

77621 Numerical Sensitivity Studies for the Joint Inversion of Pressure and DC Resistivity Measurements Acquired With In-Situ Permanent Sensors

77622 Transient Flow Into Undulating Multibranch Wells

77623 New Approach for Interpreting Pressure Transient Test After Massive Acidizing Treatment

77624 An Investigation of Pressure Transient Behavior of Horizontal Wells in Double-Fracture Systems

#### EMERGING DEEPWATER DEVELOPMENT

77625 Recipe for Success in Ultradeep Water

77626 Subsea Well Testing at the Subsea Tree

77627 Comparison of Specific Energy Between Drilling With High Power Lasers and Other Drilling Methods

77628 Well Construction Efficiency Processes Yielding a Step Change Well Architecture

77629 Mudline Tubing Hanger Experience in Auger-Gulf of Mexico Wells

77630 Life-Cycle Analysis and Optimization of Intelligent Well Systems for High Reliability

#### PETROPHYSICS

77631 Real-Time Petrophysical Analysis in Siliciclastics From the Integration of Spectroscopy and Triple-Combo Logging

77633 Improved Quantification of Fit-For-Purpose Saturation Exponents With a Maturing Core Database

77634 The Use of MRI Data for Predicting Well Performance and Aiding Reservoir Description: McAllen Field, Hidalgo Co., Texas

77635 Saturation Height Effects on Macroscopic Resistivity Anisotropy Measurements With Multicomponent Induction Log Data in Laminated Bimodal Sand Reservoir

77637 Quantification of Petrophysical Uncertainty and Its Effect on In-Place Volume Estimates: Numerous Challenges and Some Solutions

77638 Proper Core-Based Petrophysical Analysis Doubles Size of Ha’py Field

77639 Reliability of Laboratory Porosity and Pore Compressibility Obtained on Unconsolidated Deep Offshore and Heavy Oil Reservoirs

#### RESERVOIR MANAGEMENT FIELD CASE HISTORIES

77641 Maximizing Yibal's Remaining Value F.C. Mijnssen, Petroleum Development of Oman

77640 Friendswood Field: A Case Study in Reservoir Management

77642 Pore Pressure Control of Fracture Reactivation in the Ghawar Field, Saudi Arabia

77643 Prudhoe Bay E-Field Production Optimization System Based on Integrated Reservoir and Facility Simulation

77644 Schrader Bluff Development Strategy Unlocks the Next Phase of Viscous Oil Development of the North Slope of Alaska

77645 Management of a Secondary Gas Cap for Effective Depletion of the Oil Below It: A Case Study

77646 Lost Hills Field Trial—Incorporating New Technology for Reservoir Management

### MULTIPHASE FLOW OPERATIONS

77647 Multiphase Flow: Can We Take Advantage of Hydrodynamic Conditions To Avoid Hydrate Plugging During Deepwater Restart Operations?

77648 Feedback Control of the Tor-EkoJ Pipeline in the North Sea

77649 Wellbore Heating To Prevent Liquid Loading

77650 Active Feedback Control of Unstable Wells at the Brage Field

77651 Mass Transfer of Methane Into Oil for the Transportation of Gas and Oil Through a Single-Phase Pipeline

77652 Optimization of Ramp-Up Operations in a Dual Large Diameter Long-Distance Subsea Wet Gas Pipeline System

77653 Effect of Drag-Reducing Polymer on the Flow Pattern of Gas/Liquid Flow in Horizontal Pipes

### PRODUCTION OPTIMIZATION

77655 Downhole Fiber-Optic Multiphase Flowmeter: Design, Operating Principle, and Testing

77654 Downhole Fiber-Optic Multiphase Flowmeter: Field Installation

77656 ESPs and Intelligent Completions

77657 BP Machar: A Case Study for Implementation of Intelligent Well Completion Into an Existing Field Infrastructure

77658 Production Control Optimization Techniques for Petroleum Fields

77659 Prudhoe Bay Oil Production Optimization: Using Virtual Intelligence Techniques, Stage One: Neural Model Building

77660 Remotely Controlled In-Situ Gas Lift on the Norne Subsea

### SOLVING THE PORTFOLIO PUZZLE

76667 Managing Change and Uncertainty at the Field Level

77662 Modern Techniques in Petroleum Risk Management: A Discussion of Performance Effects on E&P Firms

77663 The Potential for State-of-the-Art Decision and Risk Analysis To Contribute to Strategies for Portfolio Management

77664 Application of Portfolio Analysis and Optimization: The Case of Mutually Exclusive Alternatives

77665 Project Portfolio Management: A Low-Cost, High-Return Business Solution

77666 Managing Exploration Performance

### INTEGRATED CHARACTERIZATION AND MANAGEMENT

77668 A Case Study: Field Development Plan for a Highly Overpressured Gas Reservoir in China by a Multidiscipline Consulting Team

77669 Reservoir Management Scope in a Mature Niger Delta Field

77670 Exploitation Evolution of Marimba Field, Campos Basin, Brazil

77671 A Case Study: Using Modern Reservoir Characterization To Optimize Future Development of a Mature Asset

77672 Integration of Horizontal Wells in Reservoir Models: Input From an Outcrop Study

77673 Integrated Reservoir Characterization and Simulation for Reservoir Management Using a Web-Based Collaborative Technical Workflow Manager

77674 An Integrated Approach To Optimizing a Large Asset II—Dynamic Modeling

### FRACTURING CASE HISTORIES

77675 Proving It—A Review of 50 Published Field Studies Demonstrating the Importance of Fracture Conductivity

77676 Real-Time Downhole-Mixed Stimulation Fracturing Process

77677 Hydraulic Fracturing Case Histories in the Carbonate and Sandstone Reservoirs of Khuff and Pre-Khuff Formations

77678 The First Successful Propped Fracture Treatment Campaign Conducted in Japan: Stimulation Challenges in a Deep, Naturally Fractured Volcanic Rock

77679 Coiled-Tubing Fracturing Increases Deliverability, Recoverable Reserves, and NPV of Infill Development Wells in a Mature Shallow Gas Field

77680 Large-Scale Hydraulic Fracturing in a Frontier Area in China

77681 Exceptional Proppant Flowback Control for the Most Extreme Well Environments: The Shape of Things To Come

### SAND CONTROL II

77682 Fiber-Optic Monitoring in Openhole Gravel Pack Completions

77202 Implementation of Intelligent Well Completions Within a Sand Control Environment

77683 What is the Magic of Water in Producing Sand?

77684 Startup of Screenless Sand Control Through Coiled-Tubing Fracturing in a Shallow, Unconsolidated, Steamflooded Reservoir

77685 An Improved Placement Technique for Resin-Coated Gravel in Through-Tubing Gravel Packing

77686 Sand Control: Sand Characterization, Failure Mechanisms, and Completion Methods

77687 Case History: Internally Coated Completion Workstring Successes

LONG-TERM TESTING, PERMANENT MONITORING, AND PRODUCTION DATA ANALYSIS

77688 Analysis of Well Test Data From Permanent Downhole Gauges by Deconvolution

77689 Pressure Transient and Decline Curve Behaviors in Naturally Fractured Vuggy Carbonate Reservoirs

77690 An Account of Decline-Type-Curve Analysis of Vertical, Fractured, and Horizontal Well Production Data

77691 Effective Well and Reservoir Evaluation Without the Need for Well Pressure History.

77692 Harmonic Testing for Continuous Well and Reservoir Monitoring

#### ENHANCED OIL RECOVERY

77693 Experiences Learned After Producing More Than 300 Million Barrels of Oil by Polymer Flooding in Daqing Oil Field

77694 Studies of Applications and Mechanisms of Clay Gum System

77695 FAWAG: A Breakthrough for EOR in the North Sea

77696 Quantification of Displacement Mechanisms in Multicomponent Gasfloods

77697 Effect of Composition on Waterblocking for Multicomponent Gasfloods

77698 A Model for Foam Generation in Homogeneous Media

77699 Simulating Foam Process for a Venezuelan Pilot Test: High and Low Foam Quality Approach Based on Experimental Data Obtained at Reservoir Conditions

#### OUT OF THE BOX RESERVOIR ENGINEERING

77700 Capillary Shockwave Front Blind Imaging for Reservoir Limits: A Case Study

77701 Gas/Condensate and Volatile Oil Well Testing From the Surface

77702 Managing Turbulent Technology for Exploration and Production Success

77703 A Critical Overview of Artificial Neural Network Applications: Stretching the Technology Toward the Permanent Optimization of the Oil Field

77704 Artificial Neural Network Architectures for Predicting Two-Phase and Three-Phase Relative Permeability Characteristics

#### ADVANCES IN WELL COMPLETION TECHNOLOGY

77712 Riserless Subsea Completion With Disappearing Plug Technology

77707 State-of-the-Art Hydrocarbon-Based Completion Fluids

77708 Non-Newtonian Fluid Flow in Coiled Tubing: Theoretical Analysis and Experimental Verification

77709 Accurate Full-Bore Acoustic Densometers for Use With Proppant-Laden Stimulation Fluids at High Pressures

77710 Installation of In-Well Fiber-Optic Monitoring Systems

77711 Reeled Completions in Corrosion Resistant Alloys: A Field Development and Remediation Tool for the Future

#### ELECTRICAL METHODS

77713 A Method for Computing Fast and Accurate Analytical Gradient: The Key for Routinely Performing Efficient 2D and 3D Resistivity Inversions

77714 Resistivity Modeling of Array Laterolog Tools: An Application in an Offshore Norway Clastic Reservoir

77715 On the Relationship Between Resistivity and Permeability Anisotropy

77716 Fast Induction Log Inversion Using Quasi-Newton Updates

77717 Maximizing Production for Horizontal Wells in Hassi R’mel Field (Algeria) With Resistivity Interpretation and Modeling

77718 An Analytic Method for Producing Multiarray Induction Logs That Are Free of Dip Effect

77719 Resistivity in Carbonates: New Insights

#### NUMERICAL SIMULATION

77720 Application of IMPSAT and IMPSAT-Based AIM Models in Compositional Simulation

77721 Distributed Decomposition: A Strategy To Solve Large Scale Simulation Problems

77722 Simulation of Gas/Oil Gravity Drainage in a Stack of Interacting Blocks: Pseudorelations for a Limited Number of Gridblocks

77723 Coupled Geomechanics and Reservoir Simulation

77724 A Novel Approach for Incorporating Physical Dispersion in Miscible Displacement

77725 Optimization of Gas Field Development: A Comparison Between Hydraulic Fracturing and Horizontal Well Performance in the Pre-Khuff Sandstone Reservoir, Ghawar Field, Saudi Arabia

77726 Pore-Scale Modeling of Three-Phase Flow in Mixed-Wet Systems

#### ARTIFICIAL LIFT

77727 A Novel Approach to Gas Lift Design for 40,000 bpd Subsea Producers

77728 Reducing Well Test Deferments From Clusters of Gas-Lifted Subsea Wells

77729 Field Scale Research on Gas Chamber Pumps

77730 Experimental Study of Two-Phase Pumping in a Progressive Cavity Pump Metal to Metal

77731 Hybrid Lift Technology: A Design Technique of Combining Electrical Submersible Pump With Liquid-Jet Gas Pump

77732 Stability Analysis of Continuous-Flow Gas-Lift Wells

77733 Custom Wellbore/High Horsepower ESP System Combine To Increase East Indian Basin Gas Production

#### FORECASTING AND STRATEGIC PORTFOLIO MANAGEMENT

77734 Implementing Successful Mergers in the Oil and Gas Industry

77735 Toto, We're Not in West Texas Anymore: A Challenging Examination of the Historical Global Crude Oil Production Capacity, Demand, Price, and the Changing Elasticies

77736 Energy Sources and Energy Intensity for the 21st Century

77737 A Real-Options Model for Portfolio Selection of Oil and Gas Assets

#### CHARACTERIZING FRACTURED RESERVOIRS

77738 Fracture Corridors: How to Reconcile Geological Concepts and Their Equivalent Dynamic Parameters With the Associated Uncertainty

77739 Simulation of Lithologicaly Complex and Fracture-Dominated Monterey Production From the South Ellwood Reservoir

77740 A Fractured Reservoir Modeling Workflow: Application to the Tempa Rossa Field, Offshore Italy

77741 Construction of Fracture Network Model Using Static and Dynamic Data

77742 An Effective Technique of Estimating Drainage Shape, Magnitude, and Orientation in a Low-Permeability Gas Sand

77743 Successful Integration of Sparsely Distributed Core and Welltest Derived Permeability Data in a Viable Model of a Giant Carbonate Reservoir

FRACTURING FLUIDS AND PROPPANTS: NEW TECHNOLOGY AND HISTORICAL PERFORMANCE

77744 Encapsulated Breaker Release Rate at Hydrostatic Pressure and Elevated Temperatures

77745 New Resin Coating Technology Improves Proppant Flowback Control in HP/HT Environments

77746 Maximizing Well Production With Unique Low Molecular Weight Frac Fluid

77747 A Case Study of Long-Term Production Enhancement Derived From Usage of Organo-Borate Crosslinked Fracturing Fluids

77748 A Novel Approach for Enhancing Proppant Consolidation

77749 Large Scale Study of Near-Wellbore Proppant Transport for Fracturing Fluids Subjected to Different Shear Rates

77750 Monitoring Fracturing Fluid Flowback With Chemical Tracers: A Field Case Study

#### CEMENTING

77751 Settable Spotting Fluid Used To Improve Expandable Casing Process Deployment in High Angle Applications: Case Histories

77752 Cement Pulsation Treatment in Gas Wells

77753 Subsea Remedial Cementation of Conductors on Template-Drilled Development Wells

77754 Transient Pressure Unloading—A Model of Hydrostatic Pressure Loss in Wells After Cement Placement

77755 Mechanical Response and Mix Design of Well Cements

77756 The Effect of Cement Heat of Hydration on the Maximum Annular Temperature of Oil and Gas Wells

77757 Value Created Through Versatile Additive Technology and Innovation for Zonal Isolation in Deepwater Environmen

# Text boxes

| 出 國 人: | 服務機關： | 中國石油公司探採研究所 |
| --- | --- | --- |
|  | 職 稱： | 石油開採工程師 |
|  | 姓 名： | 陳大麟 |
| 出國地區： | 美 國 |
| 出國期間： | 91年9月28日- 91年10月4日 |
| 報告日期： | 92年1月2日 |

參加裂縫油氣層評估技術研討會

行政院及所屬各機關出國報告

（出國類別：開會）