行政院及所屬各機關出國報告

（出國類別：訓練）

民航局飛航測試機飛行組員年度複訓報告書

服務機關：交通部民用航空局

出 國 人職稱：副組長、簡任技正、

專門委員、技士

姓名：張金田、周芷翔、

張羚悌、林柔君

出國地區：美國  達拉斯市

出國期間：中華民國九十二年八月二十三日~九月一日

報告日期：中華民國九十二年 十月二十一日

目錄

頁次

壹、 目的	2

貳、 過程	2

參、 心得	5-25

肆、 建議事項	26

伍、 相關附件	27

附件一	附件一1-5

附件二	附件二 2-1~3

附件三	附件三 3-1~2

附件四	附件四4-1~10

附件五	附件五-1

附件六	附件六 6-1~2

附件七	附件七 7-1~13

附件八	附件八 8-1~23

壹、目的

本次本局飛航測試機組員模擬機年度複訓係屬行政院核定九十二年度派員出國計劃（含進修、研究、實習）及財團法人中華民國台灣飛行安全基金會九十二年度支援本局經費計畫項目。旨在擷取同機型航機最新訊息以及提昇本局飛測組員飛行程序及技巧等素質；並整合經驗心得配合飛測助航設施任務的執行，提供台北飛航服務區最佳的飛測服務。

貳、過程

本次「本局飛測機飛航組員年度複訓」課程，由美國達拉斯市CAE SimuFlite飛行訓練中心提供課程之規劃、安排。課程時間為92.08.25.~92.08.29.，包括兩天共12小時之地面學科訓練以及三天共10小時之模擬機訓練；受訓地點位於美國達拉斯市Dallas Fort Worth 機場內之訓練中心。來自美國境內航空公司及其他國家之同機型飛行員共有8名學員參與本次課程。於地面課程階段一起訓練，於模擬機飛行訓練時則採每組二人分組進行，此為實際且有效的達到飛行訓練的目的。

此次訓練可分為操作程序（Operating Procedures）、限制（Limitations）、系統（System）、飛行計劃（Flight Planning）、緊急狀況（Emergency Information）及一般程序（Normal Procedures），這些課程以地面學科及模擬機訓練兩方面進行，其中地面學科訓練為飛機各項系統之介紹，包括航電（Avionics）、電氣系統（Electrical System）、火警防護（Fire Protection）、飛行操作（Flight Control）、油路系統（Fuel System）、起落架/煞車/方向系統（Landing Gear/Brakes/Steering）、防冰雨系統（Ice and Rain protection）、氧氣系統（Oxygen）、（Pneumatics）、環控系統（Environmental System）、發動機（Powerplant）。

模擬機操作訓練則分為下列細項：

Ground Operation（地面操作）、Takeoffs（起飛）、Inflight Maneuvers（飛行操作）、Instrument Procedures（儀器操作程序）、Missed Approaches（誤失進場）、Landings（落地）、CRM（座艙協調）、Abnormal/Emergency（不正常/緊急操作程序）、Precision Approaches（精確性進場）、Approach Training（進場程序訓練）等項目。

課程內容及訓練行程紀要綜整如下表：

參加「BE-350型機模擬機訓練」行程紀要表

| DATE | SCHEDULE |
| --- | --- |
| 92.08.23. 92.08.24 | TPE （TPE-＞LAX-＞DALLAS） TEXAS |
| 92.08.25. 92.08.26. | Ground School (地面學科) |
| Day 1 Time 0830 1130 1230 1530 Day 2 0830 1130 | SUBJECT INSTRUCTOR Ground School Tom Chaurero Ground School Tom Chaurero Ground School Tom Chaurero Lunch Ground School Tom Chaurero Ground School Tom Chaurero Ground School Tom Chaurero Ground School Tom Chaurero |
| 1230 1530 Day 3 0700 1900 Day 4 0700 1900 DAY 5 0700 1900 | Lunch Ground School Tom Chaurero Briefing SIM Instructor Simulator Flight Briefing SIM Instructor Simulator Flight Briefing SIM Instructor Simulator Flight |
| 92.08.30. 92.09.01. | DALLAS- LAX- TPE |

參、心得

本次課程規劃分為地面及模擬機操作兩方面進行：

- GROUND SCHOOL（地面學科）

為期兩天的地面學科課程合計上課12小時，將本機型之系統部分作以下之介紹：

最大起飛重量（Max Take-off Weight）：…………..15,000lbs

最大落地重量（Max Landing Weight）：…………..15,000lbs

最大零燃油重量（Max Zero Fuel Weight）………..12500lbs

此型機之外觀詳如附件一。

  - 引擎（Power Plant）：KingAir BE-350型機包含兩顆Pratt & Whitney Canada Corp. 生產之PT6A-60A、Two –stage Axial-flow Reaction Turboprop引擎、附有可全反桨四葉定速螺旋槳葉、，引擎系統包括潤滑（lubrication）、（fuel & fuel control）、（ignition）、（engine air），詳如附件二。

  - 油路系統（Fuel system）：油路系統包括儲油（fuel storage）、排氣（venting）、指示（indicating）and 分佈（distribution）。分為左、右及主、附油槽，整架飛機之儲油及油量之分佈如下圖：

| Tank | Gallons | Pounds | Liters | Kilograms |
| --- | --- | --- | --- | --- |
| Left Main | 190 | 1273 | 719 | 577 |
| Left Aux | 79.5 | 533 | 301 | 242 |
| Right Main | 190 | 1273 | 719 | 577 |
| Right Aux | 79.5 | 533 | 301 | 242 |
| Total usable | 593 | 3611 | 2040 | 1638 |

本型機可使用Jet-A, Jet A-1, Jet B等航空用油，一般多以磅來統稱其油量，滿載油量如上表所示3,611磅，其油路之分佈及走向詳如附件三。

  - 電氣系統：包括直流電系、交流電系、電池、發電機及外電源，電氣系統圖詳如附件四。

    - 此型機之主要電氣系統為28伏直流電。

    - 另有從直流電分歧出的交流電系提供115及26伏交流電。

    - 其他尚有一34安培小時之氣冷式鎳鎘電池（34-ampere-hour, air-cooled nickel-cadmium battery），此電池主要是用來啟動引擎及當作備分電力來源。

    - 一旦引擎啟動後，發電機之功能主要是提供直流電予航機，發電機指示器（Generator control panel）監視著輸出電伏且在不同的操作狀況下保持恆定28.25輸出電伏。下表為本型機之直流電及交流電之供電系統：

DC Electrical System

| Power Source | Battery Starter/Generators(2) 300A External power unit |
| --- | --- |
| Distribution | Hot Battery Bus Battery Relay Main Battery Bus Generator buses (left and right) Dual-fed bus Center bus Triple-fed bus Triple-fed Avionics bus L and R GEN Avionics bus |
| Control | Switches BATT IGNITION AND ENGINE START (L/R) Three-position GEN Bus Tie |
| Monitor | Generator loadmeter DC volt and BATTERY ammeter Switches Annunciators |
| Protection | Generator Control Panel Bus Tie Current sensor Line contactor relay Current limiters and diodes Fuses or circuit breakers |

AC Electrical System

| Power Source | Inverters |
| --- | --- |
| Distribution | Generator and center buses L and R GEN AC buses Avionics bus 26v AC bus 115V AC avionics |
| Control | INVERTER switches |
| Monitor | #1 and #2 AC BUS annunciator |
| Protection | AC Power Monitor Circuit Card DC Circuit Breaker Inverter output : fuses and circuit breakers. |

  - 氧氣系統（OXYGEN SYSTEM）：氧氣系統提供航機於最高至35000呎時能供給飛行組員及乘客足夠的氧氣因此當每次飛行前檢查氧氣是否有足夠的氧氣壓力是必要的程序。當客艙壓力高度超過12,500呎，客艙氧氣系統的開關閥（shutoff valve）會自動打開，致使氧氣經由供給線路至客艙氧氣面罩，此時客艙氧氣面罩會自動掉下來提供使用。

  - 起落架（Landing Gear）：鼻輪及主輪是利用液壓的方式來收放，當發生緊急狀況，例如液壓壓力太低以致於無法收放起落架，則須採用手動的方式將起落架伸放以便落地，分析圖詳如附件五。

  - 防火系統（Fire Protection System）：防火系統包括引擎防火偵測（engine fire detection）、引擎滅火（engine fire extinguishing）、測試（testing-fire detection and extinguishing）、（bleed air warning）。

引擎防火偵測（engine fire detection）：此項是經由溫度偵測，經由一個密封的不銹鋼管線，此管線連接一個警示開關用來偵測及測試用，提供座艙火警警示。

引擎滅火（engine fire extinguishing）：引擎滅火系統包括一個滅火器，以及一個連接至引擎的管線，當引擎防火偵測到火警，觸押此裝置將會關斷引擎防火牆，進而啟動滅火瓶來滅火，分析圖詳如附件六。

Fire Protection System

| Power Source | Dual-fed Bus（fire extinguisher） Triple-fed bus (fire detection) |
| --- | --- |
| Distribution | Extinguisher bottle to corresponding engine (no crossfiring) Portable hand fire extinguishers |
| Control | Left and right F/W VALVE USH CLOSED Switches Left and right DISCHARGED switches Left and right TEST switches |
| Monitor | Annunciators ENG FIRE EXTINGUISHER-PUSH DISCHARGED MASTER WARNING flashers Circuit card assembly fire extinguisher |
| Protection | Circuit breakers |

（七）螺旋槳系統（Propeller System）

每一個引擎附有一個四葉螺旋槳（conventional four-blade,full-feathering, constant-speed, counter-weighted, reversing, variable-pitch propeller and mounted on the output shaft of the reduction gearbox. ），此螺旋槳隻角度及速度由引擎油壓力控制，藉由桨葉角度的調整達到不同的飛行狀況。

（八）座艙加壓系統：客艙加壓系統包括兩部分：1. 進氣加壓系統（the pressurization air inflow system） 2. 座艙壓力控制系統（the cabin pressure control system）。加壓系統提供正常座艙壓差為6.5+_1psi（normal working pressure differential of 6.5+_1psi）；也就是當飛機航行高度為20,000呎時，座艙壓力高度大約為2,800呎；當飛機航行高度為31,000呎時，座艙壓力高度為8,600呎；當飛機航行於35,000呎時，座艙壓力高度為10,380呎，此高度35,000呎也是本型機最高巡航高度

- 模擬機操作飛行

模擬機飛行操作演練，在於將平時實機飛行時所無法演練到的不正常程序多加熟悉演練，模擬機操作飛行可分為兩大部分，1. 正常情況操作程序 2. 緊急狀況操作程序，於此先將本機型之正常操作速度表列如下：

| Max Demonstrated crosswind component | 20 kts |
| --- | --- |
| Two-Engine Best-Angle-of-Climb （Vx） | 125 kts |
| Two-Engine Best-Rate-of-Climb （Vy） | 140 kts |
| Cruise Climb： |  |
| Sea Level to 10,000 feet | 170 kts |
| 10,000 to 15,000 feet | 160 kts |
| 15,000 to 20,000 feet | 150 kts |
| 20,000 to 25,000 feet | 140 kts |
| 25,000 to 30,000 feet | 130 kts |
| 30,000 to 35,000 feet | 120 kts |
| Maneuvering Speed （Va） | 184 kts |
| Turbulent Air Penetration | 170 kts |
| Max Airspeed for Effective Windshield Ati-icing | 226 kts |
| Intentional One-Engine-Inoperative Speed（Vsse） | 110 kts |
| Air Min Control Speed（Vmca） |  |
| Flap Up | 94 kts |
| Flaps Approach | 93 kts |

（一）下列各表為飛行前-發動引擎-滑行-起飛-爬升-巡航-下降及落地各階段之正常程序檢查表：

PNF：PILOT NON FLIGHT

PF ：PILOT FLIGHT

1. 開車前檢查 (Before Starting Engines Checklist)

| BEFORE STARTING ENGINES |
| --- |
| PNF | PF |
| Exterior Condition | Checked |
| Instruments Emergency Light | On |
| Airstair Door | Locked |
| Emergency Exits | Unlocked |
| Cabin Loading | Secure |
| Passenger Briefing | Complete |
| Seats, Seat Belts/Shoulder Harnesses | Secure |
| TOLD Cards | Complete |
| Parking Brake | Set |
| Control Locks | Removed |
| Oxygen System Preflight | Complete |
| Oxygen Control | Pull on |
| Fuel Panel | Check |
| Pilots Instrument Panel | Check |
| Pilot’s Subpanel Switches | Set L/R |
| Power Quadrant | Set |
| Pedestal Switches | Set |
| Copilot’s Subpanel Switches | Set L/R |
| Copilot’s Instrument Panel | Check |
| Alternate Static Source | Normal |
| Right Circuit Breaker Panel | Check |
| Battery | On |
| Voltmeters | Check-23 DCMin |
| Cockpit Lights | As Desired |
| MIC Switches | Normal |
| Cabin Lights | Off |
| Furnishing Switch | Off |
| FSB Sign | On |
| Annunciators | Test |
| Fuel Quantity | Check |

2. 開車檢查(Engine Starting Checklist)

| ENGINE STARTING |
| --- |
| GEN TIES （Nighttime） | MAN CLOSE |
| Voltmeter | EXT PWR-28VDC |
| Voltmeter | CTR-20V DC min |
| External Power Switch | On |
| Voltmeter | CTR-28 DC Min |
| EXT PWR Annunciator | On, Steady |
| Propeller Area | CLEAR |
| Left Engine | START |
| External Power Switch | Off |
| GPU | Disconnect/Removed/Light off |
| Left Generator | Reset/On |
| Voltmeter | R GEN-28V DC |
| Right Generator | Reset/On |
| Left Generator | Rest/On |
| Propeller Levers | Full Forward |
| Propeller RPM | 1050（MIN） |
| PROP PITCH Annunciators | Illuminated |

3. 滑行前檢查(Before Taxi Checklist)

| BEFORE TAXI |
| --- |
| Electrical System | Check |
| Bus Selector Switch | TPL FED |
| Master Panel/Cockpit Lights | As Desired |
| Environmental Systems | Set |
| Inverters | On/Check |
| Avionics Master Switch | On |
| Standby Gyro | Set |
| EFIS Power Switchs | On |
| Flaps | UP |
| Exterior Lights | As Required |
| Fight and Engine Instrument | Check |
| Cabin Lights | As Desired |
| Furnishing Switch | As Desired |
| Annunciators | Test/Normal |
| Flight Controls | FREE/CORRECT |
| Flight Instruments | No Flags |
| Brakes | Release/Test |

4.滑行檢查 (TAXI Checklist)

| TAXI |
| --- |
| PNF | PF |
| Autopilot | Check |
| Electric Trim | On |
| Trim Tabs | Set |
| Fuel Quantity | Check |
| Manual Prop Feathering | Check |
| Autofeather Switch | ARM |
| Prop Sync | On |
| Friction Locks | Set |
| Flaps | As Required |
| Vacuum and Pneumatic Gages | Normal |
| Pressurization | Set |
| Avionics/Radar/ | Set |

5. 起飛前檢查(BEFORE TAKEOFF （RUN-UP）)

| BEFORE TAKEOFF (RUN-UP) |
| --- |
| Nosewheel | Centered |
| Parking Brake | Set |
| Autopilot/Yaw Damp | Check |
| Electric Trim | Check/On |
| Trim Tabs | Set |
| Ice Protection | Check |
| Overspeed Gov/Rudder Boost | Check |
| Low Pitch Stops/Primary Governors | Check |
| Autofeather | Check |
| Pressurization | Check |
| Pressurization Controller | Set |
| Bleed Air Valves | Test |
| Pneumatics and Vacuum Gauges | Normal |
| Manual Prop Feathering | Check |
| Autofeather Switch | Arm |
| Prop Sync | On |
| Flaps | As Required |
| Friction Locks | Set |
| Fuel Quantity | Check |
| Flight Instruments | Set |
| Avionics/Radar | Set/Programmed |
| ADC | Test |
| EFIS | Test |

6.起飛前檢查（最後項目）

| BEFORE TAKEOFF (FINAL ITEMS) |
| --- |
| PNF | PF |
| Bleed Air Valves | Open |
| Environmental Bleed Air | As Required |
| Electric Heat | Off |
| Aft Heat | As Required |
| Aft Blower | As Desired |
| Generator Loads | Check |
| Battery Ammeter | Check |
| Exterior Lights | Set |
| Ice Protection | As Required |
| Auto Ignition | Arm |
| Autofeather | Check/Arm |
| Annunciators | Considered |
| Headings/Flight Directors | Set |
| Prop Levers | Full Forward |
| Crew Briefing | Complete |
| Transponder | On |
| Brakes | Released |
| Engine Anti-Ice | Off |

7. 起飛（TAKEOFF）

| TAKEOFF |
| --- |
| Brakes | Hold |
| Power Levers | Set Static Power |
| Brakes | Release |
| Vr | Pitch 10 degrees |
| Landing Gear | Up |
| Landing/Taxi Lights | Off |
| Yaw Damp | On |
| Airspeed | V35 |
| Flaps | Up (125 kt MIN) |

8.爬昇（CLIMB CHECKLIST）

| CLIMB |
| --- |
| Yaw Damp | Verify/On |
| Attitude | Compare |
| Climb Power | Set |
| Props | Set (1600, or as desired) |
| Engine Instruments | Check |
| Ice Protection | As Required |
| Bleed Air Valves | Open |
| Environmental Bleed Air | As Required |
| Pressurization | Climb/Differential |
| Outside check | Confirm |
| Exterior Lights | As Required |
| 10,000 FEET |
| Windshield Heat | As Required |
| Cabin Sign | As Required |
| Exterior Lights | As Required |
| Pressurization | Normal |
| Oxygen Control | Check |
| TRANSITION (18,000) |
| Altimeters | 29.92 |
| Pressurization | Normal |

9.巡航（CRUISE）

| CRUISE |
| --- |
| Cruise Power | Set |
| Autofeather | Off |
| Systems Check | Complete |
| Aft Blower | As Required |
| COMM/NAV Radios | Set |
| Destination Weather | Check |
| Approach Procedure | Consider |
| Crew Briefing | Consider |
| Landing Data | Check |

10.下降/轉換空層（DESCENT/TRANSITION）

| DESCENT/TRANSITION |
| --- |
| Pressurization | Set |
| Fuel Balance | Check |
| Autofeather | ARM |
| Ice Protection | As Required |
| Window Defog | As Required |
| Windshield Defrost | As Required |
| Destination Weather | Recheck |
| Approach Procedures | Recheck/Brief |
| Cabin Sign | Consider |
| Exterior Lights | As Required |
| Altimeters | Set |

11.進場（APPROACH）

| APPROACH |
| --- |
| PNF | PF |
| Surface Deice | As Required |
| Autofeather | Check/Arm |
| Fuel Balance | Check |
| Pressurization | Check |
| Environmental Bleed Air | Low |
| Cabin Sign | On |
| Exterior Lights | As Required |
| Landing Data | Review |
| Approach Briefing | Complete |
| Altitude Alerter/Radar Altimeters | Set |
| Flaps | Approach |

12.落地前檢查（BEFORE LANDING CHECKLIST）

| BEFORE LANDING |
| --- |
| Landing Gear | Down (3 Greens) |
| Prop Controls | Full Forward |
| Approach Speeds | Confirm |
| Exterior Lights | As Required |
| Radar | STBY/As Required |
| Surface Deice | As Required |
| Engine Anti-Ice | Consider |

13.正常落地（NORMAL LANDING）

| NORMAL LANDING（FINAL ITEMS） |
| --- |
| Clanding Gear | Confirm (3 Greens) |
| Pressurization Differential | Check Zero |
| Flaps | Down |
| Yaw Damp | Off |

14.落地後檢查（AFTER LANDING CHECKLIST）

| AFTER LANDING |
| --- |
| PNF | PF |
| Engine Anti-Ice | Confirm/On |
| Auto Ignition | Off |
| Exterior Lights | As Required |
| Ice Protection | Off |
| Brake Deice | Cycle |
| Flaps | Up |
| Trim | Set |
| Transponder | STBY/OFF |
| Radar | STBY/OFF |
| Bleed Air Valves | Envir Off |
| Pressurization Differential | Verify Zero |
| Electric Heat | Off |

15.引擎關車（SHUTDOWN/SECURING）

| SHUTDOWN/SECURING |
| --- |
| Parking Brake | Set |
| Exterior Lights | As Required |
| EFIS Power Switches | Off |
| Oxygen Control Handles | Off |
| Instrument Emergency Lights (Nighttime) | On |
| Battery | Charged |
| Standby Gyro | Caged |
| Avionics master | Off |
| Inverters | Off |
| Aft Heat | Off |
| Vent Blowers | Auto/Off |
| Cabin Temp Mode | Off |
| ITT | Stabilized |
| Power Levers | Flight Idle |
| Condition Levers | Fuel Cutoff |
| Prop Levers | Feather |
| Pilot’s Subpanel Switches | L/R Off |
| Gang Bar | Off (<15% N1) |
| Overhead panel Light Switches | Off |
| Parking Brake | As Required |
| Instrument Emergency Lights | Off |
| Baggage Compartment Lights | Off |
| Cabin entry Lights | Off |
| Tie Downs/Chocks | Install |
| Restraints/Covers | Install |

二、模擬機飛行操作訓練

一趟正常且安全的飛航需遵循發布之操作程序，配合駕駛員的飛行技巧，而駕駛員的飛行技巧訓練則需仰賴定時之複訓，當發生緊急狀況時亦須遵循緊急操作手冊程序，飛行時之正常及緊急操作訓練科目如下：

（一）、正常狀況下之熟練科目（請參考附件7-1~13）

1.正常起飛（Normal Takeoff）-附件7-1

2. 放棄起飛（Rejected Takeoff）-附件7-2

3. 小轉彎（Steep Turns）-附件7-3

4. 失速練習（Approach to Stall）-附件7-4

5. 雙引擎儀器精確性進場落地（Two Engine ILS Approach

and Landing）-附件7-5

6. 雙引擎非精確性進場落地（Two Engine Non-Precision

Approach and Landing）-附件7-6

7. 誤失進場（Go-Around/Missed Approach）-附件7-7

8. 環繞進場（Circling Approach）-附件7-8

9. 目視進場（Visual Approach）-附件7-9

10.引擎故障（Engine Failure After V1-Takeoff Continue）-

附件7-10

11.單引擎精確性進場落地（Single Engine ILS Approach and

Landing）-附件7-11

12.單引擎非精確性進場落地（Single Engine Non-Precision

Approach and Landing）-附件7-12

13.不使用襟翼進場落地（Zero Flap Approach and Landing）-附件7-13

（二）、緊急操作程序（Emergency Procedures）

1. 緊急狀況速度限制（Emergency Airspeeds-10,000LBS）

| EMERGENCY AIRSPEEDS （25,000 LBS(6,804KG）) |
| --- |
| One-Engine-Inoperative Best-Angle-of-Climb（Vxse） | 125Kts |
| One-engine-Inoperative Best-Rate-of-Climb | 125Kts |
| One-Engine-Inoperative Enroute Climb | 125Kts |
| Air Min Control Speeds（Vmca） |  |
| Flaps Up | 94Kts |
| Flaps Approach | 93Kts |
| Emergency Descent | 184Kts |
| Max Range Glide | 135Kts |

2. 當航機發生緊急狀況時，亦應按照所發布的程序實施緊急程序處理，於此先緊急狀況處理有下列幾項（程序詳如附件8-1 ~8-23）：

- 引擎起火或飛行中故障（Engine Fire or failure In Flight 8-1）

- 引擎在地面起火（Engine Fire on Ground 8-2）

- 引擎在地面緊急關車（Emergency Engine Shutdown on the Ground 8-3）

- 起飛中引擎故障-放棄起飛（Engine Failure During Takeoff-At or Below V1）-Takeoff Abort 8-4

- 起飛中引擎故障-繼續起飛（At or Above V1）-Takeoff Continue 8-5

- 引擎在飛行中故障（Engine Failure In Flight Below Air Minimum Control Speed-Vmca 8-6）

- 潤滑油壓低（Oil Pressure Low 8-7）

- 航行油壓低（Fuel Pressure Low 8-8）

- 儅風板電氣失效（Windshield electrical Fault 8-9）

- 電氣系火警（Electrical Smoke or Fire 8-10）

- 環控系統火警（Environmental System Smoke or Fumes 8-11）

- 緊急下降（Emergency Descent 8-12）

- 緊急落地（Emergency Landing 8-13）

- 滑翔（Glide 8-14）

- 單電氣系失效（Single Inverter Failure 8-15）

- 雙電氣系失效（Dual Inverter Failure 8-16）

- 雙發電機失效（Dual Generator Failure 8-17）

- 使用氧氣（Environmental System-Use of Oxygen 8-18）

- 艙壓差異（High Differential Pressure-Cabin DIFF HI 8-19）

- 自動釋放氧氣系統故障（Auto-Deployment Oxygen System Failure 【CABIN ALT HI】Illuminated,【PASS OXYGEN ON】Extinguished 8-20）

- Bleed Air Fail（8-21）

- 緊急逃生（Emergency Exit 8-22）

- 螺旋（SPIN 8-23）

肆、建議事項

- 因本BEECH AIRCRAFT KingAir B350型機，本區無同機型之模擬機，目前全世界僅有兩架同型機模擬機可供使用，為維持飛航安全及飛行組員的操作熟練度，實應每年編列預算實施年度複訓，以達到維護飛航安全的目的。

- 身為民用航空局的成員，深知遵守紀律及操作手冊及程序的重要性，定期的飛行訓練能加強飛行組員的操控能力。

- 至不同的飛行訓練機構實施飛行訓練，能取得較多的機會及更多訊息。

伍、相關附件

- 相關附件

附件一：1-1~1-2航機外型

附件二：2-1~2.4引擎

附件三：3-1    油路系統

附件四：4-1~4-2電氣系統

附件五：5-1    液壓系統

附件六：6-1~6-2防火系統

附件七：7-1~7-13操作

附件八：8-1~8-23緊急處置