行政院及所屬各機關出國報告

(出國類別：其他)

赴美參加

第58屆IETF研討會出國報告

服務機關：中華電信研究所

出國人職    稱：助理研究員  助理研究員

姓    名：葉筱楓      連彥宗

出國地區  ：美國

出國期間  ：92年11月7日至11月16日

報告日期  ：92年11月18日

摘要

IETF為國際上重要之網際網路技術與標準制定組織，本組織為開放性質，參與者包括網路研究、設計、維運、網路產品廠商、網路服務提供者等，藉著參與會議可了解網際網路於各領域的技術演進，以及未來可能的發展動向，參與會議中IPv6及下一代網際網路相關技術的研討有助於掌握國際上相關標準技術的發展動向，以幫助我國IPv6與寬頻網路技術發展，符合時代與技術潮流的方向。

IETF依各研究性質分為不同的領域(Area)，各領域中又細分成不同的工作群(Working Group)，目前共有數十個工作群，會議中各工作群就各相關議題同時並分開成不同的議題(session)討論。由於會議議題廣泛，職選擇著重參加與IPv6及其應用的網路技術相關之重要工作群。

IPv6的運作標準早已大致完整，相關的研究已逐漸朝向管理、運作效率的提昇，以及各種應用的發展，許多網路應用領域（例如VPN）也漸漸著重研究如何順利演進至IPv6的環境。IPv6許多便利及自動的特性，期望能在現實環境中得到發揮，進而簡化並改善現有網路的許多複雜問題，但是現實使用環境中仍應先觀察廠商支援情況，作為市場接受度的指標。

由於亞洲地區發展網際網路的時間點落後於美歐等先進國家，在IPv4位址的取得也相對短缺，台灣目前上網率雖然高，但所擁有的網路資源仍較缺乏，而參與IPv6相關活動仍較不積極，我國應持續注意IPv6的國際動向，爭取較多的資源，以避免在邁入IPv6世代時又落後於其他先進國家。

目錄

一、	出國目的	2

二、	會議過程	2

三、	會議心得	3

四、	觀察與建議	6

五、	參考資料與網站	7

# 出國目的

IETF為國際上重要之網際網路技術與標準制定組織，本組織為開放性質，參與者包括網路研究、設計、維運、網路產品廠商、網路服務提供者等，藉著參與會議可了解網際網路於各領域的技術演進，以及未來可能的發展動向，參與會議中IPv6及下一代網際網路相關技術的研討有助於掌握國際上相關標準技術的發展動向，以幫助我國IPv6與寬頻網路技術發展，符合時代與技術潮流的方向。

IETF依各研究性質分為不同的領域(Area)，各領域中又細分成不同的工作群(Working Group)，目前共有數十個工作群，會議中各工作群就各相關議題同時並分開成不同的議題(session)討論。由於會議議題廣泛，職選擇著重參加與IPv6及其應用的網路技術相關之重要工作群，於後述之章節中報告。

# 會議過程

本次會議在美國Minneapolis舉行，為期六天，共十四的session，近百個working group。會議的第一天有例行為新參加者舉辦的簡介、撰稿說明、技術演講、歡迎餐會。之後便開始各working group的會議，每個working group依需要有1~2.5個小時的時間可討論，主要進行方式由該working group的主持人帶領，介紹議程並適時聽取、表決參與者的意見以作為標準制定過程的參考，Working group內若有更新狀態的文章、新消息或變動等就會依序由該作者簡報，或者提出目前該領域急待解決的問題，供參與者共同努力，與會者可隨時提出疑問、表達支持或反對的意見。

由於本次主題甚多(議程表詳如參考資料第二項)，且每個時段同時均有多個工作小組進行討論，故主要均挑選與IPv6相關的工作小組參與討論。

# 會議心得

本次參與舉辦於美國Minneapolis第58屆IETF研討會，參與會議心得簡述如下：

  - Security Tutorial

此議程是講解Security技術及應用服務之基本技術教學課程，內容涵蓋對稱式與非對稱式加密觀念、數位簽章、身分認證技術應用、CA的應用介紹、PKI簡介等課題。上述教學課程涵蓋Security基本運作原理，及延伸應用於IP網路相關技術與實務操作，藉此課程將讓相關領域學習者可有一個蓋括性的了解。IPv6中引入IPSec為其中一部份，以保障安全性的網路傳輸，因此有必要隨時了解Security技術領域的發展，與此領域於IPv6網路的應用。

- Multiprotocol Label Switching Working Group

本working group主要在建立標準的方式以使用label-switched路徑於各種不同的網路技術中，如Packet-over-Sonet、Frame Relay、ATM、以及LAN的技術（如Ethernet、Token Ring）；此外也定義所需的MIBs及相關必要的功能。由於目前MPLS基本運作標準都已底定，因此主要著重於：

- procedures and protocols for multicast protocol extensions for

point-to-multipoint TE, including soft-preemption
- Define requirements and mechanisms for MPLS OAM
- Define an overall OAM framework for MPLS applications
- MPLS-specific aspects of traffic engineering for multi-areas/multi-AS
  in cooperation with the CCAMP WG
- Determine (with CCAMP) what procedures are appropriate for evaluating
  proposals to extend the MPLS and GMPLS protocols, and document these

本會議主要提出部分draft的更新與修正，由會議的討論中並可了解目前此working group的更新主要在於讓MPLS能完整的支援 IPv6，並順利的運作，因此若這些方向進展順利，未來IPv6的骨幹網路的發展亦有可能建立於MPLS上。

- Multicast Security Working Group

本working group主要在制定一個標準讓Internet上的通訊群組能將資料傳輸於安全的環境中。因此對於群組使用的group key management、 group policy management以及容量擴展性、key distribution等問題都是研討的重點。本次主要有更新討論的文章為：GSAKMP、MSEC Group Key Management Architecture 、 MIKEY、MESP: A Multicast Framework for the IPsec ESP。

- Mobility for IPv6 Working Group

此working group著重於制定允許當IPv6主機於Internet上移動時，仍能持續使用其home address，並順利的解決路由及通訊的問題。目前並未有RFC產生，此次會議列入討論的draft如下：

- Mobility Support in IPv6

draft-ietf-mobileip-ipv6-24.txt

- Using IPsec to Protect Mobile IPv6 Signaling between Mobile Nodes and Home Agents

draft-ietf-mobileip-mipv6-ha-ipsec-06.txt

- The Mobile IPv6 MIB

draft-ietf-mip6-mipv6-mib-00.txt

Mobility一直是IPv6中重要的應用，由於此應用需要消耗的IP位址較多，且IPv6的引進又可解決三角傳輸的問題而進一步提昇傳輸與路由效率，因此相關標準的動向及廠商支援程度可再持續注意。

- IP Security Protocol Working Group

IPSec主要是希望於Internet上建立安全的傳輸環境，由於Security的領域甚廣，因此針對一些重要應用希望能盡快解決，本次會議中仍著重於下列領域的問題與解決方案的探討：

- Changes to IKE to support NAT/Firewall traversal

- Changes to IKE to support SCTP

- New cipher documents to support AES-CBC, AES-MAC, SHA-2, and
  a fast AES mode suitable for use in hardware encryptors

- IKE MIB documents

- Sequence number extensions to ESP to support an expanded sequence
  number space.

- Clarification and standardization of rekeying procedures in IKE.

- IP Version 6 Working Group Working Group

有關IPv6基本運作機制大致已經完成，目前的工作多以提昇運作效率以及MIBs為主，主要著重的工作方向有：

    - Complete Prefix Delegation requirements and publish. 相關工作有:

      - Work with the DHCPv6 working group to write a DHCPv6 option
for IPv6 prefix delegation.

      - Develop Proxy Router Advertisement solution for prefix delegation and publish. This enables a simple site border router to re-advertise downstream a prefix it hears on its upstream link. The Multi-Link subnet work will be used as the basis for this.

    - Complete revision of IPv6 MIBs (combined IPv4/IPv6 versions) and
publish.

其他方面的工作則包括：

- Complete work on "A Flexible method to manage the assignment of bits 
of an IPv6 address block".
- Revise "Aggregatable Unicast Addresses" (RFC2374) to remove 
TLA/NLA/SLA terminology and publish.
- Revise "Basic Sockets Extensions" (RFC2553) and publish.
- Revise "Advanced Sockets API" (RFC2292) and publish.
- Complete "Default Router Preferences, More-Specific Routes, and Load
Sharing" and publish.
- Update to ICMPv6 (RFC2463) and publish.
- Complete "Node Information Queries" and publish.
- Update Auto Configuration (RFC2462) and Neighbor Discovery (RFC2461)
and publish.
- Update "Privacy Extensions for Stateless Autoconfiguration" document 
(RFC3041) and publish.
- Complete work on IPv6 Node Requirements and publish.
- Complete work on Flow Label and publish.
- Explore and document the issues with site-local addressing. Determine 
appropriate limitations on the use of site-local addresses, and 
document those limitations.
- Complete work on Scoped Addressing Architecture and publish.
- Update IPv6 over PPP (RFC2472) and publish (may be done in PPP 
Extension w.g.). 
- Review Point-to-point link support in IPv6 and decide if any IPv6
specifications need to be updated.
- Complete work on "Link Scoped IPv6 Multicast Addresses" and publish.

- Layer 3 Virtual Private Networks Working Group

此Working Group主要探討如何利用L3 路由技術建立Provider-provisioned模式的VPN，目前主要的解決方式有三類：

  - BGP/MPLS IP VPNs (based on RFC 2547)

  - IP VPNs using Virtual Routers

  - CE-based VPNs using IPSEC

其運作模式的標準也逐漸陸續完成，目前許多討論已轉向如何順利支援IPv6的運作環境。此次主要納入討論的draft有：

- Service requirements for Layer 3 Provider Provisioned Virtual Private Networks:

- BGP-MPLS VPN extension for IPv6 VPN

- Network based IP VPN Architecture using Virtual Routers

- Virtual Router Management Information Base Using SMIv2

- Definition of Textual Conventions for Provider Provisioned Virtual Private Network (PPVPN) Management

- Framework for PPVPN Operations and Management

- CE-to-CE Member Verification for Layer 3 VPNs

- Security Framework for Provider Provisioned Virtual Private Networks

本次IETF會議除IPv6相關工作群之外，亦有其它相當重要之工作群召開會議，這些工作群日後亦將無可避免地與IPv6工作群有互動，值得日後加以注意。

# 觀察與建議

IPv6的運作標準早已大致完整，相關的研究已逐漸朝向管理、運作效率的提昇，以及各種應用的發展，許多網路應用領域（例如VPN）也漸漸著重研究如何順利演進至IPv6的環境。IPv6許多便利及自動的特性，期望能在現實環境中得到發揮，進而簡化並改善現有網路的許多複雜問題，但是現實使用環境中仍應先觀察廠商支援情況，作為市場接受度的指標。

由於亞洲地區發展網際網路的時間點落後於美歐等先進國家，在IPv4位址的取得也相對短缺，台灣目前上網率雖然高，但所擁有的網路資源仍較缺乏，而參與IPv6相關活動仍較不積極，我國應持續注意IPv6的國際動向，爭取較多的資源，以避免在邁入IPv6世代時又落後於其他先進國家。

IETF會場中提供WLAN服務，因此與會者可隨時使用筆記型電腦上網參閱、搜尋相關資料作為參考。會場中幾乎人手一電腦的使用WLAN，可見得此服務也已深入生活，成為生活工作的一部份。圖一及圖二為會場的參訪留影。

圖一									圖二

網際網路技術不斷發展，許多原本認為不可能的服務也漸漸深入生活的一部份，我們應該持續掌握世界技術潮流的方向，以便趕上甚至影響其發展以創造對我國最有利的競爭環境，

# 參考資料與網站

- IETF組織首頁：http://www.ietf.org。

- 議程表：

November 9-14, 2003

SUNDAY, November 9, 2003
1030-1700 IEPG Meeting - Salon A
1200-1900 Registration - Ballroom Foyer, 3rd Floor
1330-1430 Newcomer's Training - Salon B
1330-1500 Editor's Training - Conrad C
1330-1500 Intro WG Chairs Training - Conrad B
1500-1700 Security Tutorial - Salon B
1700-1900 Welcome Reception - Salon D

MONDAY, November 10, 2003
0800-2000 IETF Registration - Ballroom Foyer, 3rd Floor
0800-0900 Continental Breakfast - Ballroom Foyer, 3rd Floor
0900-1130 Morning Sessions

| Salon F | APP | apparea | Applications Open Area Meeting |
| --- | --- | --- | --- |
| Salon A | INT | hipbof | Host Identity Protocol BOF |
| Rochester | OPS | ipfix | IP Flow Information Export WG |
| Salon D | OPS | mboned | MBONE Deployment WG * |
| Salon B | RTG | ccamp | Common Control and Measurement Plane WG |
| Salon E | SEC | msec | Multicast Security WG |
| Salon C | TSV | tsvwg | Transport Area Working Group * |

1130-1300 Break 
1300-1500 Afternoon Sessions I

| Salon E | APP | lemonade | Enhancements to Internet Email to Support Diverse Service Environments WG |
| --- | --- | --- | --- |
| Rochester | INT | ipoib | IP over InfiniBand WG |
| Salon B | INT | mip4 | Mobility for IPv4 WG |
| Salon D | OPS | v6ops | IPv6 Operations WG * |
| Salon F | RTG | forces | Forwarding and Control Element Separation WG |
| Salon A | SEC | ipsec | IP Security Protocol WG |
| Salon C | TSV | avt | Audio/Video Transport WG * |

1500-1530 Break (Refreshments provided) - Ballroom Foyer, 3rd Floor 
1530-1730 Afternoon Sessions II

| Salon C | APP | iea | Internationalizing Email Addresses BOF * |
| --- | --- | --- | --- |
| Salon B | INT | mip6 | Mobility for IPv6 WG |
| Salon D | OPS | netconf | Network Configuration WG * |
| Salon A | RTG | ospf | Open Shortest Path First IGP WG |
| Salon F | SEC | pkix | Public-Key Infrastructure (X.509) WG |
| Salon E | TSV | dccp | Datagram Congestion Control Protocol WG |
| Rochester | TSV | rserpool | Reliable Server Pooling WG |

1730-1930 Break
1930-2200 Evening Sessions

| Salon E | APP | geopriv | Georgraphic Location/Privacy WG |
| --- | --- | --- | --- |
| Salon B | INT | eap | Extensible Authentication Protocol WG |
| Salon D | OPS | dnsop | Domain Name System Operations WG * |
| Rochester | OPS | rmonmib | Remote Network Monitoring WG |
| Salon C | RTG | rtgarea | Routing Area Meeting * |
| Salon F | SEC | ipsp | IP Security Policy WG |
| Salon A | TSV | pwe3 | Pseudo Wire Emulation Edge to Edge WG |

TUESDAY, November 11, 2003
0800-1800 IETF Registration - Ballroom Foyer, 3rd Floor
0800-0900 Continental Breakfast - Ballroom Foyer, 3rd Floor
0900-1130 Morning Sessions

| Rochester | APP | calsch | Calendaring and Scheduling WG |
| --- | --- | --- | --- |
| Salon A | INT | pana | Protocol for Carrying Authentication for Network Access WG |
| Salon B | OPS | psamp | Packet Sampling WG |
| Salon E | SEC | ltans | Long-Term Archive and Notary Services WG |
| Salon D | RTG | mpls | Multiprotocol Label Switching WG * |
| Salon F | TSV | rddp | Remote Direct Data Placement WG |
| Salon C | TSV | sipping | Session Initiation Proposal Investigation WG * |

1130-1300 Break
1300-1400 Afternoon Sessions I

| Rochester | APP | ldapbis | LDAP (v3) Revsion WG |
| --- | --- | --- | --- |
| Salon B | INT | send | Securing Neighbor Discovery WG |
| Salon D | OPS | dnsop | Domain Name System Operations WG * |
| Salon E | OPS | ipcdn | IP over Cable Data Network WG |
| Salon C | RTG | pim | Protocol Independent Multicast WG * |
| Salon F | SEC | enroll | Credential and Provisioning BOF |
| Salon A | TSV | enum | Telephone Number Mapping WG |

1415-1515 Afternoon Sessions II

| Rochester | APP | ldup | LDAP Duplication/Replication/Update Protocols WG |
| --- | --- | --- | --- |
| Salon C | INT | magma | Multicast & Anycast Group Membership WG * |
| Salon E | IRTF | gsec | Group Security Research Group |
| Salon B | SEC | secsh | Secure Shell WG |
| Salon F | TSV | alias | Access Link Intermediaries Assisting Services BOF |
| Salon D | TSV | nsis | Next Steps in Signaling WG * |

1515-1545 Break (Refreshments provided) - Ballroom Foyer, 3rd Floor
1545-1645 Afternoon Sessions III

| Salon B | APP | trade | Internet Open Trading Protocol WG |
| --- | --- | --- | --- |
| Salon E | INT | dna | Detecting Network Attachment BOF |
| Rochester | OPS | imss | Internet and Management Support for Storage WG |
| Salon A | OPS | multi6 | Site Multihoming in IPv6 WG |
| Salon C | RTG | ssm | Source-Specific Multicast WG * |
| Salon F | SEC | sasl | Simple Authentication and Security Layer WG |
| Salon D | TSV | midcom | Middlebox Communication WG * |

1700-1800 Afternoon Sessions IV

| Salon E | APP | opes | Open Pluggable Edge Services WG |
| --- | --- | --- | --- |
| Salon D | INT | ipv6 | IP Version 6 WG * |
| Rochester | OPS | entmib | Entity MIB WG |
| Salon A | OPS | multi6 | Site Multihoming in IPv6 WG |
| Salon B | SEC | mobike | IKEv2 Mobility and Multihoming BOF |
| Salon F | SEC | smime | S/MIME Mail Security WG |
| Salon C | TSV | rmt | Reliable Multicast Transport WG * |

WEDNESDAY, November 12, 2003
0800-1800 IETF Registration - Ballroom Foyer, 3rd Floor 
0800-0900 Continental Breakfast - Ballroom Foyer, 3rd Floor 
0900-1130 Morning Sessions

| Duluth | APP | imapext | Internet Message Access Protocol Extension WG |
| --- | --- | --- | --- |
| Salon C | GEN | nomcom | Operation of the IESG/IAB Nominating and Recall Committees WG * |
| Salon E | INT | ipdvb | IP over MPEG-2/DVB Transport BOF |
| Salon A | INT | l3vpn | Layer 3 Virtual Private Networks WG |
| Salon B | OPS | multi6 | Site Multihoming in IPv6 WG |
| Rochester | SEC | krb-wg | Kerberos WG |
| Salon D | TSV | avt | Audio/Video Transport WG * |
| Salon F | TSV | iptel | IP Telephony WG |

1130-1300 Break
1300-1500 Afternoon Sessions I

| Salon E | APP | crisp | Cross Registry Information Service Protocol WG |
| --- | --- | --- | --- |
| Salon C | GEN | problem | Problem Statement WG * |
| Salon D | INT | ipv6 | IP Version 6 WG * |
| Rochester | OPS | bmwg | Benchmarking Methodology WG |
| Salon F | OPS | netconf | Network Configuration WG |
| Salon B | RTG | rpsec | Routing Protocol Security Requirements WG |
| Salon A | TSV | sip | Session Initiation Protocol WG |

1500-1530 Break (Refreshments provided) - Ballroom Foyer, 3rd Floor
1530-1730 Afternoon Sessions II

| Salon A | INT | l2vpn | Layer 2 Virtual Private Networks WG |
| --- | --- | --- | --- |
| Salon C | INT | nemo | Network Mobility WG * |
| Salon F | IRTF | ans | Ad hoc Network Scaling |
| Salon D | OPS | v6ops | IPv6 Operations WG * |
| Salon E | SEC | sbsm | Session Based Security Model for SNMPv3 BOF |
| Salon B | TSV | xcon | Centralized Conferencing WG |

1730-1930 Break
1930-2200 IETF Administration Plenary - Salon A/B/C/D
   - Introduction to the format and Agenda (Harald Alvestrand and Leslie Daigle)
   - Current Status Overview
      - IETF Chair Welcome
      - IETF Report
      - IAB Chair
      - IRTF Chair
      - RFC Editor
      - IANA
   - IETF Evolution
   - AdvComm report and discussion
   - PROBLEM and IESG's proposal for reform efforts

2230 Late Night Session

| Rochester | PGP Key Signing |
| --- | --- |

THURSDAY, November 13, 2003
0800-1800 IETF Registration - Ballroom Foyer, 3rd Floor
0800-0900 Continental Breakfast - Ballroom Foyer, 3rd Floor
0900-1130 Morning Sessions

| Salon A | APP | simple | SIP for Instant Messaging and Presence Leveraging Extensions WG |
| --- | --- | --- | --- |
| Salon E | INT | dhc | Dynamic Host Configuration WG |
| Salon B | OPS | grow | Global Routing Operations WG |
| Rochester | RTG | vrrp | Virtual Router Redundancy Protocol WG |
| Salon F | SEC | pki4ipsec | Profiling Use of PKI in IPSEC BOF |
| Salon C | SUB | tewg | Internet Traffic Engineering WG * |
| Salon D | TSV | nsis | Next Steps in Signaling WG * |

1130-1300 Break
1300-1500 Afternoon Sessions I

| Salon A | APP | simple | SIP for Instant Messaging and Presence Leveraging Extensions WG |
| --- | --- | --- | --- |
| Salon D | INT | dnsext | DNS Extensions WG * |
| Salon B | OPS | aaa | Authentication, Authorization and Accounting WG |
| Salon E | RTG | idr | Inter-Domain Routing WG |
| Rochester | SEC | inch | Extended Incident Handling WG |
| Salon F | TSV | ippm | IP Performance Metrics WG |
| Salon C | TSV | speechsc | Speech Services Control WG * |

1500-1530 Break (Refreshments provided) - Ballroom Foyer, 3rd Floor
1530-1730 Afternoon Sessions II

| Rochester | APP | webdav | WWW Distributed Authoring and Versioning WG |
| --- | --- | --- | --- |
| Salon C | GEN | newtrk | New IETF Standards Track Discussion BOF * |
| Salon F | INT | mipshop | MIPv6 Signaling and Handoff Optimization WG |
| Salon E | RTG | manet | Mobile Ad-hoc Networks WG |
| Salon B | SEC | saag | Open Security Area Directorate |
| Salon A | TSV | sipping | Session Initiation Proposal Investigation WG |

1730-1930 Break
1930-2200 Plenary Presentation - Open Minds, Open Mic - Salon A/B/C/D
   - Introduction - Harald Alvestrand
   - Topical Presentation
   - Open Architecural Work Session
   - Opportunity for Plenary Comment (open mic)
      - IESG
      - IAB

FRIDAY, November 14, 2003
0800-0900 Continental Breakfast - Ballroom Foyer, 3rd Floor 
0900-1130 Morning Sessions

| Salon A | APP | xmpp | Extensible Messaging and Presence Protocol WG |
| --- | --- | --- | --- |
| Salon B | OPS | capwap | Control and Provisioning of Wireless Access Points BOF |
| Duluth | OPS | radext | RADIUS EXTensions BOF |
| Salon D | TSV | mmusic | Multiparty Multimedia Session Control WG * |
| Rochester | TSV | nfsv4 | Network File System Version 4 WG |