行政院及所屬各機關出國報告

(出國類別 : 實習)

SS7信號網管設備技術

實習報告

服務機關 : 中華電信研究所

出國人    職    稱 : 助理研究員

姓    名 : 賴信良

出國地區 : 美國 紐約

出國期間 : 92年12月7日至92年12月19日

報告日期 : 93年 2月4日

摘  要

利用網際網路傳送語音通信VOIP及SS7界接技術之突飛猛進，在話音品質及應用領域將日趨成熟，未來勢必成為通信網路之骨幹。本公司已積極規劃引進及建設IP網路應用，本所為研發VOIP與SS7相關技術之需求，因此有必要至國外電信機構現場實習，有關VOIP與SS7技術之設計應用與維運管理經驗，以提供本公司IP與SS7規劃建設，維運及研發相關產品之參考。

本次實習係依照本所92年度”PSTN&IP&PLMN網路SS7信號網管維運研發設備”R920456購案合約辦理，於92年12月7日啟程，赴美國Intel公司實習SS7與VOIP交換機相關技術，並於92年12月19日完成課程順利返國。

此次實習主要是針對Intel公司的SS7 Signal Gateway(CPM8) 及IP PSTN Gateway(DM/IP481)等系統設備，參與該公司訓練課程、現場實習操作、技術討論、應用實例參訪等，行程緊湊，獲益良多。

經過此次實習，職除了對於Intel公司SS7&VOIP相關產品有深入了解外，對於SS7&VOIP設計原理及應用趨勢亦有更深確的認識，將可提供本公司SS7&VOIP相關技術規範制定、建設規劃及本所研發SS7&VOIP利基產品之參考 。

本報告首先簡述此次實習之目的，接著列出主要行程及實習內容，包括Intel公司之SS7 Signal Gateway與IP PSTN Gateway 相關產品之主要特點及系統架構，硬軟體設計，第三部份描述實習心得，最後提出建議供有關單位參考。

SS7信號網管設備技術

出國實習報告

目   錄

1.	目的	4

2.	過程	4

3.	心得	11

4.	建議	12

SS7信號網管設備技術

出國實習報告

# 目的

利用網際網路傳送語音通信VOIP及SS7界接技術之突飛猛進，在話音品質及應用領域將日趨成熟，未來勢必成為通信網路之骨幹。本公司已積極規劃引進及建設IP網路應用，本所為研發VOIP與SS7相關技術之需求，因此有必要至國外電信機構現場實習，有關VOIP與SS7技術之設計應用與維運管理經驗，以提供本公司IP與SS7規劃建設，維運及研發相關產品之參考。

# 過程

## 行程

日期                      地點                  工作

92年12月 7日           桃園- 紐約            去程

92年12月8~17日         紐約                  Intel公司

實習VOIP&SS7

設備參訪

92年12月18~19日         紐約- 桃園            回程

## 內容

本次實習主要係針對Intel公司SS7 Signal Gateway(CPM8)及IP PSTN Gateway(DM/IP481)等系統設備，參與該公司訓練課程、現場實習操作、技術討論、應用實例參訪等，茲摘要如下 :

### 2.2.1  SS7 Signal Gateway(CPM8)信號閘道器

#### 2.2.1.1. 主要特點

SS7 Signal Gateway(CPM8)主要特點如下:

- 智慧型Multi-Port信號介面卡

- 具備onboard support for SS7 common channel signaling protocols

- On-borad信號處理系統

  - 處理器：MPC860

  - 時脈：50 MHz

  - 記憶體：32 Mbyte Synchronous DRAM

  - 匯流排介面：33 MHz 32 bit CompactPCI Rev. 2.1

- 信號處理器支援multiple HDLC based signaling channel including up to 4 SS7 signaling link

- 支援最多8個可軟體控制之T-1 (1.544 Mb/s)或CEPT E-1 (2.048Mb/s) digital line介面

- 具備 On-board H.110 Computer Telephony (CT) Bus interface可與其他介面卡或系統交換signaling timeslots

- 具備2個V.35-compatible序列埠

- 支援相容於PICMG標準之熱插拔

### 2.2.2 IP PSTN Gateway(DM/IP 481)電話網路閘道器

#### 2.2.2.1. 主要特點

IP PSTN Gateway(DM/IP 481)主要特點如下:

- 具備 Equiped wish  a PSTN network front end

- 具備connected via  NetSructure platform to the CT Bus

- 具備Single board digital IP to PSTN Gateway application

- 具備Conferenceing Resource

  - Shareable conference resource

  - Run time add ane remove conference

  - Active talker notification

  - Automatic notification on adding and removing parties

  - DTMF clamping

  - Volume control

  - Auromatic gain control

  - Echo Cancellation

  - Monitoring function

- 支援RFC2833以發展具擴充性系統

- 支援由IP載送傳真信號

  - Support ITU T.38 for real time fax transmission

  - 經由T.38 閘道器 透過IP-based Network

- 具備H.323規約Stack

  - Support the host-based H.323 RADVISION

  - Includeed system release software

  - Providing IP signaling for establishing calls over IP network

  - Using Global Call API for call control

- 雙音複頻信號處理 (DTMF Processing)

  - Ability to generate DTMF to and receive notification

  - From IP side via UII alphanumeric message (out of band)

  - From TDM side inband

  - Inband DTMF pass-through

  - RFC 2833 pass-through

- 服務品質(Quality of Service QOS)

  - Support the setting and retrieving of QoS

  - Setting and retrieving of QoS threshold and handling of QoS alarm

  - QoS threshold support : Lost packets, jitter, Roundtrip latency

  - Support the type of services( ToS)

- 支援IP傳送語音 (Voice over IP support)

  - RTP 處理

  - RTCP處理

  - Jitter 緩衝器管理

  - Packet loss concealm

- 具備SIP規約Stack

  - Support the host-based SIP RADVISION

  - Establishing calls over IP network

  - Using the Global Call API for call control

- 具備SNMP管理功能

  - Monitoring and control is provided

  - Provide Administration Software

- 具備應用界面( Application interface)

  - Support the R4 Programming environment

  - Global Call API for call control

  - IP Media Library(IPML) API for media management

- 具備Call control implemented on the host, RTC on board

- 提供Split call control via the IP Media Library API

- 支援Global call API support for IP and PSTN

- 提供FCD file generation utility

- 支援Flexing routing  (exportable voice resource)

- 具備Standard Internet protocol including TCP/IP,UDP and RTP/RTCP

- 具備與解碼器全雙工通信功能

- 具備Coder support including GSM,G.729

- 具備Microsoft Netmeeting and Vocal tec

- 提供IP switching bridge two calls with minimum latency

- 提供Type of service (ToS) byte

- 具備Packet redundancy : comply with RFC 2189

- 提供IP media service

- 提供High reliability configuration

- 具備IP Voice stream Resource

- 具備Object ID support when using Non-standard command

- 提供Voice quality parameter and volume control

- 具備呼叫程控功能

  - Continuous Speech Processing (CSP) support

  - Support NFAS on N12 protocals

  - Support R2MF hot down procotal

  - Support PSTN (4 ESS,5 ESS, DMS,CAS) signaling

- 具備語音特性控制功能

  - Gain control

  - DTMF volume control

  - On board PSTN interfaces

  - Support digital interface

  - Support Media load 1 voice and load 2 enhance voice

  - Basic DTMF and MF detection

  - Support call analysis

### 2.2.3. 系統發展軟體( Development Software)

### 2.3.1. 應用程式庫( API Libraries)

#### 2.3.1.1.新事件服務程式( New event service )程式庫

- Provide an interface for registering any application with the Intel Dialogic event notification framk

- Subsystem for sending asynchronous, system administration events to application

- Generated when activities take place in the system

- Single board stop or start , board removal or insertion

- CT bus line failures and T1/E1 network alarm

#### 2.3.1.2. 語音會議電話(Audio conference)程式庫

- Support development of host-based conferenceing application

- Develop customized audio conferencing services

- Including library functions, divice drivers, and firmware

- Provide conference bridging and monitoring

- Support per party basis of DTMF clamping

- Adjust the listening volume of conference

- Echo cancellation for each active talker

- High port density

#### 2.3.1.3. 連續性語音處理( CSP)程式庫

- Host based automatic speech recognition (ASR)

- High performance each cancellation

- Voice energy detection, barge-in, voice event signaling, pre-speech buffering

- Full duplex operation

- Including library functions, device driver, fireware and demonstration

- Streaming echo-cancelled data to the TDM

- Each canceller tap length of up to 512 taps

- Ability to re-arm the VAD

- More powerful Voice Activity Detector

#### 2.3.1.4. FAX API 程式庫

- 支援Wide variety of Fax applications

- 提供Intel Dialogic 第六版軟體 for CompactPCI an windows

- 支援ITU-T G3 ,V.17, 資料速度 14.4K

- 符合Data transmission encoding scheme with advanced compression

- Polling and turnaround

- 符合Simple header overlay

- 具備Image bit order (MSB/LSB) conversion

- Encoding of color fax imagines

#### 2.3.1.5.整體呼叫程式庫

- Uniform call control interface for developing application

- Protocol operation on Intel NetStructure, DM3 and Springware architecures

- Designed to support a variety of protocols

- Provide a consistent application interface

- Use the same input and output parameters at the application level

- 支援H.323 and SIP host-based stacks

- 符合 Multi-protocol support on Global call devices

- 符合Register with a Gatekeeper or Registrator

- 支援Support DTMF Mode

- 支援 Fax transmission and reception

#### 2.3.1.6 IP中介媒體( Media) 程式庫

- Used to control media on IP devices

- IP Media library (IPML) Provides DialogicR 6.0 & CompactPCI on Windows

- Preferred DTMF Mode, UII Alphanumeric

- Send and receive Fax for T.38

- Using IPML API to build a PSTN-IP gateway

- Media resource management and media resource operation functionality

- Quality of Service(QoS) threshold alarm configuration and status reporting

- Support of Standard Runtime Library(SRL)

#### 2.3.1.7 模組中繼介面應用程式(Modular Station Interface API)

- Provide high density analog station connectivity

- Support up to 120 stations with tone diction and generation

- 支援FSK caller ID transmission

- Conference Management functions to control conferencing features

- Configuration functions to set and retrieve device parameters

- Device Management functions to set and retrieve device parameters

- Diagnostic functions to test devices

- Routing functions to allow communication between time slots on the CT bus

#### 2.3.1.8. 自然建構管理(Native Configuration Manager)應用程式庫

- 提供Interface for developing customized system configuration

- 具備Get the AUID of a board

- 具備Get the board name from and AUID

- Modifying board-level and system-level configuration

- Starting, stopping and checking the status

- Setting the TDM bus clock master fallback list

- Getting stystem software version information

- Cached prompt management

- Enhancement to Multi Frequency signaling

- Enhancement to DV_TPT termination conditions

#### 2.3.1.9 標準執行( Standard Runtime)應用程式庫

- Provide a common interface for event handling and functionality

- Provide the framework for implementing the programming model

- Events are handled in a standard manner

- Support for alternative variant of the extended asynchronous programming

- Support for the synchronous model

- Support for synchronous with SRL callback model

- Support for polled model

- Asynchronous with non-signal callback model

- Extended asynchronous model

- Device event management

- Device information retrieval using ATDV_prefixed functions

#### 2.3.1.10 語音應用程式( Voice API)

- Building a wide range of high-density call processing application

- Voice messaging, interactive voice response,telemarting/call center

- Including tone signaling,global tone detection and generation

- Call progress analysis and voice encoding algorithm selectable

- Cached prompt management

- Interactive multimedia association with ADPCM algorithm

- Using linear coding ,VOX and WAVE file format

- Speed control and volume control

- Transmit/receive analog display service interface

- Perfect call call progress analysis

- Transaction record

- Bulk data buffer sizing

# 心得

## 由於電信硬體設備及相關規格標準的日趨成熟，國外通信大廠主力產品均以Internet應用環境為主，其功能更加完整且價格不斷下降，因此市場競爭非常激烈，在我們研習之Intel 公司通信部門均感受人事精簡之壓力,每位工作人員需全力以赴，才有生存之空間。

## 不論是有線與無線PSTN業者皆採用網際網路通訊協定(Internet Protocol，IP)技術作為解決方案。世界各地許多業者的現有網路中，其資料通訊流量超越語音通訊，因此IP已成為受矚目的應用模式。

## VOIP之遠景看好，語音之重要是永恆的，VOIP初期利基在廉價之長途及國際電話，但隨著電信自由化，電話費率逐年下降，VOIP在「節費」方面的色彩已淡化許多，驅動VOIP成長的背後因素，主要是IP化架構後所能衍生的各式服務與應用，這才是VOIP的真正價值。在過渡之時期中，如何透過SS7將舊有的PSTN與新建之VOIP交換機之間作適度之整合，乃是當前之重要課題。

## SS7/IP閘道器採用信號傳輸(Signaling Transport，SIGTRAN)通訊協定與架構，支援PSTN業者的需求。SS7包含一套通訊協定與架構，為PSTN與無線通訊網路提供核心智慧功能。SS7支援的服務涵蓋範圍包括最基本的電話、免付費電話服務、一直到無線通訊漫遊等。

## SIGTRAN型閘道器在大型系統中負責與各種IP型主機之間執行SS7訊號的傳送與接收的工作。它亦負責管理網路跨接的作業，並管理兩個網路之間的互動機制，達到緊密整合的目標。SIGTRAN型閘道器讓IP主機能支援不同的SS7環境。SIGTRAN亦規範出一套完善的架構，以支援各種具備高擴充性與回復能力的系統。這些特性讓代工廠商能在現有的SS7網路中建置低成本的系統，同時亦打造出理想的環境，讓業者能結合SS7與IP網路，整合至各種服務商等級的IP電話閘道器中。

## SS7/IP信號閘道器可支援多種應用系統，其中涵蓋三大類型: 通話控制、無線通訊、以及智慧型網路。在每種類型的應用系統中，信號閘道器皆是大型IP系統的重要構成元件。

## 資料與語音網路整合的時代已經到來。傳統的PSTN網路已開始承接大量的資料傳訊，其流量已超過本身的負荷能力。欲克服PSTN限制的一項關鍵技術就是採用SS7信號閘道器，如此即能達到真正整合的機制目標，為下一代網路基礎建設奠定完善的基礎。

## SS7 Signal Gateway(CPM8)主要特點為一智慧型Multi-Port信號介面卡，並具有高可靠性，支援相容於PICMG標準之熱插拔功能，在單一CompactPCI電路板可以提供支援最多8個可軟體控制之T-1(1.544 Mb/s)或CEPT E-1 (2.048Mb/s) digital line介面。

## IP PSTN Gateway(DM/IP 481)主要特點為允許語音經由IP傳送(VOIP) ，透過Intel NetStructure平台至CT Bus，利用DM/IP Board 接至PSTN網路，完成IP與PSTN介面功能，並可具有會議電話,語音辨識，文字轉語音等多樣化之應用服務。

# 建議

- 資料與語音網路整合的時代已經到來。傳統的PSTN網路已開始承接大量的資料傳訊，隨著服務需求及技術進步，未來以IP網路傳送語音信號，並結合多媒體通信服務為需求,以致應用面更為廣泛。隨著IP網路建設日趨普及，與現用SS7電信網路交接更加複雜，對於本公司現有網路建設與維運需求，建議儘早詳細規劃SS7與IP網路發展策略，維持最佳之市場競爭力及即時符合客戶之需求。

- 先進國家電信機構對於IP技術與產品，不斷推陳出新,本公司對於IP新技術之學習與引進，仍須持續進行與積極推展，以技術不斷更新，讓公司達到永續經營之目的與穩居業界之領導地位。