經濟部暨所屬機關因公出國人員報告書

（出國類別：其他）

參加美國安全工程師協會2007年會報告書

| 出 國 人： | 服務機關：台灣中油公司 工安環保處 職務：工業安全衛生師 姓名：施學堯 |
| --- | --- |
| 出國地點： | 美國 |
| 出國期間： | 96年 6月 23日至 6月30日 |
| 報告日期： | 96年 9月 26日 |

報告書摘要

參加年會活動重點敘述包含

1.ASSE 組織

2.年會活動概況

3.研討會之內容

（1）施工架的安全

（2）墜落預防之迷失與誤解

（3）關鍵控制-工業上新規則

（4）電弧危害分析

（5）以安全觀察預防現塲職災

（6）辨識重大危害的技巧

（7）工作場所安全與衛生準則的世界趨勢

4.博覽會

目 次

一、前言……………………………….…………4

二、出國目的…………………………………… 4

三、出國行程…………………………………….5

四、參加會議經過………………………..…….. 5

五、心得與建議………………………………….20

六、附件………………………………………….22

一、 前言

（一）美國安全工程師協會（American Society of Safety Engineers ，ASSE) 2007大會及博覽會於96年6月24日至27日在美國佛羅里達州奧蘭多市(Orlando)舉行，是安全衛生方面重大的盛會及博覽會。除為期三天的會議中2塲之大會演講外，並包含225 場有關人力發展、營建與鑚採、專業顧問、緊急應變與保全、環境與有害廢棄物、人因工程、健康與工業衛生、健康照護、國際性工安衛生、法規、風險管理與損失控制、安全管理、工程技術與標準、教育訓練、交通之專題發表會，與會者可依自己的需求及興趣去選擇聽講。除此，會前（6月21日至6月24日）及會後（6月28日至6月30日）並共有44 種一至三天的技術專業課程，可取得學分或參加相關之專業技能人員（CSP，CERTIFIED SAFETY PROFESSIONAL）, ASP CHST 或CHMM 等之認證測驗。今年的博覽會計有美國當地及世界各地廠商約450 餘家參展，提供有關安全衛生產品介紹及咨詢服務。

（二）美國安全工程師學會（ASSE）成立於1911年，為最早及最大的專業安全機構，是一個非營利、非政府的國際民間組織，也是一個會員制組織，目前會員數超過3萬，經營著有關工業界、保險業、政府機構與教育之安全衛生與環保事項之督導與顧問。組織由含8位區域性副董事長與協會副董事長、票選資深副董事長及財務副董事長兼執行長位組成16人之董事會做決策，下轄152小組、31分會與52學生分會，並有學術性、營建、顧問、防火工程、環境保護、健康照護、人因工業衛生、國際性、醫院及製造業管理、採礦、公共部門 、保險風險管理之訓練與溝通、油氣運輸等13種諮詢專家。

二、 出國目的

本公司雖非 ASSE 會員，但由於ASSE大會仍為國際性有關工安之主要專業研討場所，故本次參加此會議以吸取國外人士在安全衛生方面所提供的新知識及技術，並瞭解目前國際間對安全工作推動的方向與重點、未來的發展趨勢，並藉參觀博覽會瞭解最新科技產品，對安全衛生所提供的保護程度，能作為本公司在增進安全管理的參考。

三、 出國行程

| 日期 | 活動紀要 |
| --- | --- |
| 96/06/23-24 | 往程（台北－美國－佛羅里達州奧蘭多市） |
| 96/06/25-27 | 參加研討會 參觀展覽會 |
| 96/06/28-30 | 返程 |

四、參加會議經過:

(一) 開幕式專題演講 Opening Keynote

大會特別邀請文化人類學專家兼名作家與評論家，Jennifer James 闡述有關其新創「未來式的思考法」，說明領導者的文化素養及如何符合今日職場的競爭。

(二) 研討會

參加之各場研討會內容敘述如下：

甲、施工架的安全

主講者：John Palmer, CSP

主講者講述有關施工架基本上應有之安全概念：

所有暫時性架高的工作平台(支撐或懸吊)，用於支撐施工人員，建築材料或兩者的都稱做施工架。 施工架基本上分兩種，從下方支撐或從上方懸吊。

當計畫要搭架一個施工架工程時，第一件要考慮的事是訓練人員，一個稱職的人員必須監督施工並且進行每項工作的檢查。

在設置一個施工架工程時，每一不同的施工面有著各自獨特狀況，下面幾點是需要考慮計畫的:

  - 鄰近建築物的地方，管線交錯的地方或是上方的障礙物

  - 足夠的通路到施工面

  - 氣候狀況和風勢防護物

  - 有足夠堅固的地基從平穩的地面支撐施工架，可以保證承載貨物

  - 擾亂施工或施工人員的因素

  - 環境危害因素

  - 堅固的支撐物適當地設置在所有的方位

  - 平台的出入口要安全且簡易

  - 施工人員使用防墜設備

  - 上方載卸甲板的保護設施

  - 墜落物的防護設施

  - 計劃在施工架上裝卸貨物的承受量

在施工架上裝載貨物是計劃搭建一個施工架主要的因素之一。基本上，施工架架構依據裝載貨物的不同分為三個等級。輕型的是每平方英尺二十五磅以下，中型的是每平方英尺五十磅以下，重型的是每平方英尺七十五磅以下。使用者要知道工作平台將需要承受多少重量，包括施工人員、施工工具和材料。

所有搭建施工架的設施都需要仔細的檢查巡視過，以確保是良好的狀況可供使用，有損壞或是劣質的設施應拆除：

- 不使用明顯損壞的施工架設備或附件

- 不使用生鏽或受侵蝕的施工架設備

- 檢查彎曲部分，尤其是被扭曲和壓碎的部分

- 檢查在接合點、熔合處或周邊的裂痕

- 檢查管內部是否生鏽

- 檢查活動零件部分

- 檢查缺少之勾環或釘子、彎曲欄杆扶手、損壞的板面

- 檢查有顯示氣泡或裂痕油漆的部分

施工架必須綁緊及增加基地的寬度建立緊實的架構，防止它倒塌。較狹窄的基地比較不穩定，施工架容易翻覆。當施工架向上架高時，第一個連接處不應該高於最小寬度的四倍，例如寬五英尺的施工架，第一個連接處應該要在低於二十英尺的地方。

風的力量可以對施工架有驚人的影響，尤其是當施工架附有防水布或其他種掩蓋物。

工作平台應設在有安全且簡易出入口的施工架上。出入口的梯子或相等功用的出口，應該設置在至少比較低階層高兩英尺的地方。

乙、對防墜安全之錯誤或無依據的觀點

主講者：Richard J Epp，PE，CSP

Industrial Safety Engineer

###### Lawrence Livermore National Laboratory

Livermore, CA

本項專題主要重點在於OSHA（通用安全與健康條款） 29 CFR1910一般工業準則當中的D和I部分，包括地面工作，個人防護具；29CFR1926營建準則當中的M和X部分，包括防墜設備，樓梯和梯子；OSHA工具的翻譯說明，資源的使用，當你使用OSHA系統時詢問定義時，系統會依照英文字母的順序排列解答。

對防墜安全有一些共通的迷思或錯誤觀點：

- 29CFR1910 (一般工業)和29CFR1926(營建)準則可以互相交替是錯誤的觀點：

29CFR1910涵蓋一般工業，包括操作和維修。29CFR1926涵蓋營造業，例如施工、修建、改建、屋頂或拆建。

- Six-foot規則是無根據的觀點：

OSHA從未接受單一距離(從建築物的邊緣)是足以防止設施墜落的前提。

那如何才是可以接受的?第一步要先決定是屬於一般工業或營造業。一般工業來說，非常相似六英尺規則，不過有幾項條件也必須符合。

  - 坡度必須低於10%

  - 遵守29CFR 1910.28(d)

  - 附屬條件：允許活動範圍應在正常施工範圍之內，活動範圍需在至少離建築物邊緣六英尺遠的距離，施工場地的出入口應用兩條明顯繩索標示定位出來

Exhibit 1. Designated Area

至於營造業，大致上距離就可以說是安全的主要條件。以下提供幾點容易誤解的規則：

（a）29CFR 1926.502 (f)建立警告線系統--適用於低坡度的屋頂工程

（b）29CFR 1926.502 (g)控管進出口區域--適用於在上方有砌磚或相關工程

（c）29CFR 1926.502 (h)安全監視系統--適用於只有五十英尺寬的低坡度屋頂

Exhibit 2. Non-conforming Guardrail

- 防墜限制不是錯誤或無根據的觀點：

雖然現在沒有特定的準則規定，防墜限制是用設備去防止墜落的發生。如果你不會墜落，那麼就排除重大的危害並且沒有墜落保護設施的問題了。請不要混淆fall restraint和fall positioning。Fall restraint完全不允許有任何的距離發生墜落；但fall positioning允許發生墜落的距離，但即使發生也不會超過兩英尺。

Fall Positioning							Fall restraint

- 梯子的使用常引起錯誤的概念：

OSHA已經確定只要你是使用Envelope Ladder，就不必要求一定要防墜設備。所謂的Envelope Ladder有幾項要素：

  - 一個1：4的攀爬角度

  - 攀爬的地方面對梯子

  - 梯角是堅固且防止滑動的

  - 在使用者攀爬時，必須要有三個點可以接觸

本項專題主要是解釋一些OSHA資源和關於防墜方面的知識及利用，以提供客戶更多的選擇，以及在每一種狀況中提供更好機會和功效的防墜設備。

丙、關鍵點管制-工業新規則

主講者：Glenn G. Young, C.S.P. -Owner

Glenn Young & Associates, LLC PSM Consulting

及 Glenn S. Crowe, C.S.P. - Safety Manager

PCS Nitrogen-Phosphates

評估控制系統的概念基於風險，使用資源降低控制系統的風險，提高可依賴度。S84（ANSI / ISA S.84.00.01 – 2004， Parts 1-3 (IEC 61511 Mod).1之簡稱）只是一致性的標準，而沒有正式的約束力。當他們應用控制系統的使用者時，S84的大致條件如下：

- 運作一個基本風險的分析，當控制系統故障時，會造成多大的危害

- 控制系統如果操作失敗所會造成的危害，基於危害的程度給一個指標

- 如果現有的控制系統有足夠的信賴度：將分析的資料歸檔並且繼續保持維護現有的設備儀器，以持續信賴度

- 如果現有的控制系統無足夠的信賴度，持續改進到可能造成的危害程度減緩。

什麼是控制系統?一個控制系統是由一個或多個感應器連結到一個或多個邏輯元件，進而控制一個或多個啟動元件和元件中的連結。

跳俥系統(Trip System)在傳統觀念裡是視為保護裝置。是否其他剩餘獨立層級的保護裝置能夠減緩最遭之損壞結果的風險?如果是，歸檔此結果並且考慮將跳俥系統放在較低優先權。否則，設定跳俥系統為主要控制系統(Critical Control System， CCS )，並且分析跳俥系統的信賴度。

如何定位信賴程度?一般決定主要控制系統(CCS)信賴度的方法是：假設CCS發生需要跳俥的狀況且CCS功能失靈，然後製程危害分析 (PHA)對最壞可能發生的結果做評估。

典型的風險發生於化學製品、精煉廠、輸油管的傷害，產生安全整合水平等級(Safety Integrity Level，SIL)：

- Highest risk= 使用SIL-3 防護.

信賴度介於十分之一到百分之一之間，屬於最高風險的CCS需使用第三層級的保護裝置。

- Second-highest risk= 使用SIL-2防護.

信賴度介於百分之一到千分之一之間，屬於第二高風險的CCS需使用第二層級的保護裝置。

- Third-highest risk= 使用SIL-1防護

信賴度介於千分之一到萬分之一之間，屬於第三高風險的CCS只需使用第一層級的保護裝置。

- Lower risk= No SIL needed.

低風險，信賴度大於萬分之一，不需要SIL防護

如何增進主要控制系統的信賴度? 依照以下策略可以增進主要控制系統的信賴度：

- 使用更多可信賴的元件替補原始的元件

- 增加測試和校準的次數

如果CCS對所要執行的動作失效，需要評估且分析信賴度及CCS為何失敗者為使用者而不是製造商。現在化學製品、精煉廠、輸油管工業已經在考慮S84或其他相關準則的履行。

丁、電弧閃燃傷害分析-

如何適當使用工程控管以減少嚴重的電流灼傷

主講者：John J. Kolak, BSEE, MS, CSP

Praxis Corporation

了解電弧傷害分析(Arc-Flash Hazard Analysis，AFHA)是很重要的，不僅僅只是選取防焰材質(Flame Resistant，RF)的衣服。許多電機工程師已經利用許多種理論方法探討計算關於電弧的”熱度”，但最後只用這些資訊建議工程人員穿著高等級的防火材質工作服。適當的建議應該是，先企圖利用改變工程系統降低高熱度的發生，然後才選擇適當的防火工作服對抗那些無法用工程科學控制剩餘風險。

由於電弧所產生的高溫常導致工作人員死亡或重大傷殘，所以建立電弧傷害分析(AFHA)已經成為必須實行的事。由於每次電弧的發生都是獨一無二的，因為各種不同複雜的形成因素，是沒有辦法被重新再一次創造一樣的電弧供以研究的。所以只能在少數之前的案例中學習錯誤，並且在發生意外之前預計和控制電弧傷害。

AFHA由四種不同的步驟組成：

步驟 1. 系統模組化

收集所有系統的資料，設備廠房正常運作下的所有數據。

步驟2. 數據輸入

輸入所有的資料數據到AFHA軟體，電流藍圖將會幫助你了解。基本上第一跟第二步驟就佔了所有四步驟三分之二的時間。

步驟3. 分析

以下有幾種不同的方式分析先前的資料數據：

- 短路電流分析

在所有的結點做短路電流分析，例如如果所有電阻無效，總共多少的電流會在系統中發生。

- 保護裝置分析

分析電熔以及斷路器，以確保當短路電流發生時保護裝置可以打開。

- 協調分析

當系統中有部分失靈時，分析系統可以多快速的找出並協調解決問題。

- 事故能量計算

利用AFHA程式計算當電弧發生時，多少的電流會立即發生。

步驟4. 報告

報告中通常包含五個部分

- 已整理組織好的資料數據

- 保護裝置功率分析

- 電流瞬間發生的計算

- 工程人員建議需要改進的事項

- 將儀器上貼上需要警告的標誌

AFHA潛在的錯誤：

- 太過於專注在高壓電流。大部分意外常發生在低壓電流的工程上，因為大部分的公司對高壓電流的工程有嚴密的安全措施，而忽略了低壓電流的潛在危險。

b.建造一個系統程式是專注在所有適用於所有電弧傷害的，而不是只專注於在不同(高)電壓的等級。

c.當瞬間電流的發生降低到一定程度時就停止繼續分析，應該要繼續分析及控制。

d.直接接受電腦分析後的成果，而沒有去思考或研討是否是合理的成果。

戊、利用安全觀察預測及預防工作傷害的發生

主講者：Barry Nelson

Chief Executive Officer

DBO2 Inc.   Redwood City, CA

本項檢討會中探討如何根據安全觀察並且藉由發展一個評分的方式，定義出哪些地方對員工是高風險或安全的工作場所。

在安全觀察資料搜查中，主要來自12個不同的客戶提供他們的視察，1424個不同地點的觀察及損失資料(Loss，有意外發生時的損失)。總共收集了超過一千萬條的觀察資料，其中包括了一百萬的觀察結果是不安全。對此給予一到一千的評分，越危險的地點指數越高，越安全的地點單指數越低。從資料數據收集的角度來說，不是每個審查清單都是一模一樣的，但是所有都控制在不安全行為或環境的因素。

由分組歸類並且測試多種不同交錯因素目錄，其中包含時間、不安全因素觀察、安全因素觀察和審查人員。下列圖表範例出多種不同需要測試的因素：

| Safety Variables |
| --- |
| Total Inspections Per Month Safe Observations in Month One | Monthly Total of Safe Observations Percent of Observations Done in the AM |
| Monthly Total of High Severity Observations | Sites for the Same Company |
| Average Percent of Items Inspected on Other | Housekeeping Open Issues Corrected Monthly |
| Monthly Total of Unsafe Observations | Monthly Average Number of Fall Protection |
| Changes in Total Unsafe Observations in a Month | Safe Observations in Month One-Amount of Change |
| Issues on Other Sites for the Same Company | Inspections Collected in a Month |
| Total Number of Fall Protection Issues | Changes in the Average Number of Total |
| Corrected Monthly | Average Number of Unsafe Housekeeping |
| Percentage of Sub Categories Inspected | Weighted Moving Average of Inspection Totals |

Exhibit 1.安全審查清單範例

由於無法藉由單一的因素，作有力的預期未來意外或傷害的發生，接下來，依照收集的資料數據發展一個預計損失(意外發生時)的模型。下面是對大約一千個不同地點分析之後，得出對損失比率的摘要：

下列幾點是高分數者(較高風險發生意外)一些共通的特徵：

- 較少的人參予檢視或觀察的過程

- 觀察到有較多的低級或中級嚴重不安全的行為或環境

- 有較多關於清潔工作或防墜保護的不安全行為

- 介於安全專業和不安全專業中有較大的差異變動

在處理這些每樣都具有不同意義的資料數據時，設計了一種方法去測量並控制資料數據的品質。與其擔心不相信這些不好的數據(明顯不符事實的數據)，演講者利用這些數據在不同的地方，發展一個未來潛在風險發生的指標。

大致上來說，如參予越多安全專業和不安全專業的檢視過程，越能夠防止意外的發生。所有非常不安全的行為都需要被仔細的查閱過。當有損失時，防墜保護措施跟清潔工作兩項目錄，是要特別去檢視的。

己、辨認重大危害的技巧

主講者：David F. Coble， MS，CSP

President

Coble, Taylor & Jones Safety Associates

Cary, NC

什麼時候可以察覺到危害的發生?有三個機會去查覺危害的發生：

- 在危害發生前：在計畫、設計或準備階段就認知到危害發生的可能。

- 在潛在危害發生期間：在工作、任務或操作已經開始，但在危害發生前就認知到。

- 在危害發生後：發生意外傷害後才認知到危害的存在。

下列幾點是最有效認知潛在危害的技巧方法：

- 多項步驟計畫過程.

這項技巧使用在危害發生之前。每一項任務、工作、活動都需要事先計畫及組織。

- 使用前分析.

這項技巧是使用在危害發生之前。預先使用分析適用於新的個人防護具、新的工業衛生取樣儀器或新的工具或設備零件。

- 檢閱藍圖.

這項技巧使用在危害發生之前或施工期間。安全和健康相關事項，必須在工程施行前仔細檢閱藍圖。

- 工作許可.

這項技巧使用在工作或任務開始之前，將所有要執行的事項寫下許可清單，要求施工者逐一確認清單，以確認危害事項不會被忽略。

- 安衛管理系統檢點.

這項技巧使用在危害發生之前、潛在危害發生期間或發生危害之後。審核時應該要發掘在訓練、巡視、政策、醫療監督等等的不足。

- 設備檢查

這項技巧用在設備使用之前。檢視跟訓練的工作可以增加在使用儀器設備之前，發現潛在危害的機會。

- 十秒的定點觀察

這項技巧應用在潛在危害發生期間。基本上，檢視者選取一個位置做十秒的定點觀察。選定一個固定的點，觀察並紀錄四周所進行的工程、施工者的活動、環境等，觀察其中是否有潛在危害因素的存在。

- 製作有影響之圖面

這項技巧可以應用在任何時間，但最好使用在危害發生前或任務操作開始前。將工作的環境畫下來，包括週邊的地區，如果需要的話。檢視看看地圖每一個操作點到另一個是否有危害發生的因素存在或相關連。

- 視線外之督察.

這項技巧應用在潛在危害發生期間。基本上檢視者去找出表面看不到的潛在危害，例如關閉的櫃子、抽屜或機房的管線裡。

- 員工建議事項

這項技巧可以應用在任何時間。需要正式的規律條約去對潛在的危害做報告，另外，有些員工傾向於不具名的報告危害相關的事件。

- 危害操作之研究

這項技巧可以應用在任何時間。每項化工製程都可以從這項檢視方法得到好處。這項檢視的目的是，藉由檢視不適當的程序、設備、員工訓練、管理或維修系統，去預防或減低災難發生的結果，如毒氣的釋放、化學反應、易燃物或爆炸性化學原料。

- 走動管理

這項技巧應用在操作期間當潛在危害存在時。基本上檢視者就由跟員工或操作人員的互談中，去發掘尋出潛在的危害。

- 意外事件分析.

這項技巧通常應用在危害發生之後，當造成有害事件、受傷、疾病或資產損壞時。亦稱做事故調查(Accident Investigation)。

- 有感受之服務

這項技巧可以應用在任何時間。通常組織中的安全及健康管理系統分為三部分：1.你認為應該要紀錄進安全手冊的事。2.你認為你在工作環境中擁有的。3.你已經在環境中擁有了。此項目標是要將三個不同的部份達到相同的水準。

- 變更管理

這項技巧通常用於過程之中或之後，部分的零件、機器、或工具在任務開始後需要被改變。這要去分析做改變之後，有那些潛在危害因素會產生，例如錯誤的閥件、漏電斷路器，材質不正確之管線，不適用的手套或不適合的梯子等等。

管理識別危害發生的方法，必須要協調、領導和控制。這裡有五個步驟去建立這個管理系統：

    - 準備一個清單包含所有已運用在組織中，已知危害辨識的技巧。

    - 利用巡視觀察、員工訪談、事故報告、OSHA 300、其他醫療紀錄和自己擁有工作方面的知識，去決定是否有適當的方法可以為每一項任務、工作或操作，分辨和分析潛在危害發的發生。

    - 決定誰將使用這些辨識危害發生的技巧，確認他們有被授與足夠的訓練和教育，以適當充分的使用這些技能。

    - 施行系統紀錄或整理所有關於危害的觀察的紀錄，追蹤且分析每一樣發現的危害紀錄。

    - 確認辨識危害發生的管理系統要每年審核。

庚、工作場所安全與衛生準則的世界趨勢

主講者：Kathy A Seabrook CSP , CMIOSH (UK)

Global Solutions, Inc. /Global Solutions International Ltd. (UK)

Walton on Thames, UK

現階段，安全與衛生的一些主要關鍵議題，包含的趨勢挑戰：

- 化學物品的管理：歐聯和亞洲領導潮流

- 政府管制，執行領導者與工作環境的安全與衛生

- 傳染病預防

- 中國之危害物管理

- 印度之競爭趨勢及機會

- 在地球村的安全—一種商業資源

- OHSAS 18001

A. 化學物品的管理：歐聯和亞洲領導潮流

歐聯持續不斷的發展擴張他們引導全球的環境安全及衛生準則及條款。目前在化學品管理裡主要準則是：Registration， Evaluation and Authorization of Chemicals (REACH)， Restriction of Hazardous Substances (RoHS) and Waste Electronic and Electrical Equipment (WEEE)。基本上，RoHS和WEEE準則主要是去除或限制有害的物質使用在產品或零件上。化學品和非化學產品的生產商和進口商都面臨著詮釋 REACH的挑戰，去生產或進口他們的產品進入歐洲。

日本、大陸和韓國已經擁有或正在執行像RoHS類型的準則，去限制特定的物品和特定物質中原料濃度的最小限制。日本類似RoHS的準則和韓國正在草編的準則是相似的領域，然而，卻跟歐聯和中國的RoHS不同。所以全球的電子的生產商，供應商和進口商都預期這些準則可以協調一致。

- 政府管制，執行領導者與工作環境的安全與衛生

以往工安事件發生後，公司需要檢討事件發生的原因、重新規劃改進以免錯誤再次發生。大致上來說公司只需要加強控管並花費成本去改進。但現在政府加強對公司安全、領導者的監控，工安危害事件的發生會大大降低公司的信譽。公司聲譽風險的管理，除了財務和管理風險之外，現在安全及衛生的管理也是主要趨勢之一了。

- 傳染病預防

許多公司和政府機關都在持續緩慢的規劃、測試和執行傳染病預防計畫。如果你的公司還沒開始規劃傳染病預防計畫，US Center for Disease Control (CDC) 發行了一個很好的核對清單可以參考。

Business Pandemic Influenza Planning website from the Center for Disease Control:

<http://www.pandemicflu.gov/plan/pdf/businesschecklist.pdf>

美國OSHA也出版了一份文件叫：Guidance on Preparing Workplaces for an Influenza Pandemic. 可由下列網站查詢: <http://www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=NEWS_RELEASES&p_id=13698>

- 中國

現在許多工廠都往大陸內陸地區拓展，建立起內陸系統去利用低成本和有技能的員工。鑒於越來越多的工廠發展，代表著越來越多生生產商/供應商在發展科技產業之前，應需要安全與衛生風險問題的管理。

中國已採RoHS類型的準則，其跨國公司中主要關注於這些約束條款將會如何發展和哪些地方將會不同於歐洲現有的條款。試圖使用監管中國和美國標準條款的跨國公司，可以參照Standards Portal.org。

- 印度

印度仍是全球經濟成長最快速的國家之一。因為成本較低和一定教育水準的員工，公司產業持續的向印度繁榮發展。安全與衛生方面來說，印度已經有施行的條約規範，但是強迫施行的條款常常不一致。

- 在地球村的安全

歐洲的一組織，Institution of Occupational Safety and Health中的國際特別小組對企業組織發行了一個線上指南準則。主要分成兩部分，一是Safety in the Global Village：確保員工在海外的安全與健康。其中包含一個簡易的活動計畫和核對清單，以協助評估跨國員工的旅遊風險。另一個是較個人化的性質：Your guide to safety international travel.主要是針對員工旅遊前、旅遊中和旅遊後核對清單並給予建議。

- OHSAS 18001

現在British Standards Institute正在修改第二版本的Occupational Health and Safety Assessment Series (OHSAS) 18001，並預計在大陸上海舉行研討會和出版的議題。現階段，美國、歐洲、英國、澳洲、中國、日本、韓國、芬蘭和加拿大持續的利用科技資訊，跟發展和正在發展的世界各國分享他們現有的安全與衛生政策。

（三）安全衛生器材展覽

ASSE於6月24日至26日為期三天，舉辦安全衛生器材展覽會，來自世界各地工業安全衛生廠商展示相關產品或服務，依據展示產品佔地多寡之需要，分別租用大小不同之面積，在展示產品方面，大抵包括個人防護具如安全帽、安全鞋、安全眼鏡、防護衣、手套、呼吸防護具、耳塞、反光帶警示背心等，消防器材、逃生器具、適合人體工學的手工具諸、施工架組裝、藥品及急救器材、氣體測試儀器、道路工作警示裝置、安全衛生教育訓練、書籍及雜誌、安全管理資訊系統等，其中仍以個人防護具為參展大宗

本次展覽會現場超過400家製造廠家或代理商之攤位展示。各廠商為吸引人員與會，現場均有專人示範解說，並提供型錄文宣資料、產品介紹光碟片、試用品等，另外參加人員如對參展產品有興趣時，亦可將識別證交與廠商複製條碼，會後廠商便會寄上產品目錄或以電子郵件提供相關訊息。

五、心得與建議:

（一）美國安全工程師協會的年會的確具有相當的規模，短短一週的時間舉辦了博覽會、225 場技術性研討會及44場訓練課程。年會的整體籌備與規劃相當繁複，一年前即開始籌備包括徵稿、聘請講座、場地租用、住宿與交通安排等相關事宜，皆相當完善，終於使會議順利進行，確實是用盡心思與花費大筆費用。我國在辦理相關國際性會議上在對與會者之交通服務似不如ASSE安排定時定點、多路線且頻繁之專車服務。

（二）由於各項會議內容皆無書面資料，如想要資料須事後向其購置錄音片，此係該協會之經費完全需自行籌劃，此亦為其籌經費方式。

（三）對於交通安全，此次年會亦有相當多之研討會，顯示此項已是一個不亞於工廠安全之項目，本公司近年加強對於交通安全之宣導，即是因交通事故頻率高於工作職災而採行對策。

(四)  美國人呼籲要關心逐漸老化的中年員工，並給予再就業及教育的機會，與我國要淘汰老人重用年輕人的觀念大不相同。在此次之會場，服務人員皆是中老年人，顯示其對中老年人照顧確實落實。本公司人力結構目前也出現老化及人才斷層的現象，希望公司在鼓勵專案退休的同時也能重視他們長期所累積的經驗。目前部分單位雇用退休同仁當監造即係藉重其過去的專業經驗，惟僅為少數，希望能擴展至其他層面，使有各類專長之退休同仁能再為公司做另類的貢獻。

(五) 美國的安衛法規有些定義非常清楚，但亦有未規範或未詳盡之情形，引用法規需切合方不致造成誤解，造成浪費資源或失去防護功能，甚至發生嚴重後果。此種情況在國內之安衛法規亦有類似情形，如主管機關對法規之解釋與引用，明顯超過母法，常造成業界之困擾。

（六）在6月26日之午餐時間，會場因一件誤信號引起火警警報作動，當火警警報響起，所有建築物內包含正在用餐人員逾千人，皆順序由各樓層下至地面層，並離開建築物至室外空地觀察情況，室內看不到一個人，約五分鐘後警車及消防車到達，經詳查確認為虛驚，警車於警報後約15分廣播實際情況，此時所有在室外之人員再依序返回會場餐廳，繼續享用未完之午餐。此事顯示所有與會者及服務人員對火警事故之應變皆遵守其要求，實施一場完美的無預警應變演習。

（七）由於網路之普及，會場亦設置約二十部網路電腦供與會人員免費使用，在使用者付費之歐美社會，實為難得，正因如此，會期中每部電腦皆無閒置時刻，亦顯示與會人員平常亦須藉其處理事務。

（八）目前全球對於安全衛生法規之制訂，歐盟仍處於領先地位，對於環境保護，利用可回收或自然分解之材質為產品之法規要求，利用貿易限制之手段來達成保護環境之目的。此亦為全球永續發展之作法。

（九）本公司對於安全衛生體系之建置與實施，自早期之製程安全管理（PSM）、ISRS安全評估系統、BS 8800，至目前之OSAS 18001，這些安全衛生系統差異性不大，如要達成零災害及零事故之目標，惟有賴落實執行，這亦是安環處對安衛管理體系依PDCA之方式嚴格執行之理由。

附件

ASSE年會會場外觀及大廳

博覽會場

研討會會場

火警警報所有人員撤出至建築物外

研討會及專業課程

Monday, June 25, 2007

| 10:45am - 11:45am |
| --- |
| 501 | Using Project Management and Consulting Tools | 512 | Beyond Compliance: Breaking Through to the Next Level of H, S & E Excellence |
| 502 | The Potomac Crossing | 513 | The Case for Inherent Safety: A Review of the Principles of Inherent Safety and Case Studies of Tragedies |
| 503 | Egress Exit Technology Opens in New York City | 514 | Strategic Planning in Safety |
| 504 | Environmental Compliance for the Safety Manager | 515 | Introduction to Fireground Strategies and Tactics for the Non-Firefighter Safety Professional - Understanding the Capabilities and Limitations of the Fire Department |
| 505 | An Introduction to Lean Principles for Ergonomists and Engineers for the Healthcare Industry | 516 | Implementing Z359.1 - Managed Fall Protection Program Standard: Newer, Better Fall Protection |
| 506 | Potential Effects of Fungal Contamination on Health | 517 | Using the Table Top Exercise Technique to Improve Your Organization's Emergency Response Preparedness |
| 507 | People-Based Leadership: Gaining and Sustaining Engagement in Occupational Safety | 518 | Ignorance Is No Excuse - Combustion Systems Standards and Codes 101 |
| 508 | Can We Be Both Safe and Sorry? When Safety Programs Reach Saturation | 519 | When Driver Safety Fails - Then What? Vehicular Accident Analysis: The Big Picture |
| 509 | Introduction to OSHA's New VPP for Construction Program | 520 | Fundamentals of SH&E - Overview of Regulatory Compliance 101A |
| 510 | Effective Methods of Legal Risk Management for Safety and Health Professionals | RT01 | Sponsored by the Construction Practice Specialty - Key Issue Roundtable #1: Challenges of Managing Multi-employer Worksites |
| 511 | Effective Safety Audits & Plans |  |  |
| 3:00pm - 4:15pm |
| 526 | Benefits of Participation in the STS (Safety Trained Supervisor) Program | 537 | Controlling Human Error in Complex Manufacturing Systems |
| 527 | Indoor Air Quality Issues During Construction and Renovation Projects | 538 | Motivating Employees for Safety Improvement: Reaching from the Shop Floor to the Boardroom |
| 528 | Planning for the Worst Case Scenario: Katrina as a Case Study for Emergency Response Planning and Recovery | 539 | When the Safety System Fails the Worker: Did We Do Our Job? |
| 529 | SPCC - Preventing the Sheen | 540 | Implementing and Developing Industry Standards in the Design of Agricultural Safety Systems |
| 530 | When the Rubber Hits the Road: Lessons from the Goodyear Tire & Rubber Company's Global Ergonomics Process | 541 | Introduction to Basic Scaffold Safety |
| 531 | Global IH Programs | 542 | Hydrogen Sulfide, the ASSE/ANSI Z390.1-2006 Standard and the Impact of the Latest Revisions |
| 532 | The Myths of Safety | 543 | Confessions of a Business Driver: Understanding Driver Safety Risks |
| 533 | Beyond Rhetoric - How to Arrest the Public Sector’s Very High Injury Rates by Combining Actuarial Analysis with Safety Management | 544 | You Cannot Get Lean Without Safety |
| 534 | Application of the United States Army Accident Causation Model During Combat Operations in Iraq | SP01 | Culture Barriers to Safety / Barreras Culturales Hacia la Seguridad |
| 535 | What Have You Done for Me Lately? | RT02 | Sponsored by the Consultants Practice Specialty - Key Issue Roundtable #2: Growing Your Consulting Business |
| 536 | The Value of OSHA's Voluntary Protection Program (VPP) |  |  |
| 4:30pm – 5:30pm |
| 551 | Achieve Your Safety Outcomes with Effective Communication, Motivation & Presentation Techniques | 561 | Lean Six Sigma - Innovative Safety Management |
| 552 | Multi-Employer Job Sites - The Need to Effectively Pre-Qualify Contractors | 562 | Managing Diversity for Safety, Health & Environmental Excellence |
| 553 | Emergency Preparedness for All Industries… Yes, You Too | 563 | Lessons From Eladio (Breaking the Cycle of Management by Luck) |
| 554 | Visual Ergonomics in the Workplace | 564 | The SH&E Performance Consulting Partnership at Canadian National Railway: Engaging System-Wide Stakeholders to Transform Safety Culture |
| 555 | Birdflu Pandemic Planning, Preparedness and Response | 565 | Storage Occupancies - Are Your Sprinkliers Up to the Task? |
| 556 | Emerging Issues for Professional Practice in Healthcare | 566 | Permit Required Confined Spaces - A Workshop for Proper Classification of Spaces |
| 557 | Briefing 2007: Global Trends in Workplace Safety and Health | 567 | ANSI/ASSE Z690: Results of the Writing Project and Canvass |
| 558 | OSHA Construction Update | 568 | REP: Utilizing the Rational/Emotional/Physical Approach for Effective Employee Training |
| 559 | Lift Truck Safety in Distribution Environment - A Behavioral Approach to OSHA 1910.178 | 569 | Advancing Your Career in Safety |
| 560 | Enterprise Risk Management for the Safety Professional | RT03 | Sponsored by the Environmental Practice Specialty - Key Issue Roundtable #3: Wearing Two Hats - Balancing Environmental and Safety Responsibilities and Priorities |

Tuesday, June 26, 2007

| 10:45am - 12:00pm |
| --- |
| 601 | Making Your Consulting Practice Work With an Effective Business Plan | 612 | Techniques for Hazard Recognition |
| 602 | Traffic Control Safety (Meeting the FHWA Minimums Is Not Enough) | 613 | Culture is Quantifiable |
| 603 | Environmental, Health and Safety Concerns During Facility Decommissioning | 614 | Boosting Safety With An Aging Workforce |
| 604 | Soft Tissue Injuries: Questions Every Manager Should Ask to Get to the Heart of the Issues | 615 | Why Is Mechanical Integrity So Tough? |
| 605 | Complying With the Hexavalent Chromium Standard | 616 | ANSI Z87.1 - What's Coming in 2008 |
| 606 | Flight Safety Management "Best Practices" - What Can We Learn From Them | 617 | Drawing the Big Picture for Slip, Trip, and Fall Prevention |
| 607 | Global Safety: Emerging Trends and Challenges | 618 | Tell Me a Story: Using Stories to Improve Occupational Safety Training |
| 608 | Approaches to Ensuring Mine Safety in the Wake of Recent Disasters | 619 | Developing a Quality Contractor Prequalification Program |
| 609 | OSHA Enforcement Update | 620 | Fundamentals of SH&E - Hazard Identification and Control 101B |
| 610 | High-Stakes Communications and the Media: What Environment, Health, and Safety Professionals Need to Know | RT04 | Sponsored by the Transportation Practice Specialty - Key Issue Roundtable #4: Port Security |
| 611 | Creating a Healthy Workplace Culture |  |  |
| 3:15pm - 4:15pm |
| 626 | Ethics Awareness for the Practicing Safety Professional - What Can We Learn From the Engineering Profession | 637 | Lean Manufacturing: Managing Safety & Ergonomics in a Lean Environment |
| 627 | Critical Issues in the Development and Implementation of Construction and Demolition Standards (ANSI/ASSE A10 Standards) | 638 | Helping Safety Managers Make Project Decisions in the Workplace: The Weighted Scoring Decision Making Approach |
| 628 | EMS - A Safety Emergency | 639 | How to Move from Excellent to Extraordinary Safety Performance |
| 629 | Lead-Based Paint Initiatives - OSHA & EPA Update | 640 | Partnering to Move Research into Practice: Safety and Health in Nanotechnology Manufacturing |
| 630 | ADA and EEOC - Compliant Functional Testing of Employees: A Defensive Hiring Method to Reduce Injuries and Increase Productivity | 641 | Fall Protection: Certified vs. Non-Certified Anchorages |
| 631 | Safe Patient Handling: Strategies, Solutions and Challenges for Success | 642 | Even More… Wild, Wacky, and Highly Effective Training |
| 632 | Human Performance Improvement | 643 | Trucking Industry Best Practices |
| 633 | OSHA Construction Health Cases | 644 | Biomechanics for Risk Managers - Slip, Trip & Fall Injuries |
| 634 | Assessing Opportunities for Inherent Safety in Industrial Systems | SP02 | New Generation of Safety Performance Metrics / Nueva Generacion de Metricas de Seguridad |
| 635 | Bridging the Gap Between Liability Loss Control and Prevention and Occupational Safety and Health Management Practices in Addressing Liability Related Losses | RT05 | Sponsored by the International Practice Specialty - Key Issue Roundtable #5: Developing and Implementing Global SH&E Metrics |
| 636 | Safety and Health Integration: Understanding Systems Thinking to More Effectively Implement ANSI Z10 |  |  |
| 4:30pm – 5:30pm |
| 651 | How to Communicate With and Empower Your Spanish-Speaking Workforce | 662 | Does Superior Performance in Occupational Safety Really Affect Business Performance?: A Search For Answers |
| 652 | I-9 Forms, Legislation and eSolutions | 663 | Accident Prone or Unfit for Duty? Assessing Fitness-for-Duty in a Medical-Legal Framework |
| 653 | The 25 Greatest Hazards of Excavation | 664 | Management-Based Safety... Leading Your Organization to New Heights |
| 654 | Confined Space Emergencies | 665 | Achieving Sustainable World Class Safety Performance and Culture |
| 655 | Taking Safety Home - Protecting the Whole Worker | 666 | Mitigating Soil-Gas Vapor Intrusion in New and / or Existing Structures |
| 656 | Hazardous Materials Management Considerations in Healthcare | 667 | The HAZWOPER Regulation Simplified |
| 657 | Culture Change: A Breakthrough in Safety Performance | 668 | Warm Up to Wrap Up: Twenty One Great Safety Training Activities |
| 658 | Diesel Particulate Matter Exposure in Mining | 669 | New Developments in Fall Protection Planning |
| 659 | OSHA Construction Safety Cases | 670 | Fundamentals of SH&E - Workplace Health 101C |
| 660 | Safety vs. Risk Management - Can’t We All Just Get Along? | RT06 | Sponsored by the Academics Practice Specialty - Key Issue Roundtable #6: What Should Colleges and Universities Teach? What do Employers Want Their Entry-Level Occupational Safety Graduates to Know? |
| 661 | Emerging Issues Survey "What's Up Doc?" |  |  |

Wednesday, June 27, 2007

| 7:45am - 9:00am |
| --- |
| 701 | Presenting Safety as a Positive Experience | 712 | Accurate Accident Investigations: Just the Facts |
| 702 | First Things First - "Pre-Construction" Safety Issues | 713 | 3 Attributes to World Class Safety |
| 703 | @ Your Service: Business Continuity Planning, Surviving Katrina | 714 | Determining "What Works" in Safety and Health |
| 704 | ISO 14000/14000/14XXX An Update on What is Happening | 715 | Procedures for Managing the Incident Investigation After Serious and Catastrophic Incidents |
| 705 | Development of an Ergonomic Surveillance Tool (EST) for Work-Related Musculoskeletal Disorders (WMSDs) | 716 | Reducing Slip, Trip and Fall Accidents on Walkways and Stairs |
| 706 | Two Sampling Methods to Enhance the Safety Professional's Air Monitoring Capabilities | 717 | Fire Suppression Considerations for Storage Facilities |
| 707 | What Injury-Free Workers Can Teach Us | 718 | The High Risk Driver - What to Look for and How to Know |
| 708 | Application of the Process Safety Management Standard in Canada | 719 | Using Your Safety Observations to Predict and Prevent Worksite Injuries |
| 709 | OSHA Emergency Preparedness Update | 720 | Fundamentals of SH&E - Basic Risk Management 101D |
| 710 | Achieving World Class Safety Performance Through Metrics | SP03 | Intercultural Diversity - An Integrated Approach to Cultural Diversity in the Workplace / Diversidad Intercultural - Un Enfoque Integral a la Diversidad Cultural en el Trabajo |
| 711 | A Primer in Risk Management for the Safety Professional | RT07 | Sponsored by the Management Practice Specialty - Key Issue Roundtable #7: Maximizing Safety Performance Through Employee Involvement and Empowerment |
| 9:15am - 10:30am |
| 721 | Gaining Commitment Through Influencing and Collaborating With Others | 731 | Forecasting Incident Rates Using Artificial Intelligence |
| 722 | Obtaining an Accredited SH&E Related Degree Through Online Learning | 732 | Contractor Safety Networks in the Petroleum Industry: A Case Study of Effectiveness |
| 723 | Construction Safety Forum | 733 | Out of the Dark Ages and Into the Light - New Ways of Measuring Your Safety Program's Success |
| 724 | Evacuation! Understanding Behavioral Aspects of Emergency Response in Individuals | 734 | VPP: Leaders in Safety and Health Excellence |
| 725 | Environmental Management Systems: From Burden to Opportunity | 735 | Do You Have a Fatal Fall Protection Program? |
| 726 | The Boston Globe's Best in Class Ergonomics Program | 736 | Critical Controls - New Imperatives for Industry |
| 727 | Contemporary Model of Behavior Based Safety | 737 | Communicating Health and Safety Issues in Training: From Basics to Board Level |
| 728 | Road and Sign Liability Issues in the Public Sector | 738 | A Fearless Look at What Really Causes Accidental Injuries and Fatalities |
| 729 | Overview of OSHA's Hispanic Outreach Initiatives | 739 | ASSE Government Affairs Committee Update |
| 730 | Integrating a Balanced Scorecard Approach to Risk Management in an OHSAS 18000/ANSI Z 10 Management System | RT08 | Sponsored by the Industrial Hygiene Practice Specialty - Key Issue Roundtable #8: Hexavalent Chromium |
| 11:00am - 12:00pm |
| 741 | International Professional Certifications | 752 | Assessing Safety Program Effectiveness |
| 742 | Craft-Specific Injury Prevention Programs: A Multi-Faceted Approach to Reducing Costs Associated with Musculoskeletal Injuries | 753 | Leading Measures for Improving Safety Performance |
| 743 | Emergency Response Planning: New York City Mandate - A Case Study | 754 | An Electrical Arc-Flash Hazard Analysis Primer: How the Proper Use of Engineering Controls can Significantly Reduce the Severity of Electrical Burn Injuries in Your Facility |
| 744 | Vapor Intrusion: A Growing Environmental Challenge | 755 | Enhancing Your Safety Program with Safety Signs |
| 745 | Managing Safety and Health - Latex Products | 756 | Motivational Secrets of the Best EH&S Trainers (How to Train in Safety More Effectively) |
| 746 | C.A.S.T. For $ucce$$ | 757 | A Photo Is Worth 1,000 Words - Or $30,000 |
| 747 | Made In China - Safely | 758 | Ergonomics Risk Assessment: Maximizing the Value of a Physical Demands Analysis |
| 748 | Process Safety Management Issues During Mergers and Acquisitions | 759 | The Use of Fall Protection Anchorage Systems in Building Construction |
| 749 | What Safety Professionals Know (and Don't Know) About Older Workers | 760 | Fundamentals of SH&E - Environment 101E |
| 750 | Job Demands Analysis: Defining the Physical Demands of the Work for Post-Offer and Return-to-Work Functional Testing | RT09 | Sponsored by the Risk Management/Insurance Practice Specialty - Key Issue Roundtable #9: How Can the Safety Professional Remain Engaged Within Their Organization's Risk Management Process |
| 751 | @ At Your Service - Golf & Resorts - Cutting Edge Safety |  |  |
| 1:45pm - 3:00pm |
| 761 | The Career Significance of the Safety Through Design Provisions in Z10 | 770 | Corporate Sustainability: Leading from the EHS Perspective |
| 762 | Unearthing TREX: What This Past Project Can Teach Us About Modern Construction Safety | 771 | Planning and Conducting Comprehensive EHS Audits - A Critical Component of Your Global Compliance Programs |
| 763 | Setting Up & Managing a Medical Emergency Response (MERT) Team | 772 | A Motivational Safety System: Moving Toward World Class Performance |
| 764 | Ergonomics Update: Why Women Are at Greater Risk? | 773 | Electrostatic Hazards Associated with Liquid & Powder Processing |
| 765 | HIV / AIDS: A Journey to Employee Awareness and Action | 774 | Update - Myths and Misconceptions in Fall Protection |
| 766 | Healthcare Safety Leadership: Back to Basics | 775 | Laser Safety: Corporate Responsibility, Training & Hazard Analysis |
| 767 | Are Your Company's Profits Slipping Through the Cracks? | 776 | Games for Trainers! |
| 768 | Post Injury Management: Techniques to Reduce Workers' Compensation Costs | 777 | Implementing a Machine Hazard Assessment Program |
| 769 | Making the Choice for Safety Is Always the Right Choice: Evaluating Service Provider ESH Performance in Your Workplace | 778 | Fundamentals of SH&E – Basic Safety Management 101F |
|  |  | RT10 | Sponsored by the Healthcare Practice Specialty - Key Issue Roundtable #10: How Are The SH&E Professionals in the Healthcare Industry Preparing to Deal With Pandemic Illness - Community Issues, Resources, Personal Protective Equipment, Medications, Food/Water, and Other Problem Areas? |
| 3:15pm - 4:15pm |
| 781 | Identity Theft - Identification, Detection and Prevention | 790 | Executive Safety Committees - Common Pitfalls and Implementation Considerations |
| 782 | Implementing a Behavioral Safety Process on Construction Projects | 791 | Mastering the 5 Principles and 10 Key Elements of a Successful Safety Process |
| 783 | Safety and Health Guidelines for Volunteers to Disaster Sites | 792 | Using Safety Culture Assessments to Develop More Effective Safety Interventions |
| 784 | Macroergonomics - A Systems Approach to Safety Excellence | 793 | Route Sales, Service, & Delivery: Safety "No-Man's Land" |
| 785 | Evaluation of Laboratory Fume Hood in a Volume Generating Process | 794 | Safety Business Plan |
| 786 | The Impact of Globalization on Occupational Safety and Health | 795 | Implementing An Electrical Safety Program Using NFPA 70E |
| 787 | Hazmat Shipping: Must Know Issues for the SH&E Manager | 796 | Horizontal Lifelines: Methods and Pitfalls |
| 788 | A Tool for Assessing the Benefit / Cost of Risk Reduction Alternatives | 797 | Green Beans and Ice Cream: The Recipe for Employee Behavior Change |
| 789 | In the Path of Disaster - Run, Hide or Prepare? | SP04 | Why the Latino's Workforce has the Highest Rate in Death and Injuries at Work? / ¿Por qué los trabajadores latinos tienen los índices más altos de accidenatbilidad y muertes en el trabajo? |

# Pre-Conference Seminars

|  | Seminar | Thursday, June 21 | Friday, June 22 | Saturday, June 23 | Sunday, June 24 |
| --- | --- | --- | --- | --- | --- |
| 111 | Math Review for Certification Exams | x |  |  |  |
| 231 | ASP Exam Preparation Workshop |  | x | x | x |
| 232 | CSP Exam Preparation Workshop |  | x | x | x |
| 233 | Safety Management I |  | x | x | x |
| 234 | Corporate Safety Management |  | x | x | x |
| 235 | Managing the Business Aspects of Safety |  | x | x | x |
| 236 | Risk Management for the Safety Professional |  | x | x | x |
| 311 | The Business of Safety |  |  | x |  |
| 312 | Confined Space Evaluation, Entry and Rescue |  |  | x |  |
| 313 | Nanotechnology: Being Prepared for the Next Big Thing |  |  | x |  |
| 314 | Advanced Fire Protection |  |  | x |  |
| 321 | Techniques for Hazard Recognition |  |  | x | x |
| 322 | Basic Electrical Safety with Application of NFPA 70E |  |  | x | x |
| 323 | Incident Investigation and Root Cause Analysis |  |  | x | x |
| 324 | Global Environmental, Health and Safety Management |  |  | x | x |
| 325 | Return on Health, Safety and Environmental Investment (ROHSEI) |  |  | x | x |
| 411 | The Safety Professional’s Role in Compliance with the Sarbanes-Oxley Act |  |  |  | x |
| 412 | Lockout/Tagout |  |  |  | x |
| 413 | People-Based Safety: The Human Dynamics of Achieving an Injury-Free Workplace |  |  |  | x |
| 414 | Predicting Errors Using Human Performance Measurement Tools |  |  |  | x |
| 415 | Training Supervisors to Become Safety Coaches |  |  |  | x |
| 416 | Building Safety Into the Design |  |  |  | x |
| 417 | Ergonomic Leadership: Motivating and Developing Ergonomic Behavior |  |  |  | x |
| 418 | Managing Safety in a Pandemic |  |  |  | x |
| 419 | Managing Contractor Safety: Implementing an Effective Contractor Safety Program |  |  |  | x |

# Post-Conference Seminars

|  | Seminar | Wednesday, June 27 | Thursday, June 28 | Friday, June 29 | Saturday, June 30 |
| --- | --- | --- | --- | --- | --- |
| 801 | 1/2-day Math Review | x |  |  |  |
| 810 | Auditing Safety and Health Management Systems |  | x |  |  |
| 811 | Principles of Leadership |  | x |  |  |
| 812 | Facilitating Decision-Making in Your Organization |  | x |  |  |
| 813 |  |  | x |  |  |
| 814 | Critical Issues in Construction Safety |  | x |  |  |
| 815 | Creating Safety Training Programs That Work |  | x |  |  |
| 816 | Cost Analysis for Safety and Health Professionals |  | x |  |  |
| 817 | Criminal and Liability Issues Facing the Health and Safety Professional |  | x |  |  |
| 818 | You Don’t Have to Speak Spanish to Communicate with your Spanish-Speaking Workforce |  | x |  |  |
| 819 | Root Cause and Practical Prevention of Strains, Sprains and Pain |  | x |  |  |
| 821 | Safety Management II |  | x | x |  |
| 822 | Management-Based Safety |  | x | x |  |
| 823 | Industrial Hygiene for the Safety Professional |  | x | x |  |
| 831 | ASP Exam Preparation Workshop |  | x | x | x |
| 832 | CSP Exam Preparation Workshop |  | x | x | x |
| 833 | CHST Exam Preparation Workshop |  | x | x | x |
| 834 | CHMM National Overview Course |  | x | x | x |
| 911 | Fall Protection |  |  | x |  |
| 912 | Strategic Planning for Safety Programs |  |  | x |  |