行政院所屬各機關因公出國人員出國報告書

（出國類別：其他）

新船Ｈno.932主機(7RT-flex 96C)廠試報告

服務機關：台灣國際造船股份有限公司

出國人職稱： 九等工程師

姓    名：  陳錫銘

出國地區：韓國釜山

出國期間：97年12月15日至97年12月18日

報告日期：98年02月02日

| 單位主管 | 人事處 | 批 示 |
| --- | --- | --- |
|  |  | □是□否登錄KM平台共享專區 |

註：送存報告應由出國人員自返國之日起二個月內提出，依行政程序併陳逐級審核。

壹、前言

依建造合約，主機於製造完成後需於主機廠進行測試主機各項性能。於廠試期間應核對廠家是否依採購規範(POS)製造主機，對於船廠與船東之審圖意見，廠家是否已反映並執行，並於廠試期間即時發現缺失及檢查有無震動、漏油、異音、高溫等現象並要求廠家配合修改，儘量避免主機運抵船廠後增加船廠之修改，以確保建造日程。

貳、廠試

N932船主機7RT-flex 96C(MCR:54460ps x 102rpm)為韓國斗山機器(Doosan Engine)廠家所供應，依廠家正式廠試測試時程表可分為(A)Official Shop Test (2008年12月16日)和(B) Overhaul Inspection(2008年12月17日)兩階段進行，除了Peter Dohle公司長駐在Doosan的資深監工Mr. Behrmann外，船東駐船廠辦公室則由Mr.In go參與主機廠試，於Trial Running Test時須檢查有無震動、漏油、異音、高溫等現象；Overhaul Inspection 於主機開放檢查時，檢查各部份有無刮傷、裂痕、剝離、異常磨耗或其他缺點。

(A) Official Shop Test(測試日期為97年12月16日)：

包括下列測試項目及測試結果：

- Safety device confirmation test

        - Thrust pad high temperature: 90.3℃(settling value:90±2℃)

        - Turning gear interlock test：ok

        - Oil mist detector function test for crankcase & F.O. supply unit(including simulation and M/E running)：ok

        - Main L.O. inlet low pressure：4.5bar (settling value:4.4±0.1)

        - Main L.O. inlet low-low pressure：4.1bar (settling value:4.1±0.1)

        - Cylinder C.F.W. inlet low pressure：2.46bar(settling value:2.5±0.1)

        - Exhaust valve spring air low pressure：4.47bar (settling value:4.5±0.1)

        - T/C L.O. inlet low pressure：0.63/0.64 bar (settling value:0.6±0.1)

        - Piston cooling oil inlet differential pressure：0.64~0.66bar (settling value:0.6±0.1)

- Emergency running test at engine side：ok

- Emergency trip test at engine side：ok

- Astern test at no load：ok

- Factory Acceptance test (FAT) for WECS-9520 function check：

        - Protocol & signature:

Engine type: 7RT-flex96C-B,

Hull type: CSBC932

Software version:  31;  Build: 080;   BLV: 1.04

APP CRC value: OXAE27 ;   IMO SW-NO: LN-BE9801

IMO CRC value: OX38B9;   IMO data length: 428

        - Function and failure test:

- Software verification

- Injection rail valve and sensor function

- Exhaust rail valve and sensor function

- Power supply failure FCM-20 and loss of one cylinder

- Correct function of “fuel shut down pilot valve”(ZV7061S) and “fuel shutdown valve” when the engine is running. (This test is usually done as “emergency stop test” during standard shop test Procedure )

- Crank angle bus / sensor failure – crank angle bus wiring

- Engine failure and communication test WECS-9520 safety system

- Load test (Nox measurement at 25%, 50%, 75% and 100% MCR load for Hno.932 engine only)

        - 25% MCR (13615ps x 64.3rpm)：30 minutes

        - 50% MCR (27230ps x 81rpm)：30 minutes

        - 75% MCR (40845ps x 92.7rpm)：30 minutes

        - 90% MCR (49014ps x 98.5rpm)：30 minutes (SFOC measurement witness)

        - 90% MCR (49014ps x 103.8rpm)：30 minutes (include propeller margin)

        - 100% MCR (54460ps x 102rpm)：60 minutes

        - 110% MCR (59906ps x 105.3rpm)：30 minutes

- Governor test：102rpm(103.4rpm(102rpm (51.33 seconds)

- Over speed test：112.4rpm (settling valve：112.2rpm)

- Minimum revolution test：engine speed is 24.5rpm & water brake is 403ton (T/C revolution: 1447/1450rpm)

- One turbocharger cut-off test for Hno.932 engine only：ok

- One cylinder cut-off test for Hno.932 engine only：ok

(B) Overhaul Inspection (visual inspection, 檢驗日期為97年12月17日) ：

1. Crankshaft without lifting from bedplate：Ok

2. No.2 main bearing (shell to be dismantled from engine)：Polishing

3. No.3 crank pin bearing (without dismantling from engine)：Ok

4. No.1 crosshead bearing (ditto)：Ok

5. No.1 crosshead pin and guide shoe (ditto)：Polishing

6. No.1 cylinder liner (inner surface, ditto)：Ok

7. No.1 cylinder cover (combustion surface, dismantled from engine)：Ok

8. No.1 piston complete (dismantled from engine)：Ok

9. Camshaft driving & gear drive (without dismantling from engine)：Ok

參、結論

1. 在出發前，先準備並研讀相關的採購規範、重要機材廠試查核表、由設計提供船廠和船東審圖意見以及廠家的工作圖，事先核對廠家是否已將審圖意見反映到工作圖上，以Hno.932主機而言，船東在審圖與建造階段陸續追加下列部份裝備：

a. Bearing distance (wear ) measurement system (BDMS)

b. Bearing temperature measuring system (BTMS)

c. Water in oil system

d. Cylinder liner wall temperature monitoring system

e. Cylinder pulse jet lubrication system

f. Oil mist detector in supply unit

g. Low load tuning modification( exhaust gas waste gas with pneumatic actuator.

Hno.932系列主機使用新式汽缸潤滑油系統(cylinder pulse jet lubrication system) ，該新式汽缸潤滑油系統由WECS-9520程式直接控制，有較佳潤滑效率，故可大幅節省汽缸油成本，

兩年前本公司建造萬海公司系列船N872/873船使用主機型式SULZER 10RTA96C-B，萬海公司提出追加PLS(汽缸潤滑油系統)，因RTA  TYPE主機沒有COMMON  RAIL 系統 供 PLS 使用，需另外加裝兩部L.O. SERVO PUMP  才能提供高壓作動油供PLS使用。

主機廠家不斷研發新產品，不但節省油品消耗及降低機件磨耗，進而節省維修費用、提升效能是受船公司青睞主要原因。

2. Hno.932船主機廠試在Crank shaft deflection check, Load Running Test, Starting Test, Generator Test, Engine Protecting System, Turning Gear Interlock Test, Engine Side Manoeuvring, Minimum revolution Test, Astern Running Test及Overhaul test等各項性能測試皆能符合合約規範及廠家標準之要求，詳如附件之廠試報告。

3.  配合低負荷運轉有較佳的燃油消耗率表現，Hno.932系列主機由原先標準delta tuning改為low load tuning，燃油霧化器atomizer也配合改變，並加裝exhaust gas waste gate，當主機出力超過85%，exhaust gas waste gate會開啟，5%的排氣會從渦輪增壓機旁通掉，在 WECS 9520程式中，顯示主機85%以上負荷時，exhaust gas waste gate已開啟，T/C排氣溫度趨勢有明顯的改變，證實exhaust gas waste gate已經調校良好。

4. 由廠試結果顯示，在90%負載下的燃油消耗率測量値為129.68 g/BHP/hr，修正到標準狀況下為128.07 g/BHP/hr，此燃油消耗率可以合乎保證燃油消耗率124.0 g/BHP/hr + 5%餘裕的要求。

5. 主機開放檢查時欲抽驗的項目，船東指定抽驗第五缸的活塞、汽缸蓋、缸套、十字頭軸承、導靴、#6主軸承、第3缸曲柄銷、軸承和曲拐軸，檢查項目都良好。

6. Hno.932廠試過程，船東的意見都隨時張貼在機器本體上，且船東有派監工人員常駐在DOOSAN工廠內，所有意見在出廠前會改善完成。

7. 廠試意見如下：

a.FUEL/SPEED MODE 控制對照表須提供在LCP上。

b.GAUGE BOARD 上的閥需掛名牌。

c.十字頭滑油的溫度表需移位。

d.平台未加COAMING。

e.第六缸旁欄杆改正。

f.NO.2 AIR COOLER 固定扣環未裝。

g. 第六缸排氣溫度錶換新

h. TOP BRACING 之撐座的固定孔有誤。

I. 電纜線佈置不當未保護。

j. AIR RECEIVER 的門碰管子。

k.曲拐軸箱的門碰管子。

l. 第六，七缸PISTON UNDER SIDE 檢查門換新。

# Text boxes

RT-flex 主機有common rail 高壓作動油可供PLS 系統使用。

RTA 主機須加裝servo oil pump才能提供高壓作動油供PLS使用。