|  | ASIA–PACIFIC LEGAL METROLOGY FORUM |
| --- | --- |

2009 The Current Development in Chinese Taipei

1. Regulations and technical specifications revision

(1). Technical Regulation of Law enforcement equipment

The accuracy of Law enforcement equipments which have been widely used by Police such as Breath Alcohol Testers and Analyzers, Radar Speedometers, Laser Speedometers and Inductive Loop speedometers have raised public concerns in recent years. Extensive studies on those equipments were conducted by BSMI. Those studies gathered the current metrological controls in other countries, reviewed the current technical regulations against the public’s concern and conducted several testing on those instruments.  According to the findings of these studies, BSMI have been working on revising three technical regulations. The focal points to revise the technical regulation of Breath Alcohol Testers and Analyzers are Influence of Interruption in the Flow of Breath Test, Memory and Residual Effect Test, and Standard Gas with CO2 Test. The focal points to revise the technical regulation of Radar Speedometers are Temperature Test and Horizontal Beam-Width Test. The focal points to revise the technical regulation of Laser Speedometers are Direction of Traveling Vehicle Discriminator Check and Smoothly Moving Target with Saw Tooth Perturbation Check. BSMI also drafted the technical regulation of Inductive Loop speedometers. All the above four technical regulations are already open to public hearings and expectedly to put into force in next year.

(2). The revisions of other technical regulations

With gas price surged dramatically, the consumer incumbent agencies urged BSMI to review the technical regulations of petroleum dispenser. BSMI is revising the Technical Specification for Verification and Inspection of Oil Meters and focus on the testing flow rate.

In response to the request from the manufacturer and in view of the fraud incident happened this year, BSMI is also revising the Technical Specification for Verification and Inspection of Weighing Instruments.

In addition, in view of the fire hazard, BSMI is revising Technical Specification for Verification and Inspection of Electricity Meters. All of these three regulations are also expected to put into force next year as well.

2. E-learning website

In order to provide a training platform for newly metrological technicians, we set up an E-learning website (http://metrology.bsmi.gov.tw). This website also provides necessary information for prospective metrological technicians as well as newly technology for metrological Industry employees.

During the past year, the website has been added to the new content of E-learning, including the introduction of sampling, categories of weighing instruments, mechanism and theory of weighing instruments, the theory and the application of load cell, fundamental electrical science.

3. APLMF Activities

BSMI sent its staffs to participant in training courses organized by APLMF, including training course on water meters held in Viet Nam, electricity meters in Malaysia.

4.Providing the training courses and calibration service for temperature measurement instrument

The H1N1 Flu has taken lives worldwide and was alerted by countries this year. Detecting fever by using temperature measurement instrument is still the preliminary measure to screen the flu in school, hospital and public place.  BSMI has provided several training courses to inform the public especially school faculty, hospital staffs the correct usage and maintenance of ear thermometer, electric thermometer and so on. Over hundreds attended the training. BSMI also provide free calibration service of the instrument to public.