經濟部暨所屬機關因公出國人員報告書

（出國類別：洽公）

赴卡達參加「台達1號船岸匹配會議」報告書

服務機關：台灣中油公司台中液化天然氣廠

姓名職稱：曾世文 經理

派遣國家：卡達

出國期間：98年10月07日至10月09日

報告日期：98年12月2日

摘要：

依卡達FOB買賣契約Clause 14，至卡達裝貨之船舶需為卡達確認船岸合格者方得運送卡達LNG貨氣，本公司「卡達LNG船計時租船契約」首艘LNG船於98年10月13日交租，並直接航向卡達裝貨港裝貨；船方應由事業部人員代表買方負責相關之協調整合，其中船岸匹配會議為其重點。雙方訂於98年10月8日在卡達多哈舉行該項會議，會議中由船岸雙方參與人員就匹配項目提出研討，以便於靠泊裝貨前完成相關確認，進而順利完成台達LNG船隊之首艘LNG船裝貨作業。

目次：

- 目的...........................................3

- 過程...........................................3

- 報告內容.......................................3

- 心得與建議事項.................................7

壹、 目的

目前卡達是全世界最大液化天然氣輸出國，而LNG交易一般區分FOB與CIF方式；本公司與卡達Ras Laffan Liquefied Natural Gas Company 簽訂之液化天然氣買賣契約為FOB貿易條件，故以自有或租用LNG船於裝貨港(Ras Laffan, Qatar)裝貨。卡達裝貨港為維持LNG船裝貨時之安全性，對LNG船裝貨前之船岸匹配要求甚高，船岸雙方於與會前交換相關資料以便順利進行會議，匹配會議時雙方參與之人員均按照匹配項目逐一確認。

貳、 過程

10月07日  起程(台北→曼谷→卡達(多哈))

10月08日  擔任買方代表進行船岸匹配之討論

10月09日  回程(卡達(多哈) →香港→台北)

參、 報告內容

匹配會議時雙方參與之人員均按照匹配項目相互確認，其匹配項目如下:

| 項目(Items) | 岸方(Shore Specification) | 船方(Ship Specification) |
| --- | --- | --- |
| I一般要求General Requirement 1. Max. Size of Vessel | Max. Size of Vessel Acceptable LOA: 350 m Breadth: 55 m Draft: 12.5 m Displacement:195000 t Cargo Volume:267000m3 Air Draft: Main Alongside: Port | Max. Size of Vessel Acceptable 均符合此一般要求 |
| II.卸料臂配置Loading Arm / Manifold Arr't | Loading Arm | Manifold |
| III. 防舷材Fender / Flat Body 1. Arrangement 2. Maximum Design Contact Pressure 3. Berthing Energy | 符合要求 1. Fender Arrangement 2. Maximum Design- Contact Pressure 3. Max. Approaching Speed | 符合要求 Flat Body 2. Maximum Contact Pressure 3. Max. Approaching Speed |
| IV. 繫纜配置Mooring Arr't Mooring Facilities 2. Tension / Strength Limit 3. Arrangement (Page7 Appendix 1) | Mooring Facilities Mooring capstans 12 x 4T starting pull, 2T running pull Dolphin Arrangement | Winch (1) Windlass 1000/770kN x 9/12m/min x 2sets(2) Mooring Winch294kN x 15m/min(3) Number of Druma. Wire Drum:21 c. Brake 2. Wire Strength IWRC Plastic-Filler Wire 44mm dia x 275mwith 90mm dia x 11m Lenghth Polypropylene/Polyester Tail 3. Mooring Arrangement |
| V. 舷梯Gangway / Support 1. Position of Gangway 2. Gangway Working Area | 1. Gangway Position Working Range of Gangway | Gangway Support Gangway Landing Position |
| VI. 卸料臂1.Loading Arm / Cargo Pump 2. Loading Arm Working Range | 符合要求 1. Loading Arm Information 2. Loading Arm Working Range | 符合要求 1. Pump Spec. 2. Loading Arm Compatibility |
| 3.LN2 Arm 4. Fuel Oil Arm 5. Diesel Oil Arm 6. Fresh Water Hose |  | 3.不需岸方供給 4.Design Flow of F.O Line : 600m3/h 5.Design Flow of D.O Line : 40m3/h 6.Design Flow of F.W Line: 23m3/h |
| VII.緊急關斷裝置 Emergency Shut Down Optical Fiber System Pneumatic System 3. Electric System | 符合要求 NFI, Seatechnik,UK NITTA MORE Electrical System | 符合要求 FURUKAWA ELECTRIC CO., LTD NITTA MOOR SEATECHNIK |
| VIII. 緊急關斷作動ESDS Activation | 符合要求 ESD signal from ship | 符合要求 Manual switch |
| IX. 通訊系統Communication System 1.Optical Fiber System (main) 2. Electric System 3. Radio System | 符合要求 1. Optical Fiber System (main) PYLE NATIONAL 37 Pins See attachment for details VHF Channels for operations | 符合要求 Optical Fiber System (main) SEATECHNIK: PYLE NATIONAL, 37 pin (female) Two way VHF Handheld transceiver FM-8 |
| X. 拉力監視系統Tension Monitoring System (1) Manufacture (2) System Type (3) Connection Type (4) Connection Box Position (5) Cable Length | 符合要求 Marix. K.K STRAINSTALL Load sensors Through either PYLE or OPTICAL Link, Ship Side (5) 50 m | 符合要求 YOKOGAWA ELECTRIC Windows PC Enhanced PC system Optical combination connector Upper deck below manifold platform |
| XI. Bonding Cable & Connector | 無 | 無 |
| XII. 滅火系統Fire Fighting System | All Equipment Located on Jetty Head |  |
|  | 1) Upper Platform : D/P, W/S, S/W, F/E 2) Middle Platform : 3) Lower platform : W/S, S/W, F/E High Expansion Foam 4) Remote Control Fire Water Monitor(2) Cover berth No.3 5) Fire Hydrant with International Connector | Exposed Deck in Cargo Area Loading Station Cargo Tank Dome Area Accom. House Front Wall |
| XIII. 壓縮機H/D Compressor | 符合要求 Shore Compressor | 符合要求 30,000 m3/h x 2 (46200 kg/h x 2) |
| XIV.碼頭排放塔及排放量 Jetty Flare & Volume 1) Number 2) Capacity 3) Pressure 4) Vapour Temperature | 1) 1 2) 86 tons/h 3) a. Pressure @ ship flange 3.55 bar A 4) -161 ℃ for Liquid | Loading Rate : 10,000m3/h |
| XV.碼頭靠泊限制 Limitation of Wind Speed and Current Speed | - Speed of Approach for berthing 0.12 m/sec | 船方配合 |
| XVI. 靠泊設備 Limitation Approaching Speed Meter 1) Position 2) Manufacture 3) Specification | Laser sensor #1 on BD-2Laser sensor #2 on BD-3Speed & Distance : Distance Display Panel - On Shore Matrix K.K. 3) S-67-1386-017 Rev.2 | 船方配合 |
| XVII.補給服務 Services | Services |  |
| XVIII.碼頭潮位Port Water Level | Highest Astronomic Tide+0.97 m Mean High High Water:: +0.58 m Mean Lower High Water: +0.15 m Mean Sea Level: +0.00 m Mean High Lower Water: -0.33 m Mean Lower Low Water: -0.44 m Lower Astronomic Tide: -0.76 m | 船方配合 |

Appendix 1. LAYOUT OF BREASTING & MOORING DOLPHIN

肆、心得與建議

經本次實際參與LNG裝貨港船岸匹配後，有關其細節部分如拉力監視系統之插座、舷梯支撐之厚度等會後均已確認，並於98年10月30日在裝貨港(Ras Laffan, Qatar)港外由岸方代表Mr. Muslim對台達一號LNG船逐一核對相關項目及檢查相關證書後准予靠泊，而後並順利完成裝貨作業，該LNG船經過12天航程後於98年11月12~13日於臺中港西13碼頭順利完成卸收LNG作業。此次船岸匹配會議可以作為將來台達二、三、四號LNG船船岸匹配會議之參考。