2010 ECONOMY REPORT

THAILAND

- Revision of Weights and Measures Act

Department of Internal Trade has made a proposal to revise the Weights and Measures Act.  The revision is to develop “ Pattern Approval “ system in Thailand. The revised Act is now under the consideration of the Office of the Council of State. We expect that the revised Act will be approved by the Office of the council of State, the Cabinet and then submitted to the Parliament next year.

- Improvement of Infrastructure

Department of Internal Trade is establishing the Southern Weights and Measures Center in Surat Thani province. The construction of the building of the Center is finished. The equipments are being installed. At the end of the year 2010, the Center will be able to provide calibration, verification and inspection services in southern region of Thailand.

Department of Internal Trade is also setting up a new test rig for large flow meters at the Eastern Weights and Measures Center in Chonburi province. The test rig can be used for calibration and verification of PD meter, Turbine meter, Coriolis meter and Vortex meter at the flow rate ranging from 300 L/min to 5000 L/min and from 300 kg/min to 5000 kg/min. The set up will be completed in December 2010.

- Permission of manufacturers to carry out initial verification

According to the provisions of the Weights and Measures Act, any manufacturer may apply for a license to carry out initial verification.

Up to now, Department of Internal Trade has issued licenses to 6 water meter manufacturers, 1 fuel dispenser manufacturer, 2 measuring tape manufacturers and 1 spring scale manufacturer. Next year, DIT is going to issue the license to truck scale manufacturer, LPG dispenser manufacturer and CNG dispenser manufacturer.

- Improvement of Rice Moisture Meters

Department of Internal Trade in co-operation with manufacturers of rice moisture meters has been studying on the measurement of moisture of various kinds of rice. The purpose of this study is to improve the accuracy of rice moisture meters to be used in Thailand.

Furthermore, the scope of present regulation relating to the control of moisture meters covers only moisture meters used for moisture measurement of rice. Department of Internal Trade is upgrading its facilities in order to be able to measure the moisture content of corn (maize) and revising the regulation to expand its scope to cover the moisture measurement of corn.

- Co-operation with APLMF

In 2010, Department of Internal Trade has Sent weights and measures officials to attend various training courses organized by APLMF i.e.

  - Training course on Gas Meters held in China

  - Training course on High Capacity NAWI held in Indonesia

  - Training course on Mass Flow Meters held in Singapore

DIT in co-operation with APLMF organized the Workshop on Software Controlled Measuring Instruments in Bangkok on 3-6 August, 2010.

Department of Internal Trade

Ministry of Commerce

Thailand