出國報告（出國類別：開會）

2012年台美民用核能合作會議

服務機關：台灣電力公司

姓名職稱：劉明哲  核能發電處副處長

派赴國家：美國

出國期間：101年11月5日至11月10日

報告日期：101年11月29日

行政院及所屬各機關出國報告提要

出國報告名稱：2012年台美民用核能合作會議

頁數 26 含附件：■是□否

出國計畫主辦機關/聯絡人/電話

台灣電力公司/陳德隆/02-23667685

出國人員姓名/服務機關/單位/職稱/電話

劉明哲/台灣電力公司/核能發電處/副處長/02-23667042

出國類別：□1.考察□2.進修□3.研究□4.實習■5.其他

出國期間：101/11/5-101/11/10    出國地區：美國

報告日期：101/11/29

分類號/目

關鍵詞：民用核能、原能會、核管會、能源部

內容摘要：（二百至三百字）

我國在台美民用核能合作協定項下，與美國核管會(NRC)、能源部、及橡樹嶺、布魯克海汶、阿岡、愛達荷、聖廸亞等著名的國家研究所有合作研究項目，其範圍包括嚴重事故與相關現象、熱流與動力學、儀控、人因工程、用過燃料之處理、廢料管理與除役技術、保健物理、核能安全技術等，本公司為此合作協定之參與單位。

本年度會議於11月6~8日在美國勞倫斯利佛摩國家實驗室(Lawrence Livermore National Laboratory)舉行。

美國方面報告世界核能和平用途現況、美國用過燃料處置、能源部核能計畫、下一代核子保防作為、後福島法規更新等項目，我國報告台灣民用核能計畫、核能研究工作、台電放射性廢棄物處理及核一廠用過燃料乾貯、台電運轉中電廠現況及福島事故後的強化措施、後福島法規作為評估等議題，並與美方討論目前進行中合作項目。此外，美方安排參觀勞倫斯利佛摩國家實驗室的國家大氣擴散諮詢中心、質子加速器、緊急應變中心等。

本文電子檔已傳至出國報告資訊網（http：//report.nat.gov.tw/reportwork）

目   錄

| 內容 | 頁次 |
| --- | --- |
| 出國目的 | 4 |
| 出國行程 任務過程 | 4 4 |
| 心得與建議事項 一、心得 二、建議事項 伍、附件一 附件二(不上傳) | 13 13 13 15 |

附件三

壹、出國目的

  - 我國與美國民用核能合作會議已有28屆，今年輪由美方主辦，選定能源部核子安全局所屬勞倫斯利佛摩國家實驗室為開會地點，雙方報告一年來核能的研究計畫、世界核能和平用途現況、美國用過燃料處置、能源部核能計畫、下一代核子保防作為、後福島法規更新、台電放射性廢棄物處理及核一廠用過燃料乾貯、台電運轉中電廠現況及福島事故後的強化措施、後福島法規作為評估等議題，互相瞭解核能使用現況。

  - 討論目前雙方合作研究項目之進度，澄清困難或連絡負責人更換項目，共有68項，確定繼續合作方向與作法。

貳、出國行程

11月5日   搭機前往美國舊金山

11月6日   前往勞倫斯利佛摩國家實驗室參加第一天會議(詳細議程如附件一)

11月7日   前往勞倫斯利佛摩國家實驗室參加第二天會議

11月8日   前往勞倫斯利佛摩國家實驗室參觀

11月9日--10日搭機返國

參、任務過程

11月6日

會議開幕由美方國務院美國在台協會環境科技健康處長Scott Hansen(美方代表團領隊)首先致詞，他歡迎台方能到舊金山地區開會，在福島事件發生19個月後，世界各國政府及國際原子能總署均分別針對長期核能安全訂出行動計畫，希望各國確實執行提升核能安全，在此次會議中美方將報告美國的作法，也希望瞭解我國核能應用的近況，藉由雙方的年會促進核能安全，期望明年在台灣見面。

接著由我方代表團領隊原能會周副主委致詞，他感謝美方此次熱情的接待，安排在美麗的舊金山地區開會，期待美方能夠報告後福島美國提升核能安全的作法以及法規的修訂、美國最近的核能計畫、今年召開的第2屆核能安全特別會議的結論、用過燃料處置作法，檢討雙方核能研究合作進度，促進雙方進一步的瞭解，並預祝會議順利成功。

美方代表團包括美國在台協會、國務院、能源部、國家核子安全局、核管會、聖地亞實驗室、勞倫斯利佛摩國家實驗室等共17人；我方代表團包括原能會、核研所、清華大學以及台電公司、台北經濟文化代表處等共18人，雙方名單詳如附件二。 (本名單電子檔上傳時將予刪除)

一、各項簡報內容摘要

1.核能國際發展及和平用途: 國際原子能總署於今年8月召開核安特別會議，討論後福島長期核安作為，強化核安的行動計畫，並於9月召開會員大會，報告核安行動計畫的執行方式，並呼籲會員踴躍參加今年12月在日本舉行的部長級核安會議，G-8領袖會議強烈支持核能設施風險評估及強化核能安全，福島教訓將是未來必須學習的，而這顯示獨立且有足夠資源的核能管制單位的重要性。

2.台灣民用核能計畫現況:馬總統於去年11月宣佈新的核能政策，3座運轉中電廠不再延役，除非確保安全否則龍門電廠不商轉，若2016年前龍門電廠兩部機穩定運轉核一廠將提前除役，在不限電及合理電價前提下履行減碳的承諾。最近的管制作為包括：後福島管制、地震重新評估、核二廠反應器支撐裙板螺栓受損、龍門電廠建造及試運轉視察。2012年核安演習檢視核能電廠安全強化措施，測試斷然處置指引，空中及海上輻射偵測，大規模民眾疏散及安置，國際間及海峽兩岸核子事故通知。醫療曝露品保計畫，乳房攝影管理，電腦斷層掃瞄品保。放射源管制及操作人員資格管理，線上通報系統之建立，從日本進口食品取樣及核種分析之管理，台灣本島及周邊島嶼環境偵測和數據收集，低放射性廢棄物處置場址選擇，核一廠核二廠用過燃料乾式貯存計畫，電廠除役準備，核能及輻射教育延伸，資訊透明化及公眾參與，政府組織改組。

3.美國用過燃料處置現況:核能是清潔可靠的基載能源，提供美國19%的電力，也佔非碳電力的61%，每年減少7億噸二氧化碳排放，也減少氮化物和硫化物排放，美國現有104個核能機組共100GWe裝置容量，容量因素平均約90%，大部分將延役運轉至60年。每年產生2000噸用過燃料，至2012年底將累積70,000噸，其中27%為乾式貯存，估計到2020年用過燃料將達88,000噸，現行政策是直接地質處置。

美國總統歐巴馬成立藍帶委員會(	Blue Ribbon Commission)負責用過燃料決策，委員會建議建立全新的方法來選擇核廢棄物場址管理設施，設置新組織獨立執行廢棄物管理計畫，立即發展一個或多個地質處置設施，立即發展一個或多個強化貯存設施，立即準備大規模運輸系統以便將用過燃料和高放廢棄物運送至強化貯存設施和處置設施，支持核能技術繼續發展，領導國際上核能安全、廢棄物處理，防核武擴散和核子保防的關切。

美國能源部仍負責核廢管理，對於不需成立新組織就能進行的工作項目要求儘速進行，如強化貯存設施、提供基金和州政府及地方政府共同訓練運輸用過燃料事宜、繼續地質條件和工程障壁研究。

4.核能研究所最近主要工作報告:在核能安全方面包括地震再評估和緊急應變，檢視核能電廠地質研究並執行地震危害分析，地表移動的模擬，地震分析確認，建物結構地震反應及老化影響，重新評估核能電廠緊急計畫區，核子事故劑量評估系統之發展。在核子設施除役和廢棄物處理方面，包括除役技術及經驗、固體廢棄物除污外釋、廢水處理技術、低放射性廢棄物最終處置、用過燃料最終處置、核能設施地下水處理技術、核一廠乾貯。在輻射生醫應用方面，癌症影像標靶使用，錸-188微脂體抗癌新藥人體試驗，乳房影像拍攝裝置改進癌症偵測技術，二維及三維X光影像模擬。

5.美國能源部核能計畫:今年3月26日歐巴馬總統在漢城提到竄升的油價和氣候暖化，使核能更形重要，美國重新啟動核能工業作為能源多源化策略的一部分。能源部朱部長強調核能是歐巴馬總統能源策略”高於一切”的重要部分，以協助美國經濟持久。能源部核能司的使命是(1)發展先進核能電廠具有提供國家能源需求、環境和能源安全的能力，(2)透過目標研究、發展和證明解決技術、安全、保安、經濟和管制的問題，(3)指導研發計畫使核能電廠能夠提供電力及製程熱汽。核能司的目標是(1)核電廠延役由60年提高至80年，並提升績效，(2)建廠技術的提升和發展先進的下一代電廠(3)建立可長可久的燃料循環(4)設計有效系統和保護核物料、設施、敏感技術和專家以防止核子擴散和保防威脅。

6.能源部環境管理司報告:環境管理司的任務是安全清除過去50年美國發展核武、生產核武以及政府能源研究的遺留物，這任務包括在全世界最複雜管制環境下執行全世界最大的環境整治計畫，並使能源部能夠順利推動環境法案關鍵任務。從1989年開始環境清除工作，包括110個場址，分佈在35個州面積3125平方哩，至2011年尚有17個場址11個州318平方哩，預定2020年剩下Hanford未完成以及較小的Savannah River、Portsmouth、 Oak Ridge等，整體清除工作尚需美金2740億至3090億，預定到2052年全部完成。優先處理的工作是整個計畫必須在安全、確切、順利的完成，放射性廢棄物槽穩定化、處理及處置，地下水和土壤找出特性加以整治並監測，多餘的設施停用並除役，用過燃料貯存、接收及處置，特殊核物料固化、處理、處置，超鈾元素及混合低放廢料加以處置。

7.台電放射性廢棄物管理及乾貯計畫現況:台電廢棄物管理策略是來源最小化、減容、穩定化、貯存、最終處置。低放廢棄物最終處置場選定台東達仁鄉和金門小坵島為候選場址，今年8月17日經濟部通知台東縣和金門縣政府，請他們辦理公投，但兩縣政府皆以政治和社會氛圍不宜辦理而拒絕辦理公投。核一廠乾貯水保計畫在2010年9月13日獲台北縣政府同意，現場邊坡穩定、水泥地面和輔助系統將於11月底完成。試運轉計畫於今年5月23日獲原能會核准，分成二階段：第一階段測試操作設備、廠內運輸和貯存設備，第二階段將各56束燃料裝入2個箱罐(casks)中。期望本年底能獲得原能會許可進行第二階段熱測試，明年3月完成熱測試，4月向原能會提出營運執照申請，8月取得運轉執照。核二廠乾貯說明，計畫修正及環差評估報告已獲環保署同意，乾貯設備已決標，安全分析報告正由原能會審核中，貯罐型式及設施修改報告，環保署待原能會安全分析報告通過後進行審查，期望2013年1月原能會核准安全分析報告，6月環保署核准貯罐型式及設施修改報告，2013年7月將提水保計畫給新北市政府審查，2014年底開始試運轉，2015年底取得運轉執照。

8.核能安全大會特別會議CNS報告: CNS成立目標(1)透過強化國家法令和國際合作來達成並維持世界核能安全，(2)建立有效的防護防止潛在輻射以保護人民及環境，(3)防止具有輻射後果的事故，若發生時減緩其後果。CNS係1994年於奧地利維也納提案於1996年10月實施，目前參與的會員國有75個。藉由檢視和共享會員針對福島事故所接受的教訓和所採行動以強化核安，並審查核安大會規章的效能和持續穩定性，作為本次特別會議的目標。本次特別會議在今年8月於維也納舉行共有64個會員國參加，日本的NISA副局長Shinichi Kuroki簡報福島電廠現況，本次會議分成6個小組討論並分享會員國針對福島事故所採取行動，此次會議也討論為提昇大會效能的提案，及修訂大會規章的提案，本次會議的結論如下:(1)電力公司(營運者)須負核能安全責任，(2)會員國同意核能電廠設計、建造、運轉都應防止事故發生，不幸發生也要減緩事故防止輻射汙染，(3)會員國應確保管制機關的獨立性並有足夠資源執行職務，(4)鼓勵國際合作，(5)會員國為強化核安訂定行動目標並考量達成IAEA行動計畫、IAEA的安全標準、資訊透明和有效管制、同業評估。

9.下一代核子保防倡議:國際原子能總署提出下一代核子保防的構想，這是因為總署工作量增加，核子設施增多、設施種類複雜、核物料數量遽增，預期核能電廠數量還會陸續膨脹，而總署預算與員工並未增加，專業人員流失，使得核子保防工作日益艱困，因而提出這項倡議，這項倡議包括5個子計畫：(1)政策發展及延伸，(2)概念和方法，(3)技術發展，(4)人力資源發展，(5)國際承諾。第(1)個計畫支持美國的國際保防政策以達成全球非核擴散，各國和國際原子能總署合作核子保防。第(2)個計畫發展先進的概念和方法以及評估方法論，以強化國際保防的效用、效率和可信度。第(3)個計畫發展及應用各式工具、技術和方法使核子設施和國家的保防效用、效率最佳化，已有先進技術從實驗室應用到現場。第(4)個計畫提供連續性教育和訓練年輕專家擔任能源部的實驗室、美國政府、專家小組、學院、國際原子能總署的保防工作。第(5)個計畫為原子能總署和各合作夥伴一起強化核子發展各階段的保防，2011年有19國85個計畫進行中。

10.台灣在福島事故後法規再評估及行動:福島事故發生後，原能會要求台電公司重新評估發生極端天然災害時的應變能力，此項再評估包括核能安全、輻射防護和緊急應變計畫。再評估分成二階段，第一階段於2011年6月完成，第二階段在2011年12月完成。2011年10月原能會發布「國內核能電廠現有防護體制全面體檢第一階段安全評估報告」，2012年8月原能會發布「國內核能電廠現有防護體制全面體檢方案總檢討報告」，總檢討包括(1)電廠失去交流電源應變能力，(2)防洪及海嘯能力，(3)燃料池完整性及冷卻能力，(4)評估熱移除及最終熱沉，(5)緊急操作程序書再檢討及再訓練，(6)建立斷然處置指引，(7)機組互相支援，(8)複合式災變，(9)減緩超過設計基準事故後果，(10)應變準備及支援設備，(11)人力、組織及安全文化再檢討。後續行動包括龍門電廠評估、根據西歐壓力測試檢查深度防禦和安全餘裕，找出弱點並提出改善方法，壓力測試報告在2012年3月(運轉中電廠)和4月(建造中電廠)提出，原能會將邀請國際專家進行同業評估。

11.美國核管會福島事故後採取行動進度報告:2011年7月發布近程專案小組報告，2011年10月將專案小組報告依優先次序分為3類，2012年3月發行第一優先命令及要求通告，2012年7月發行第三優先計畫(SECY-12-0095)，2012年8月發行命令執行指引。已採取行動如下：(1)命令:EA-12-049超出設計基準外部事件的減緩事故後果策略，要求以3階段方式維持或恢復爐心冷卻、圍阻體完整和用過燃料池冷卻。EA-12-050針對沸水式反應器馬克一型和二型圍阻體，失去正常功能時移除熱量控制圍阻體壓力，防止爐心損壞，並且在電廠全黑時能夠運作。EA-12-051強化用過燃料池水位儀器，必須能夠指示下列3種水位：正常燃料池水位、低於正常水位但仍有足夠屏蔽能夠靠近燃料池、水位接近燃料頂部必須立即補水。此3種命令指引已於2012年8月發行，10月完成更新，2013年2月繳交完整計畫，於最近2次大修完成或2016年12月完成，視何者先到期。(2)要求通告(10CFR50.54(f)):執行地震及洪水電廠勘察、重新評估地震和洪水風險、檢查緊急通訊設備以確保長期電廠全黑時的通訊能力、評估長期多機組全黑時的人力。(3)立法進度:電廠全黑，針對長期全黑修正規定強化應變能力，將於2014年完成。緊急操作程序書整合的法規要求預定2016年完成。第二優先建議事項有:用過燃料池補水能力、緊急應變程序、其他外部風險再評估。

12.台電核能電廠運轉績效及福島後安全強化措施:民國100年在台電公司2130億度發電量中，核能發電佔19%為405.2億度，容量因素93.06%，6個機組皆無急停事件，是運轉績效良好的一年。福島事故後，台電經過檢討，學習到在事故發生時要確保反應器燃料和燃料池有水覆蓋、防止放射性物質外釋避免大規模民眾疏散、確保民眾安全。核能電廠針對地震海嘯有5重深度防禦，緊急泵室、廠房防海嘯高程設計、第5台氣冷式柴油發電機、2台高程氣渦輪發電機、設於高地的生水池。台電進行核能總體檢，包括成立天然災害專案小組，核能電廠進行12大項的評估，增設多樣化的交流電源和水泵，多樣性補水水源，強化防震能力及防火能力，強化防洪防海嘯能力，執行安全評估，以提升超出設計基準事故的處理能力；為了確保民眾安全，台電新創斷然處置措施，只要碰到超大地震及海嘯、失去所有補水水源或電廠全黑失去內外交流電源時，立即啟動斷然處置預備工作，連接各種水源、反應爐洩壓和圍阻體排氣。通報決策者(核能副總或廠長)，獲得同意後進行補水行動，即使因灌入海水犧牲反應器，只要能確保民眾安全亦在所不惜。

11月7日

二、合作研究項目討論(各組詳細項目如附件三)

第一組反應器法規及管制研究:結論如下

討論項目23項，結案2項，新增0項，合併1項(由第三組併過來)，尚有21項

重點事項：

- 美國核管會同意提供原能會用過燃料運輸罐再申請審查項目的資料，此項運輸罐執照每3年須更新一次。

- 美國核管會同意提供若用過燃料貯存罐傾倒事件發生，處理程序書和設備的資料。

- AE-IN-TP-NR-C18項事故編排、特性和狀況報告的編碼，核研所將決定從龍門電廠收集資料的可行性。

- AE-IN-BN-D66美國核管會同意分享10CFR40法規訂定的結果，將於2013年初發行。

- IN-BL-SN-F20台北經濟文化代表處對NFPA805訓練有興趣，美國核管會將決定是否讓原能會參加下次NFPA805訓練。

- AE-NR-S42對於核三廠圍阻體集水池問題，原能會同意提供核管會爐內效應及硼酸沉澱的資料。

7.AE-NR-S49原能會同意提供政府組織再造新資訊給核管會。

8.AE-NR-JJ1針對龍門電廠試運轉及啟動測試，原能會同意提供時程並邀請核管會參加觀察。

第二組廢棄物處理及環境恢復:結論如下

討論18項，進行中15項，結案1項，合併1項(併入第三組)，新增1項，尚有17項

重點事項:

- AE-DE-DD26結案

- IN-INL-U3將併入第三組 TU-DE-Y4項目

- 台灣宣布新能源政策後，3座運轉中電廠不再延役，雙方同意下列項目更重要FC-IN-NR-G23、 AE-NR-J2、 IN-ANL-J4、 TP-EM-DD22、 AE-DE-DD29

- 政府組改後，核研所將改隸經濟部並改名能源研究所，現有UF6將尋求轉化廠協助再利用，將此列為新合作項目。

- 明年繼續進行項目有:G23, G33, G34, G35, J2, J4, U2, U3, X1, Z9, DD12, DD19, DD22, DD23, DD26, DD27, DD28, DD29,以及新合作項目IN-DE-DD30 UF6 Stabilization and Disposition。

第三組核子科學、技術及保防:結論如下

討論23項，結案0項，新增0項，合併2項，尚有21項

重點事項:

- 針對TU-DE-Y3和 TU-DE-Y4兩項，已在今年5月和8月分別在愛達荷實驗室和核研所舉行研討會議，交換資訊，明年將派遣員工或學生進行教育訓練。

- 和國際原子能總署的核子保防三邊協定資訊交換。

- 針對AE-DE-EE6 和AE-DE-EE7核物料實體保防，美國在台協會將於2013年3月訪台瞭解，此訪問團意將至清華大學訪問並瞭解反應器保安問題。2013年3月將針對國際原子能總署保安新標準舉辦一個研討會議，以確認核子設施符合保安新標準。

- 今年8月在台灣針對核子法學舉辦一個研討會，並計畫2013年由美國聯邦調查局在台灣辦理訓練。

- 明年第一季由美國派專家來台辦理一次訓練，針對非源自美國特殊核子物料的庫存計算方法作說明，並在雙方同意時間駐廠擔任顧問。

第四組緊急應變管理:結論如下

第四組4項議題由第三組分出，為今年新設組別，經過討論，美國核子安全局和原能會皆同意4項議題將繼續進行

- 原能會將事務性支援2012年12月17日舉行的國際事故後果管理會議。

- 基於本項中長期合作計畫原能會建議2013年第3季舉行特別的核子事故(醫院)研討會。

- 雙方同意檢討本合作計畫執行情形，以決定下一步，並於明年作修訂。

- 原能會將參與美國核子安全局的活動以強化核子事故應變處理能力。

- 明年下半年在核三廠舉辦的全國核安演習，原能會將通知美國核子安全局。

- 放射性雲模式互相比較(2014年)將在20132年先討論。

- 美國邀請台灣登錄為國家大氣擴散諮詢中心網路國際交換計畫的使用者。

11月8日

三、參觀項目內容

1.國家大氣擴散諮詢中心NARAC:本中心在發生事故有害物質洩漏釋放到大氣時，能夠提供專家、工具和服務，繪出煙雲地圖，並預測落塵時間、方向及範圍，以協助緊急應變保護民眾。在應變過程，中心專家和偵測取樣團隊密切配合，利用現場收集到的數據修正預測模式，以得到最精確結果。本中心成立於1979年，為三哩島事故後的應變改善，為各核能設施事故(如車諾比)、工業化學品噴濺排放和火災、放射物質事件或火山噴發服務過，中心服務能力與範圍也日益提升。本中心隸屬能源部國家核子安全局，每年服務超過300個聯邦、州、地方機構、緊急應變團隊、營運中心和國際組織，每年超過10000個模擬空浮煙雲的申請，參與100個主要演習。本中心提供國際交換計畫的網路平台支援國際合作。

2.緊急指揮中心EOC:由於勞倫斯利佛摩國家實驗室本身有數百棟建物和實驗室，工作人員數千人，因此成立緊急指揮中心作為發生緊急事件或天然災害的救災指揮處所，以最壞的情況假設會發生，針對救災、滅災、救人、資訊收集、通訊連絡、運送、糧食等等，予以分組，配備所需裝備、車輛等，訂定作業程序書，每年均進行演練，並有不定期演習，每人均指派任務，還指定代理人，指揮中心24小時均有人員值班，為防止指揮中心災難時本身受損無法使用，另設後備指揮中心，作為備援。由於加州處於地震帶，所有建物每5年須評估一次，確認沒有危險才能使用，否則必須補強。

3.質子加速器CAMS:以質子加速器撞擊同位素的方法，利用其半生期測定年代，例如碳-14半生期約6000年，可以得知枯木年齡，或利用氫-3含量測知地下水。

4.馬歇爾群島計畫說明:馬歇爾群島位於太平洋中間，與菲律賓和檀香山約各距離4千公里，是由數百個珊瑚礁島組成的島國，在40年至60年代，美國在此群島作核彈試爆數百次，後因聯合國禁止大氣試爆終止，但已造成島嶼落塵污染嚴重，後來在1968年美國宣布島嶼已經乾淨，島民開始搬回居住，至1972年居民在此蓋房子種蔬菜椰子樹等，1978年居民被發現有銫137超過限值的情況，因此決撤離島民，引起居民輻射恐慌並且不信任美國政府；研究發現早期的環境輻射學偏重海洋污染途徑和鍶90劑量，後來發現銫137占核爆落塵95%以上，馬歇爾群島北方各島居民經由飲食當地食物吸入的劑量占85%至90%。落塵掉落地面，使島上的珊瑚土壤含有銫137必須加以處理，予以移除並更換新土，根莖類蔬菜易吸收銫137而經由食用進入人體。美國政府和當地政府達成協議，負責剷除含高濃度的土壤，並為居民健康檢查，蓋房屋給居民，安頓居民。當地居民的年劑量由1毫西佛降到0.01毫西佛。

11月9日

各單位僅留下代表參加本次代表團參加台美民用核能合作協定會議檢討，其他人員先行回國，本公司由後端處李處長代表參加檢討。

肆、心得與建議

一、心得

1. 勞倫斯利佛摩國家實驗室的門禁管制森嚴，雖然代表團所有成員資料已經事先送美國審查，但是第一天進入實驗室前，仍須個別面談，核對證件護照，才發給識別證，而且每天進入實驗室時，大門口警衛均會逐一核對識別證和護照，即使是該室員工仍需出示識別證，比起我國核能電廠有過之而無不及。

2.美國在福島事故後，並未因此停下腳步，檢討美國各核能電廠的安全後，確認美國仍將核能視為能源供給重要的選擇，目標是訂出可長可久的核燃料循環政策，延役目標80年，建造新一代的反應器，防止核子擴散的燃料循環，美國最近發給4座反應器的建造執照，代表美國對核能的信心。

3.美國核管會在福島事件後，雖然頒布了多項命令及要求，但也訂出短中長期的分類，區分輕重緩急，並且發行各項指引，提供業者參考，以符合核管會要求，不會因別國作了什麼就趕緊要求業者比照辦理，較符合管制精神。

二、建議事項

1.國際原子能總署訂出保安新標準，美國辦理研討會，使各核子設施瞭解新的要求，今年台電曾派龍門電廠同仁參加，明年將繼續辦理，希望各核能電廠派員參加。

2.針對非源自美國特殊核子物料的庫存計算方法，本公司表示早年因資料不全，回朔計算有困難，希望美方協助，本次會議美方表示將於明年派專家來台作說明，希望各廠相關作業人員均能參加。

3.本公司核能電廠門禁管制尚稱嚴謹，但以往因便民之故，並未詳細核對申請進廠人士和實際進廠人員是否相同，勞倫斯利佛摩國家實驗室在人員進廠時核對附有相片的證件(例如護照)，較為確實，同時警衛對進入上班員工也都確實核對識別證，落實保安，值得我們借鏡。

4.美國能源部確定將持續使用核能，延役計畫繼續進行，並將目標放在延役至80年，正研究其技術可行性，藉核能的使用以降低碳排放量，我國是否應訂定可長可久的全國能源計畫，有效解決碳排放問題，建議上級單位參考。

2012 AIT-TECRO Joint Standing Committee on Civil Nuclear Cooperation (JSCCNC) Meeting 附件一

AGENDA

November 6 – 8, 2012

November 6	AIT - TECRO JSCCNC Plenary Session

08:00 - 08:30		Transportation from hotel to LLNL

08:30 - 09:15 		Registration of AIT/TECRO participants and others.

09:15 – 09:25		Opening remarks

- Scott Hansen, AIT

- Yuan-Ching Chou, Deputy Minister, AEC

09:25 – 09:40		Welcoming remarks

- Admiral Joseph Krol, Associate Administrator, NNSA

- LLNL representative (TBD)

09:40 – 09:55		Overview of World Developments and Peaceful Use of Nuclear Energy

Alex Burkart, Deputy Director, DOS/ISN/NESS

09:55 – 10:10		Overview of Civil Nuclear Programs in Taiwan

Ching-Luh Wu, Senior Scientist, AEC/PD

10:10 – 10:30 	Update on Activities: Used Nuclear Fuel Disposition in the U.S. (DOE/NE) TBD

10:30 – 10:45 		Break

10:45 – 11:15		Review of Current Nuclear Research Activities in Taiwan

Kin-Fu Lin, Chief Secretary, INER

11:15 – 11:45	Review of DOE Nuclear Energy Projects (DOE/NE) TBD

11:45 - 12:15 	Office of Environmental Management Program Overview

Rosa Elmetti, DOE, Office of Environmental Management

12:15 - 13:00 		Working Lunch

13:00 - 13:30 	Current Status of Taipower's Radioactive Waste Management Program and ISFSI at Chinshian Plant, Chin-Shan Lee, Director, TPC/NBM

13:30 - 14:00 	Convention of Nuclear Safety 2nd Extraordinary Meeting and Summary

William Ruland, Division of Safety Systems, NRC

14:00 - 14:30 	Next Generation Safeguards Initiative (NNSA) - TBD

14:30 - 15:00 		Fukushima Regulatory Actions/Assessments Update

Lee, Chi-Szu, Section Chief, AEC/NRD

15:00 - 15:30 	Fukushima Regulatory Actions Update (NRC)

William Ruland, Division of Safety Systems, NRC

15:30 - 16:00 	Operating Performance & Safety Enhancement of Nuclear Power Plant in Taipower

Ming-Jer Liu , Deputy Director, TPC/NGD

16:00 - 16:30		Discussion and closing

18:00			Dinner

| November 7 | AIT-TECRO JSCCNC Meeting Working Groups |
| --- | --- |
| 08:00 08:45-15:00 Room 1 Room 2 Room 3 Room 4 15:00 – 16:00 16:00 | AIT and TECRO participants meet in hotel lobby for transportation to LLNL AIT-TECRO Working Groups Meetings Working Group I: Reactor Regulation and Regulatory Research Co-chairs: AIT: William Ruland, NRC TECRO: Shin Chang, AEC The Radiological Consequence Evaluation in Design Basis Analysis with FCVS (Filter Containment Vent Systems) Activation - William Ruland, NRC Spent Fuel Storage Regulations and Guidance in the U.S. - William Ruland, NRC Working Group II: Waste Management and Environmental Restoration Co-chairs: AIT: Rosa Elmetti, DOE/EM TECRO: Wuu-Kune Cheng, AEC/FCMA Depleted Uranium Hexafluoride and Enriched Uranium Hexafluoride Stabilization for Safe Storage in INER. - Kwang-Fu Tsai, INER Working Group III: Nuclear Science, Technology, Security, and Safeguards Co-chairs: AIT: NNSA (TBD) TECRO: Kin-Fu Lin, INER Nuclear Forensics Workshop Feedback and Path Forward- William Rhodes, NNSA Safeguards Programs in US and Taiwan- NNSA (TBD), Ming-Jer Liu , TPC Current status of proposed new Part 37 for security of Category 1 and Category 2 quantities of radioactive material in the U.S.- Danielle Emche, NRC INL-INER Workshop Feedbacks and Findings- Mike Goff, INL Working Group IV: Emergency Management Co-chairs: AIT: Vince McClelland, NNSA TECRO: Ming-Te Hsu, AEC Emergency Assistance CONOPS (Concept of Operations) Working Groups Discussion and Preparation and Signature of Summaries. Adjourn and dinner |

| November 8 08:30 09:00-15:00 | LLNL Technical Tour AIT and TECRO participants meet in hotel lobby for transportation to LLNL Briefing and Tours The Marshall Island Program Overview - NNSA NARAC / IXP (National Atmospheric Release Advisory Center/International Exchange Program) CAMS (Center of Accelerator Mass Spectrometry) EOC (Emergency Operations Center) |
| --- | --- |

| November 9 09:00-10:30 | TECRO Participants Review Meeting |
| --- | --- |

Contact:

Santiago Aguilar

Aguilarsr@state.gov or 202-647-8353

Index for TECRO-AIT Nuclear Cooperation Active Working Items

(Group I: Reactor Regulation and Regulatory Research)    附件三

| ITEM & PROJECT NAME | COORDINATORS | STATUS |
| --- | --- | --- |
| REF. NO | SUBJECT | TECRO | AIT |  |
| A. SEVERE ACCIDENT PROGRAM |
| IN-AE-NR -A8 | Cooperative Severe Accident Research Program (CSARP) | Yi-Bin Chen, AEC/Tai-Ming Chiu, INER | Danielle Emche, NRC | On-going |
| IN-AE-NR-A10 | Radiological consequence analysis using RADTRAD code and its application | Yi-Bin Chen, AEC/Tai-Ming Chiu, INER | Danielle Emche, NRC | On-going |
| B. THERMAL HYDRAULIC AND KINETICS |
| IN-TP-AE -NR-B1 | Participation in the USNRC Program of Thermal-Hydraulic Code Applications and Maintenance Research (CAMP) | Tai-Ming Chiu, INER/Tung-Li Weng, TPC | Danielle Emche, NRC | On-going |
| C. INSTRUMENTATION AND CONTROLS |
| AE-IN-TP-NR -C18 | Digital I & C Information Exchange | Yi-Bin Chen, AEC/ Tai-Ming Chiu, INER | Danielle Emche, NRC | On-going |
| AE-IN-TP-BN-C19 | PRA application for digital I&C control system | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| D. HEALTH PHYSICS |
| AE-IN-BN -D66 | Administrative Regulation of the Naturally Occurring Radioactive Material (NORM) | Ruoh-Tsann Lee, AEC | Danielle Emche, NRC | On-going |
| F. TECHNICAL SAFETY SUPPORT |
| AE-NR -F1 | Cooperation in Event of Nuclear Emergencies | Ming-Te Hsu, AEC | Danielle Emche, NRC | On-going |
| IN-BL-SN -F20 | PSA Applications | Tai-Ming Chiu, INER | Danielle Emche, NRC | Propose F36 to merge in |
| IN-TP-NR -F21 | Introduction of the LAPUR Code to Taiwan | Tai-Ming Chiu, INER | William Ruland, NRC | Propose to close |
| AE-FE-NR -F22 | Off-site Nuclear Emergency Preparedness | Ming-Te Hsu, AEC | Danielle Emche, NRC | On-going |
| AE-NR -F31 | Peer Review of National Report of Taiwan for the Convention of Nuclear Safety | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -F33 | Reactor Inspector Training | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -F34 | Physical Protection of Nuclear Materials, Facilities, and Power Plants | Ming-Te Hsu, AEC | Danielle Emche, NRC | On-going |
| H. REACTOR AGING PROGRAM |
| S. TECHNICAL AND REGULATORY INFORMATION EXCHANGE |
| AE-IN-TP -NR -S1 | Technical and Regulatory Information and Bilateral Meetings | Yi-Bin Chen, AEC/ Tai-Ming Chiu, INER | Danielle Emche, NRC | On-going |
| AE-NR -S42 | PWR Containment Sump and BWR ECCS Suction Strainer Performance Evaluation | Yi-Bin Chen, AEC | William Ruland, NRC | On-going |
| AE-NR -S43 | Information Exchange on Nuclear Reactor Power Uprate Safety Review | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -S48 | NRC-AEC AIT-TECRO Arrangement | David Yao, AEC | Danielle Emche, NRC | On-going |
| AE-NR -S49 | NRC and AEC Cooperation associated with IRRS | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -S50 | Post-Fukushima Safety Evaluation and Information Exchange | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -S51 | Aging Management of Operating Nuclear Power Plants | Yi-Bin Chen, AEC | William Ruland, NRC | On-going |
| Z. OPERATIONAL SAFETY |
| AE-NR -Z1 | Exchange of Data and Analysis on Incidents and Events | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| DD. RW/EM PROJECTS |
| JJ. NEW REACTORS |
| AE-NR -JJ1 | Pre-operational and Start-up Testing of Lungmen NPP | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |
| AE-NR -JJ4 | Operational Readiness Inspections of Lungmen ABWR plant | Yi-Bin Chen, AEC | Danielle Emche, NRC | On-going |

Total 23 items (as of 10/25/2012)

Propose to close 1 item

merge in 1 item (from group 3)

Index for TECRO-AIT Nuclear Cooperation Active Working Items

(Group II: Waste Management and Environmental Restoration)

| ITEM & PROJECT NAME | COORDINATORS | STATUS |
| --- | --- | --- |
| REF. NO | SUBJECT | TECRO | AIT |  |
| D. HEALTH PHYSICS |
| G. SPENT FUEL MANAGEMENT |
| FC-IN-NR -G23 | Licensing of Independent Spent Fuel Storage Installations | Syh-Tsong Chiou, FCMA | Danielle Emche, NRC | On-going |
| IN-LANL -G33 | PCC for Material Declaration of TRR Spent Fuel | Tai-Ming Chiu, INER | Alex Burkart, DOS | On-going |
| FC-NR -G34 | Peer Review of National Report of Taiwan for the Joint Convention on the Safety of Spent Fuel Management and on the Safety of Radioactive Waste Management | Syh-Tsong Chiou, FCMA | William Lahneman, DOE | Propose to close |
| AE-SNL -G35 | Information and Data Management System for SNF Interim Dry Storage Facility | Syh-Tsong Chiou, FCMA, Chin-Shan Lee, TPC | Robert Finch, SNL | Propose to close |
| J. DECONTAMINATION AND DECOMMISSIONING |
| AE-NR-J2 | Management of Decommissioning Waste | Syh-Tsong Chiou, FCMA | Danielle Emche, NRC | On-going |
| IN-ANL -J4 | Information transfer on decontamination and dismantling of research nuclear facilities | Tai-Ming Chiu, INER | L. Boing/T. A. Taiwo, ANL; Ana Han, DOE | On-going |
| U. POST-IRRADIATION EXAMINATION |
| AE-IN-AT -U2 | Irradiated Fuels and Materials Research Program from 2004 to 2014 | David Yao, AEC/ Tai-Ming Chiu, INER | Alex Burkart, DOS | On-going |
| IN-INL-U3 | Hot Laboratory Management and Post-Irradiation Examination Technology | Tai-Ming Chiu, INER | Steven N. Bakhtiar, INL | On-going |
| AE-DE -X1 | Transport and Disposal Practices of Irregular Waste Forms | Chin-Shan Lee, TPC | Ana Han, DOE | On-going |
| AE-NR -Z9 | Response and Management of Radioactive Material Events | Ruoh-Tsann Lee, AEC | Danielle Emche, NRC | On-going |
| DD. RW/EM PROJECTS |
| AE-TP-EM -DD12 | Public Participation | Chin-Shan Lee, TPC / Syh-Tsong Chiou, FCMA | Ana Han, DOE | On-going |
| TP-IN-RW -DD19 | Geological Repository Sciences | Chin-Shan Lee, TPC / Tai-Ming Chiu, INER | Jeffrey Williams, DOE | On-going |
| TP-EM -DD22 | Planning for Decommissioning | Chin-Shan Lee, TPC | Ana Han, DOE | On-going |
| IN-SNL -DD23 | Technology Transfer for Radioactive Waste Disposal | Tai-Ming Chiu, INER | Robert Finch, SNL | On-going |
| AE-DE -DD26 | Clearance Measurement Systems | Ing-Jane Chen, INER | Ana Han, DOE | Propose to close |
| AE-DE -DD27 | TRU Waste Management | Tai-Ming Chiu, INER | Robert Finch, SNL | On-going |
| AE-DE -DD28 | Contaminated Soil Remediation | Tai-Ming Chiu, INER | Ana Han, DOE | On-going |
| AE-DE -DD29 | Used Nuclear Fuel Extended Storage | Syh-Tsong Chiou, FCMA / Chin-Shan Lee, TPC / Tai-Ming Chiu, INER | Jeffrey Williams, DOE | On-going |

Total 18 items (as of 10/23/2012)

Propose to close 3 items

| New Item | UF6 Stabilization | Tai-Ming Chiu, INER |  |  |
| --- | --- | --- | --- | --- |

Index for TECRO-AIT Nuclear Cooperation Active Working Items

(Group III: Nuclear Science, Technology, and Safeguards)

| ITEM & PROJECT NAME | COORDINATORS | STATUS |
| --- | --- | --- |
| REF. NO | SUBJECT | TECRO | AIT |  |
| C. INSTRUMENTATION AND CONTROLS |
| D. HEALTH PHYSICS |
| AE-NR -D59 | Radiation Protection Training Program | Ruoh-Tsann Lee, AEC | Danielle Emche, NRC | On-going |
| AE-IN-DE -D64 | Radiation Protection Technical and Regulatory Information Exchange | Ruoh-Tsann Lee, AEC/ Lie-Hang Shen, INER |  | On-going |
| AE-DE -D65 | Epidemiology Study on Effects of Prolonged Low-dose Radiation Exposure on Residents living in 60Co-contaminated Rebar Buildings in Taiwan | Ruoh-Tsann Lee, AEC | Danielle Emche, NRC | On-going |
| E. ACCESS TO NNDC AT BNL |
| F. TECHNICAL SAFETY SUPPORT |
| IN-IN -F36 | Methodology development of damage evaluation to NPPs under severe weathers and other natural hazards | Tai-Ming Chiu/INER | Robert Finch, SNL | Propose to merge into F20 in group I |
| AE-DE -F39 | Nuclear Forensics Initiative | Ming-Te Hsu, AEC | William Rhodes, NNSA/DOE | On-going |
| I. RADIOISOTOPE PRODUCTION AND APPLICATIONS |
| IN-OR -I7 | Production and Evaluation of Isotopes and New Radiopharmaceuticals | Lie-Hang Shen, INER | Kirsten Cutler, DOS | Propose I13 to merge in |
| IN-DE -I13 | Nuclear Medicine Application Project | Lie-Hang Shen, INER | Kirsten Cutler, DOS | Propose to merge into I13 |
| IN-DE -I14 | Information Exchange of Certification, Quality Control and Licensing Procedure of Radiopharmaceutical | Lie-Hang Shen, INER | Kirsten Cutler, DOS | On-going |
| IN-DE -I19 | Cooperative Programs on the Development and Improvement of Nuclear- Imaging Instrumentation Associated Technology | Lie-Hang Shen, INER | Kirsten Cutler, DOS | On-going |
| T. ENERGY PLANNING |
| V. PLANT LIFE EXTENSION |
| W. CODE DEVELOPMENT |
| Y. ADVANCED REACTORS |
| TU-DE -Y1 | Generation IV Nuclear Reactors | Ji-Jung Kai, NTHU | William Lahneman, DOE/NE | Ongoing |
| TU-DE -Y3 | Explore opportunities related to DOE Engineering Innovation Hub for Modeling and Simulation Program. | Min Lee, NTHU | Steven Bakhtiar, INL | Ongoing |
| TU-DE -Y4 | Formation of New Partnership INL/NTHU/INER/SNL for Education and Training in Nuclear Science and Technology | Ji-Jung Kai, NTHU | Steven Bakhtiar, INL | On-going |
| AA. SABBATICAL/DISSERTATION RESEARCH |
| CC. BASIC RESEARCH |
| TU-AN -CC1 | Neutron Research at Research Reactors | Chih-Hao Lee, NTHU | Kirsten Cutler, DOS | On-going |
| EE. PHYSICAL PROTECTION OF NUCLEAR MATERIAL |
| AE-DE -EE2 | International Training Course on Physical Protection | Ming-Te Hsu, AEC | Kirsten Cutler, DOS | On-going |
| AE-DE -EE3 | Nuclear Export Control Training | David Yao, AEC | William Rhodes, NNSA/DOE | On-going |
| AE-DE -EE5 | Radioactive source security cooperation | Ruoh-Tsann Lee, AEC | Ross Matzkin-Bridger, NNSA/DOE | On-going |
| AE-DE -EE6 | Physical Protection Consultations | Ming-Te Hsu, AEC | Alex Burkart, DOS and Melissa Krupa, NNSA | On-going |
| AE-DE -EE7 | Training in Implementation of New PP Standards and Guidance | Ming-Te Hsu, AEC | Melissa Krupa, NNSA | On-going |
| FF. SAFEGUARDING OF NUCLEAR MATERIAL |
| AE-AIT -FF1 | State Systems of Accounting and Control (SSAC) | David Yao, AEC | Kirsten Cutler, DOS | On-going |
| AE-IN-AIT.LA-FF2 | Cooperation in Safeguards Technology | David Yao, AEC | Kirsten Cutler, DOS | On-going |
| AE-AIT -FF3 | Exchange of information on Implementation of IAEA Safeguards and the Additional Protocol | David Yao, AEC | Alex Burkart, DOS | On-going |
| AE-AIT -FF4 | Inventory of U.S. obligated nuclear material in Taiwan | David Yao, AEC | Kirsten Cutler, DOS | On-going |
| HH. MEDICAL THERAPY |
| TU-OR -HH1 | Design of Medical Therapy Facility for THOR | Yen Wan Liu, NTHU | William Lahneman NE/DOE Dan Ingersoll, ORNL | On-going |
| II. ENVIRONMENTAL MONITORING |

Total 23 items (as of 10/19/2011)

propose 1 item merge into other group

propose 2 items merge together in this group

Index for TECRO-AIT Nuclear Cooperation Active Working Items

(Group IV: Emergency Management)

| ITEM & PROJECT NAME | COORDINATORS | STATUS |
| --- | --- | --- |
| REF. NO | SUBJECT | TECRO | AIT |  |
| F. TECHNICAL SAFETY SUPPORT |
| AE-DE -F27 | Emergency Management | Ming-Te Hsu, AEC | Vince McClelland, NNSA/DOE | On-going |
| AE-DE -F28 | Atmospheric Plume Modeling | Ming-Te Hsu, AEC | Vince McClelland, NNSA/DOE | On-going |
| AE-DE -F37 | Emergency Assistance | Ming-Te Hsu, AEC | Vince McClelland, NNSA/DOE | On-going |
| AE-DE -F38 | Aerial and Other Detection Technique | Ruoh-Tsann Lee, AEC | Vince McClelland, NNSA/DOE | On-going |

Total 4 items (as of 10/12/2012)